# GENERAL

## REFERENCES

### Canadian Standards Association (CSA)

#### CAN/CSA-Z259.1, Body Belts and Saddles for Work Positioning and Travel Restraint.

#### CAN/CSA-Z259.10, Full Body Harnesses.

#### CAN/CSA-Z259.11, Energy Absorbers and Lanyards.

#### CAN/CSA-Z259.2.1, Fall Arresters, Vertical Lifelines and Rails.

#### FCC No. 301, Standard for Construction Operations.

#### CSA Z275.2, Occupational Safety Code for Diving Operations.

#### CSA Z275.4, Competency Standard for Divers Operations.

#### CSA Z797, Code of Practice for Access Scaffold.

### FCC No. 302, Standard for Welding and Cutting.

### Transportation of Dangerous Goods Act & Regulations.

### Newfoundland and Labrador Occupational Health and Safety Act, Amended

### Consolidated Newfoundland and Labrador Regulations 1149 WHMIS Regulations under the Occupational Health and Safety Act.

### Consolidated Newfoundland and Labrador Occupational Health and Safety Regulations under the Occupational Health and Safety Act.

### Canada Labour Code, Part 2.

### National Building Code of Canada.

### Department of Transportation and Infrastructure Occupational Health and Safety Manual.

### Department of Transportation and Infrastructure Contractor Safety Management Program.

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 35 43 - Environmental Procedures.

### Section 01 41 00 - Regulatory Requirements.

### Section 02 82 00.02 - Asbestos Abatement.

## GENERAL

### All work to be performed in accordance with the requirements of the Newfoundland and Labrador Occupational Health and Safety Act and Regulations as amended, the Department of Transportation and Infrastructure’s Contractor Safety Management Program and any specified Contract requirements.

### The Contractor shall comply with and enforce compliance by employees, subcontractors, suppliers and visitors with all safety requirements of the Contract Documents, applicable federal, provincial, territorial and local statutes, regulations, and ordinances, and with the Site Specific Health and Safety Plan (SSSP).

### The Contractor is responsible for all work coordination at the project site, safety oversight, and must maintain full ownership and control of safety within the project area at all times.

#### The Contractor shall ensure co-ordination of work schedules and tasks, and communication thereof for the purpose of ensuring health and safety on the worksite.

### Owner may perform project due diligence, site visits, safety monitoring activities, make suggestions or recommendations for improvement, and/or request changes in how work is performed. Notwithstanding, the Contractor has full responsibility, authority, and accountability for safely performing all work on the project site and/or under the project. Owner solely relies on the Contractor to know how to safely perform all Work including making appropriate decisions on Owner recommendations or requests.

### The Contractor shall ensure that in addition to those requirements set forth in the OHS Act and Regulations, all persons, including those employed by the Contractor or their subcontractors, working on projects for DTI shall wear the following mandatory Personal Protective Equipment at ALL times while working on the project.

#### CSA approved safety boots meeting the CSA Z195 Standard.

#### CSA approved hard hat meeting the CSA Z94.1 Standard.

#### CSA approved safety glasses meeting CSA Z94 Standard.

#### High visibility apparel as defined in the OHS Regulations.

#### Where noise exceeds standards set out in the OHS Regulations hearing protection shall be worn, and hearing conservation program implemented.

#### Other personal protective equipment, as may be required by the work tasks, hazard assessments or the Contractor, depending on duties being performed.

## SUBMITTALS

### At least 10 (ten) working days prior to commencing any site work: submit to Owner copies of:

#### A complete Site Specific Health and Safety Plan (SSSP).

#### If work entails blasting, submit the following:

##### Valid Blaster’s Certificate and Certificates of Qualification acceptable to the OHS Regulations 5/12 under section 419 identifying the Level of Qualification for the project requirements (Journey Persons Blaster Certificate will still be accepted). An acceptable letter of extension of blasters certificate from the Apprenticeship and Trades Certification Division of the Provincial Department of Immigration, Skills and Labour is required when certificate expires (5 years max.). Certificate numbers and names are required for all blasters proposed for the project.

##### Temporary Magazine License, when required issued, by Natural Resources Canada.

##### Explosives Vehicle Certificate, when required, issued by Transport Canada for transport of explosives regulated under the Transportation of Dangerous Good Act.

##### Blaster resume which clearly states and demonstrates:

###### Minimum five (5) years of experience in handling, storage and detonation of explosives.

###### Training at a blaster’s school which is acceptable to the provincial government.

#### If work entails diving, submit the following:

##### Diver(s) and dive supervisor (s).

###### Copy of valid Diving Certificate and Supervisor Certificate from the Diving Certification Board of Canada (or equivalent) for the required work on the project. (i.e. Restricted SCUBA Diver, Unrestricted SCUBA Diver, SCUBA Supervisor, Restricted Surface-Supplied Diver, Unrestricted Surface-Supplied Diver, etc. (See www.divercertifcation.com)

###### Resume which clearly demonstrates years of experience for the specific type (SCUBA, Surface Supplied Air, etc.) of diving to be performed at the site and projects completed to achieve minimum number of logged bottom time, hours and

###### First aid and CPR Training Certification.

##### Dive tender(s) resume which clearly states relevant training (including first aid and (CPR) and experience for the specific task (i.e. dive tender log book).

##### Current (less than one year) medical examination certificate (s) from a licensed medical doctor in the Province of Newfoundland and Labrador who is knowledgeable and competent in diving and hyperbaric medicine for all dives.

##### Certificates of Analysis for quality/purity of breathing air to be used by diver(s).

##### Documentation showing that diving life support equipment is in good working order and properly maintained.

##### Copies of documentation shall be submitted to show:

###### An up-to-date dive site listing of the contact Hyperbaric facility and phone numbers for each location.

###### Written arrangements with standby physician(s) specializing in diving/hyperbaric medicine for contingent emergency response and post dive follow-up for 48 hours after dive is completed.

###### Effective means of communication between the diving supervisor and physician are available.

###### The name, location and telephone number of the hospital and emergency department nearest the dive site.

#### If work entails confined space, submit the following:

##### Copies of current confined space entry training certificates acceptable to Workplace NL, as well as copies of confined space entry programs, confined space assessment, safe work practices and rescue plans.

### Review and acceptance of the SSSP and other submitted documents by the Owner shall only be viewed as acknowledgement that the contractor has submitted the required documentation under this specification section.

### Owner makes no representation and provides no warranty for the accuracy, completeness and legislative compliance of the Site Specific Health and Safety Plan and other submitted documents by this acceptance.

### Responsibility for errors and omissions in the SSSP and other submitted documents is not relieved by acceptance by Owner.

### Contractor to complete and submit to the Construction Manager, on a monthly basis, the Monthly Safety Performance Form, indicating monthly OHS performance indicators, OHS activities, training information and equipment maintenance.

#### Monthly Safety Performance Form: use form provided at the end of this section.

## OCCUPATIONAL HEALTH AND SAFETY (SITE SPECIFIC HEALTH AND SAFETY PLANS)

### Conduct operations in accordance with latest edition of the Newfoundland Occupational Health and Safety (OHS) Act and Regulations, with specific reference to codes and standards referenced therein, the Department of Transportation and Infrastructure Occupational Health and Safety Manual (https://www.gov.nl.ca/ti/files/publications-ohs-full.pdf), and the Department of Transportation and Infrastructure Contractor Safety Management Plan (https://www.gov.nl.ca/ti/files/Contractor-Safety-Management-program-November-20212.pdf).

### Prepare a detailed Site Specific Health and Safety Plan (SSSP) that shall identify, evaluate and control job specific hazards through a detailed hazard assessment of the tendered project outlining phases of the project and hazards/controls associated with specific work, equipment, locations and tasks associated with the work conducted during each phase of the project and the necessary control measures to be implemented for managing hazards.

### The plan shall also ensure adequate policies, procedures and safe work practices are in place to manage hazards identified in the hazard assessment that cannot be addressed through engineering controls.

### It is the responsibility of the Contractor to submit only one SSSP that incorporates all relevant portions of their subcontractors’ safety documentation.

### For projects exceeding thirty (30) days, provide a copy of the SSSP upon request to Occupational Health and Safety Division, Digital Government and Service NL, Province of Newfoundland and Labrador and the Owner.

### The written SSSP shall incorporate the following:

#### Hazard assessment results.

#### Engineering and administrative demonstrative controls (work-practices and procedures) to be implemented for managing identified and potential hazards, and comply with applicable federal and provincial legislation and more stringent requirements that have been specified in these specifications.

#### An organizational structure, in the form of an organizational chart with contact information of the key positions, which shall establish the specific chain of command and specify the overall responsibilities of contractor’s employees at the work site.

##### The chart shall also include relevant information for all subcontractors.

#### Identification of the designated qualified work coordinator(s) (i.e. Supervisor, Contractor Safety Representative) as per Section 21 of the OHS Regulations.

#### A comprehensive work plan which shall:

##### Outline the phases of the Project and the required tasks, equipment, positions, resources and objectives for each phase, including all subcontracted work.

##### Conduct a detailed hazard assessment of each project phase, including all subcontracted work, taking into consideration the objectives, tasks, equipment, positions, resources, training, etc.

##### Identify the controls required for all identified hazards and project phases that may include engineering controls, policies, procedures, equipment, safe work practices, training and communication with staff, etc.

#### Establish personnel requirements for implementing the plan and controls, and establish site-specific training and notification requirements and schedules.

#### A personal protection equipment (PPE) Program which shall detail PPE:

##### Selection criteria based on site hazards as determined by the hazard assessment.

##### Use, maintenance, inspection and storage requirements and procedures.

##### Decontamination and disposal procedures.

##### Inspection procedures prior to, during and after use, and other appropriate medical considerations.

##### Limitations during temperature extremes, heat stress and other appropriate medical consideration.

#### An emergency response procedure, refer to clause 1.6 Supervision and Emergency Response Procedure of this section for requirements.

#### A hazard communication program for informing workers, visitors and individuals outside of the work area as required. This will include but not be limited to a visitor safety and orientation policy and program that will include education on hazards, required PPE and accompaniment while on site.

##### This program shall also take into consideration the safety of the general public that may come in contact with the work site and appropriate measures for notification and safety

#### A hearing conservation program in accordance with Part VI, Section 68 of the OHS Regulations.

#### A vehicle inspection matrix (tabular or spreadsheet format) showing required inspection type and date of most recent inspection for all powered mobile equipment (including light vehicles) that will be used in fulfilling the terms of the contract, including rented and the subcontractor’s equipment. Upon request, the Contractor shall provide to the Owner, individual inspection forms that at a minimum state that the equipment is in a safe operating condition and is signed by a qualified journeyperson mechanic..

#### A complete listing of employee names, their driver’s license classification, expiry date, endorsements and the type of equipment that they are qualified to operate for the complete scope of work for this project. The Driver’s License Number should not be provided as this is confidential information. Provision of the License Number may breach PIPEDA - the Personal Information Protection and Electronic Documents Act. (Federal Act) or ATIPPA - Access to Information and Protection of Privacy Act - Part IV. (Provincial Act of Newfoundland and Labrador). This shall also include documentation where required of certification in power line hazards.

#### An acceptable parking policy for all powered mobile equipment to be used on this project.  The policy shall, at a minimum, be based on a hazard assessment that considers factors such as equipment type, potential for roll over, load capacity of the parking area, pedestrian and vehicular traffic, and potential for equipment tampering, equipment energy, and equipment contact with power lines.

#### A diving program which shall contain standard operating procedures to be followed in the diving operation.

#### A traffic control plan. Refer to clause 1.24 Traffic Control.

#### A fall protection plan, if necessary. Refer to clause 1.22 Working at Heights.

#### A dust suppression management program, if necessary.

#### An assessment of all possible risks of violence for the project and corresponding control measures. Considerations should include location and circumstances of the site, previous history of incidents and or possible triggers.

#### .

#### General safety rules.

### Periodically review and modify as required each component of the SSSP when a new hazard is identified during completion of work and when an error or omission is identified in any part of the SSSP.

### Review the completeness of the hazard assessment immediately prior to commencing work, when a new hazard is identified during completion of work and when an error or omission is identified.

#### Be solely responsible for investigating, evaluating and managing any report of actual or potential hazards.

#### Clearly define accident incident investigation procedures.

#### Clearly define policy and processes for early and safe return to work.

#### Retain copies of all completed hazard assessments at the project site and make available to the Owner immediately upon request.

### Implement all requirements of the SSSP.

#### Ensure that every person entering the project site is informed of requirements under the SSSP.

#### Take all necessary measures to immediately implement any engineering controls, administrative contacts, personal protective equipment required or termination of work procedures to ensure compliance with the SSSP.

### Conduct site orientations to advise workers of the hazards on their worksites. Site orientations to be performed by the party most familiar with the hazards of the worksite.

### Hold regular toolbox talks, with additional talks if there are changes to the job.

### Conduct weekly site inspections of the worksite.

## SUPERVISION AND EMERGENCY RESCUE PROCEDURE

### Develop an organizational structure which establishes a specific chain of command and overall responsibilities of all employees at the work site.

### Carry out work under the direct supervision of competent persons responsible for safety by ensuring the work complies with the appropriate section of OHS Act and Regulations

### Assign a sufficient number of supervisory personnel to the work site.

#### Any person assigned to supervisory duties shall not conduct significant work in relation to the contract that inhibits them from the ability to properly supervise the work site.

### Ensure the site supervisor has complete understanding, working knowledge and familiarity with the SSSP, applicable codes and standards as well as the OHS Act and Regulations.

### Ensure the site supervisor fully implements, enforces, and monitors the SSSP.

### Prior to the start of work, ensure that the site supervisor(s) have the training, knowledge, and understanding in:

#### Project tasks and construction activities.

#### Hazard recognition evaluation and control.

#### Development and implementation of safe work practices and procedures.

#### Accident incident investigations and reporting.

#### Workplace violence and harassment prevention.

#### Equipment maintenance and inspections required for preventive safety.

#### Care and maintenance of PPE to be used on site.

#### Standard First Aid training certified by WorkplaceNL.

#### WHMIS 2015.

### The Site Supervisor shall:

#### Be responsible for project safety by ensuring the work complies with all requirements of the SSSP and with the appropriate section(s) of OHS Act and Regulations, latest edition.

#### Prior to mobilization on site, hold a pre-start Health and Safety meeting with the Contractors, subcontractors, and Owner to review of the SSSP including all its contents.

#### Be responsible for the delivery and documentation of the site safety orientations and ensure that personnel who have not been oriented are not permitted to enter the site. This applies to all workers (Contractor, Subcontractor, and Department), and visitors.

#### Advise of the health and safety hazards for the work site, provide written or verbal instructions of any precautions to be taken to protect everyone at the work site and ensure that the applicable personal protective equipment is used and worn on site at all times.

#### Review hazard assessment for completeness immediately prior to commencing work, when a new hazard is identified during completion of work, or when an error or omission is identified.

#### Address all safety concerns brought to their attention in a timely manner depending on the severity of the hazard.

#### Be responsible for the maintenance of a daily log of inspections, meetings, infractions and mitigating measures. The log is to be filed daily and copies provided to the Owner as requested.

#### Be responsible to log, investigate, track and follow-up on mitigations for all near misses, incidents and/or accidents.

#### Promote employees’ right to work in a respectful, harassment-free, and psychologically healthy and safe work environment. Assist the Owner to investigate incidents of workplace violence or harassment carried out against a DTI employee by contractor or sub-contractor employees.

#### Ensure the correct traffic control signage plan is utilized on site and staff have been notified of the requirements. Ensure that road signage is inspected for accuracy and condition by a competent and trained person upon set-up, each morning prior to work, and at any point in which the signage requires change during the workday or life of the contract. A Traffic Control and Signage Log must be submitted with the Contractor’s Monthly OHS Performance Report.

#### If required for the project, coordinate with and support the efforts of the on-site safety representative.

### Assign a dedicated on-site safety representative to assist the Site Supervisor during the completion of high-risk activities. This person shall have training, knowledge, and understanding regarding the activity(s) being completed. High-risk activities may include, but are not limited to:

#### Heavy lift operations which includes items greater than 1000 kg or which may need an engineered lift plan due to other identified risk factors.

#### Lift operations that occur closer than 10 m of energized power lines or close proximity to moving traffic, public and residential areas, or other sensitive locations.

#### When greater than three (3) employers are working in close proximity at the same time. Close proximity execution means any time the operations of each employer are close enough to directly influence or add risk to another employer.

#### Working within or near highly populated residential areas when there is an appreciable ongoing risk to the public that needs continual safety oversight.

#### When a complex traffic control plan is needed in high volume areas.

#### Work involving confined space entry.

#### Working with or near toxic and hazardous substances.

#### Any other high-risk activity identified through hazard/risk assessment by the Contractor or by the Owner.

#### In such instances, the Contractor may request and the Department may agree that such dedicated safety representation is not needed if the Contractor demonstrates there are adequate safety controls in place to mitigate the risk.

### Provide a suitable means of communications and check–in for workers required to work alone.

### Develop an emergency rescue plan for the job site and ensure that supervisors and workers are trained in the emergency rescue plan.

### The emergency response plan shall address, as a minimum:

#### Pre-emergency planning (included the assessment of controls to reduce the likelihood of such an emergency if possible).

#### Personnel roles, lines of authority and communication (include a communication list of all emergency services in the immediate and surrounding areas).

#### Emergency recognition and prevention (identification of each potential type of emergency and evaluation of requirements for response).

#### Required communication equipment including landlines, mobile phones, radios, satellite phones, and/or other equipment needed to ensure appropriate emergency communications in the area of the Project.

#### Safe distances and places of refuge.

#### Site security and control.

#### Evacuation routes and procedures.

#### Decontamination procedures which are not covered by the site specific safety and health plan.

#### Emergency medical treatment and first aid.

#### Emergency alarm, notification and response procedures including procedures for reporting incidents to local, provincial and federal government departments.

#### PPE and emergency equipment.

#### Procedures for handling emergency incidents.

#### Procedures and protocol for working alone and/or remote working.

#### Site specific emergency response training requirements and schedules.

#### For diving operation, include procedures for:

##### Managing deteriorating environmental conditions.

##### Managing unexpected weather or sea-state condition.

##### Evacuation of diver(s) under pressures greater than atmospheric pressure.

##### In-water emergency transfers.

##### Managing failing of equipment below the surface that impairs the ability of a diver to complete a dive.

##### Managing failure of any major component of diving plant or equipment.

##### Emergency signalling between divers involved in the diving program and between the diver(s) and the attendants using umbilical, tethers or other suitable methods.

##### Mobilizing stand-by divers.

##### Mobilizing crafts, stand-by boats and any other devices to be used for rescue.

##### Contacting evacuation, rescue, treatment facilities and medical services that will be used in the diving program.

##### Operation of emergency power and lighting facilities.

### The emergency response procedures shall be rehearsed regularly as part of the overall training program and the results documented. The frequency at which all aspects of the emergency response plan will be rehearsed must be stated.

### Provide adequate first aid facilities for the jobsite and ensure that a minimum number of workers are trained in first aid in accordance with the Occupational Health and Safety First Aid Regulations.

## CONTRACTORS SAFETY REPRESENTATIVE

### The contractor shall employ a Contractor’s Safety Representative (CSR) who shall have as a minimum successfully completed the following training, and must have current credentials for those that have expiration dates:

Editorial Note Replace sentence 1.7.1 with the following if the Design Manager specifies a requirement for a site dedicated full time Contractor’s Safety Representative (CSR). Delete this editorial note if a full time site dedicated Contractor’s Safety Representative (CSR) is not specifically required. The contractor shall employ a site dedicated full time Contractor’s Safety Representative (CSR) who must be on site during execution of the Work. Periodic absences during the workday of short duration for project related activities are acceptable provided they have been pre-arranged with DTI’s construction manager. In unusual situations absences of one full day or longer will require a replacement. The replacement will be required to have prior familiarization with the site and the SSSP. The CSR and any temporary replacement shall have as a minimum successfully completed the following training, and must have current credentials for those that have expiration dates:

#### Training in hazardous materials management and response/protocols.

#### Training in the use, maintenance of fall protection systems certified by Workplace NL at a minimum.

#### Training in the inspection of scaffolding in accordance with CSA Z797.

#### Training in confined space entry protocols, techniques and rescue plans, certified by Workplace NL at a minimum.

#### Supervisory training.

#### Training in records and statistics.

#### Training is hazard identification, inspections, analysis and control.

#### Training in WHMIS 2015.

#### Training in health and safety program content.

#### Training in investigations and reporting.

#### Training in occupational health/hygiene.

#### Training in employee training and communication.

#### Training in Emergency Preparedness and First Aid.

#### A working knowledge of, and experience satisfactory to the Department, using the occupational safety and health legislation and regulations specific to Newfoundland and Labrador.

#### Experience, satisfactory to the Department, with the safe work practices required for execution of the work and operation of equipment specific to the project.

#### Experience, satisfactory to the Department, in developing and monitoring site safety and housekeeping policies.

#### Experience, satisfactory to the Department, in developing and monitoring a preventative maintenance and inspection program for Construction Site Equipment.

### The CSR shall:

#### Be responsible for developing, implementing, daily enforcement, monitoring and updating of the SSSP.

#### Be responsible for the delivery of the site safety orientation and ensure that the personnel who have not been orientated are not permitted to enter the site. This applies to workers, inspectors and visitors.

#### Report directly to and be under direction of the Site Superintendent or Contractor’s Project Manager.

#### Prior to mobilization on-site, hold an orientation meeting with the contractors, subcontractors and Owner to review project occupational health and safety. Include but not limit meeting to a review of:

##### The SSSP.

##### Construction Safety Measures.

##### Supervision and Emergency Rescue Procedures.

##### Hazard Assessments

#### Maintain a daily log of inspections, meetings, infractions and mitigating measures. Log is to be filed daily and copies to be provided to the Site Superintendent and Owner.

#### The CSR shall have:

##### Formal training in OHS Management (degree, diploma, or certificate) combined with at least two (2) years of relevant experience, or

##### A designation of National Construction Safety Officer (NCSO), Construction Safety Officer (CSO), Canadian Registered Safety Professional (CRSP), Canadian Registered Safety Technician (CRST), or Certified Health and Safety Consultant (CHSC), or other similar designation.

## HEALTH AND SAFETY COMMITTEE

### Establish an Occupational Health and Safety Committee where ten or more workers are employed on the job site for greater than 30 days as per the OHS Act and Regulations.

### Committee members shall receive training from a WorkplaceNL recognized training provider.

### Provide a copy of all committee minutes with the Contractor’s Monthly OHS Performance Report.

## CONTRACTOR ROLES AND RESPONSIBILITIES

### Ensure that their organization is staffed appropriately to ensure completion of project tasks and all necessary safety related duties and responsibilities.

### Ensure co-ordination of work schedules and tasks, and communication thereof for the purpose of ensuring health and safety on the worksite.

### Be responsible for health and safety of persons on site, safety of property on site and for protection of persons adjacent to site and environment to extent that they may be affected by conduct of Work.

### Develop a SSSP that thoroughly assesses the health and safety hazards of each project phase, including all subcontracted work.

### Implement all requirements of the SSSP. The Contractor shall take all necessary measures to immediately implement any engineering controls, administrative controls, personal protective equipment required or termination of work procedures to ensure compliance with the SSSP and the OHS Act and Regulations. All measures should be immediately communicated to staff.

### Comply with and enforce compliance by employees, subcontractors, suppliers and visitors with safety requirements of Contract Documents, applicable federal, provincial, territorial and local statutes, regulations, and ordinances, and with SSSP.

### Where safety risks exist, the contractor must stop the work until such time as the risk can be mitigated to a safe level.

### Take appropriate steps to ensure that the hazards are mitigated to a safe level, workers are notified of the hazards and how to protect themselves. As well, workers must be provided with any new safe work practices or information regarding mitigation of the risk.

### Periodically review and modify the SSSP as required including but not limited to when a new hazard is identified during completion of work or when an error or omission is identified in any part of the SSSP.

### Support/permit periodic inspections of the Contractor’s work by the Owner to maintain compliance with the SSSP. Inspections may include visual inspections of the site and documentation, as well as testing and sampling as required.

### Be responsible for any and all costs associated with delays as a result of the Contractor’s failure to comply with the requirements outlined in this Section or the OHS Act and Regulations.

### Ensure that all workers receive necessary training as per the training matrix contained in the SSSP prior to the start of work. Maintain training records in a tabular format or spreadsheet for all employees on the project site and complete periodic reviews to ensure that necessary re-certifications are completed prior to expiration dates.

### Ensure all equipment, vehicles, tools, or other devices necessary throughout the Project are suitable for the task and are inspected and maintained in accordance with the manufacturers’ specifications and/or CSA standards adopted by the OHS Regulations.

### Be responsible to ensure that site inspections have been completed at no less than one (1) week intervals. These site inspections shall include risk assessments where the nature of the ongoing work or tasks associated with the work increase in risk or significantly change due to phases in the project or project progression.

### Ensure that toolbox meetings are held with staff no less than once per week and shall include review of safety related information that is pertinent to the safety of employees.

### Ensure that all toolbox meetings, site inspections, risk assessments, OHS Committee meetings and any OHS Directives or reports are documented and submitted with the Contractor’s Monthly OHS Performance Report.

### Review for completeness the hazard assessment results immediately prior to commencing work, when a new hazard is identified during completion of work or when an error or omission is identified.

### Be solely responsible for investigating, evaluating and managing any report of actual or potential hazards.

### Retain copies of all completed hazard assessments at the project site and provide a copy to the Owner. Copies of any hazard assessments not included in the original SSSP must be submitted immediately to the Owner and noted on the Contractor’s Monthly OHS Performance Report.

### Promote the employees’ right to work in a respectful, harassment-free, and psychologically healthy and safe work environment. Assist the Owner to investigate incidents of workplace violence or harassment carried out against a DTI employee by contractor or sub-contractor employees.

## UNFORSEEN HAZARDS

### Should any unforeseen or peculiar safety-related factor, hazard, or condition become evident during performance of Work, follow procedures in place for Employee's Right to Refuse Work in accordance with Acts and Regulations of Province having jurisdiction. Advise Owner verbally and in writing.

## REPORTING AND INVESTIGATION

### The Contractor shall adhere to a documented incident, hazard, safety reporting, and investigation process. The system shall:

#### Ensure all hazards, near misses, incidents, accidents, injuries, equipment damage are recorded and properly investigated.

#### Rank actual and potential severity of observations and report all high potential near misses, accidents, and incidents immediately to the Owner and to the OHS Division of Digital Government and Service NL.

#### Advise the Owner and the OHS Division of Digital Government and Service NL verbally and in writing immediately of any incident that results in serious injury to a person or results in the death of a person; or had the reasonable potential to cause serious injury.

#### Provide a copy of all notifications made to the OHS Division of Digital Government and Service NL to Transportation and Infrastructure.

#### Where life safety risks or other high potential risks exists, the Contractor must stop work until such time as the risk can be mitigated to a safe level.

#### Make appropriate steps to ensure that the hazards are mitigated to a safe level, workers are notified of the hazards and how to protect themselves. Additionally, workers must be provided with any new safe work practices or information regarding mitigation of the risk.

## INSTRUCTION AND TRAINING

### Workers shall not participate in or supervise any activity on the work site until they have been trained to a level required by this job function and responsibility.

### Contractors shall develop an OHS training program that reflects OHS Legislative requirements and specific safety hazards based on Project work

### Training shall as a minimum thoroughly cover the following:

#### Federal and Provincial Health and Safety Legislation requirements including roles and responsibilities of workers and person(s) responsible for implementing, monitoring and enforcing health and safety requirements.

#### Safety and health hazards associated with working on a contaminated site including recognition of symptoms and signs which might indicate over exposure to hazards.

#### Limitations, use, maintenance and disinfection-decontamination of personal protective equipment associated with completing work.

#### Limitations, use, maintenance and care of engineering controls and equipment.

#### Limitations and use of emergency notifications and response equipment including emergency response protocol.

#### Work practices and procedures to minimize the risk of an accident and hazardous occurrence from exposure to a hazard.

#### Workers must receive training from a WorkplaceNL recognized training provider as outlined in the OHS legislation (i.e. fall protection, confined space entry, power line hazards, traffic control persons training).

#### Training in the use, care and maintenance of PPE to be used on site.

#### Training in the Contractor’s emergency response plan for the Project. Workers engaged in fall arrest or confined space rescue operations will require specific training for the tasks involved.

#### All workers at site must receive training in Workplace Violence and Harassment Prevention.

#### Training in WHMIS 2015.

#### Safety and health hazards associated with working in extreme weather conditions (i.e. heat/cold hazards).

### Provide and maintain training of workers, as required, by Federal and Provincial legislation.

### Provide copies of all training records to Owner for review, before a worker is to enter the work site. Site training records must be in tabular or spreadsheet format, stating employee name, occupation, required training, date that training was obtained and expiry date. This must be signed and dated by a member of the Contractor’s management team.

### Authorized visitors shall not access the work site until they have been:

#### Notified of the names of persons responsible for implementing, monitoring and enforcing the SSSP.

#### Briefed on safety and health hazards present on the site.

#### Instructed in the proper use and limitations of personal protective equipment.

#### Briefed as the emergency response protocol including notification and evacuation process.

#### Informed of practices and procedures to minimize risks from hazards and applicable to activities performed by visitors.

#### Accompanied while on site, and provided with the appropriate PPE.

### All workers will be instructed and trained on the hazards associated with work they will perform and how to protect themselves. This will include a review of all safe work practices, the reporting and documentation of hazards, reporting accidents and injuries as well as, formal training in areas of high risk (i.e. fall protection, power line hazards, traffic control persons training).

### The work site shall have the appropriate number of persons trained in emergency and Standard First Aid according to the First Aid Regulations.

## CONSTRUCTION SAFETY MEASURES

### Observe construction safety measures of National Building Code, latest edition, Federal and Provincial Government, OHS Act and Regulations, Workplace NL and Municipal Authority provided that in any case of conflict or discrepancy more stringent requirements shall apply.

### Administer the project in a manner that will ensure, at all times, full compliance with Federal and Provincial Acts, regulations and applicable safety codes and the SSSP.

### Provide Owner with copies of all orders, directions and any other documentation, issued by the Occupational Health and Safety Division, Digital Government and Service NL, immediately after receipt.

### Forward copies of all orders, directions or any other documentation immediately after receipt.

## POSTING OF DOCUMENTS

### Ensure applicable items, articles, notices and orders are posted in conspicuous location on site in accordance with Acts and Regulations of Province and authority having jurisdiction, and in consultation with Owner.

## HEALTH AND SAFETY MONITORING

### Periodic inspections of the contractor’s work may be carried out by the Owner to maintain compliance with the Health and Safety Program. Inspections will include visual inspections as well as testing and sampling as required.

### The contractor shall be responsible for any and all costs associated with delays as a result of contractor’s failure to comply with the requirements outlined in this section.

## NOTIFICATION

### For projects exceeding thirty (30) days or more, the contractor shall, prior to the commencement of work, notify in writing the Occupational Health and Safety Division, Digital Government and Service NL with the following information and provide a copy to the Owner:

#### Name and location of construction site.

#### Company name and mailing address of contractor doing the work.

#### The number of workers to be employed.

#### A copy of the SSSP, if requested.

## CORRECTION OF NON-COMPLIANCE

### Immediately address health and safety non-compliance issues identified by authority having jurisdiction or by Owner.

### Provide Owner with written report of action taken to correct non-compliance of health and safety issues identified within ten (10) working days.

### Owner may stop work if non-compliance of health and safety regulations is not corrected.

## WHMIS 2015

### Ensure that all controlled products are in accordance with the Workplace Hazardous Materials Information System (WHMIS 2015) Regulations and Chemical Substances of the OHS Act and Regulations regarding use, handling, labelling, storage, and disposal of hazardous materials.

### Deliver copies of relevant Safety Data Sheets (SDS) to job site and the Owner. The SDS must be acceptable to Labour Canada and Health and Welfare Canada for all controlled products that will be used in the performance of this work. All SDS should be located in accessible locations for all workers and visitors throughout the site, bound and organized in binders.

### Train workers required to use or work in close proximity to controlled products as per OHS Act and Regulations. This must be documented as part of the on-site orientation and a copy provided to the Owner.

### Label controlled products at jobsite as per OHS and Regulations and WHMIS.

### Provide appropriate emergency facilities as specified in the SDS where workers might be exposed to contact with chemicals, e.g. eye-wash facilities, emergency shower.

#### Workers to be trained in use of such emergency equipment.

### Contractor shall provide appropriate personal protective equipment as specified in the SDS where workers are required to use controlled products.

#### Properly fit workers for personal protective equipment

#### Train workers in care, use and maintenance of personal protective equipment.

### No controlled products are to be brought on-site without prior approved SDS.

### The SDS are to remain on site at all times and are accessible to everyone on site.

## OVERLOADING

### The Contractor’s Full Time CSR and/or Site Superintendent shall ensure no part of work or associated equipment is subjected to loading that will endanger its safety or will cause permanent deformation.

### Ensure equipment operations follow manufacturer’s operating manual.

## FALSEWORK

### Design and construct falsework in accordance with CSA S269.1.

## SCAFFOLDING

### Design, erect, inspect, operate, modify, and dismantle scaffolding in accordance with CSA Z797, Part XI: sections 147-249 of the OH&S Act and Regulations, and the scaffold manufacturer’s written instructions.

### Provide trained and certified Competent Scaffold Erectors for all scaffold erection, modification and dismantling. Training certification must be valid at time of erection, modification and dismantling of scaffold.

### Conduct and document daily inspections of scaffolding by trained and certified Competent Scaffold Inspectors or Erectors. Training certification must be valid at the time of inspection.

#### Records and copies of these inspections shall be kept on site and provided upon request to the Department of Transportation and Infrastructure officials, Owner, etc.

### Scaffolding inspection reports may be required to be provided with the Contractor’s Monthly OHS Performance Reports, at the discretion of the Owner.

### Provide a scaffold tagging system as described in CSA Z797.

### Ensure that all industry best practices for safe scaffold usage, including fall protection, proper loading, safe access, electrical hazards, exit door management and other concerns are strictly adhered to.

## WORKING AT HEIGHTS

### Develop a site specific fall protection plan, including a rescue plan, and provide it to the Owner as a part of the SSSP when fall protection systems are required during the course of the Project

### Ensure that fall restraint or fall arrest devices are used by all workers working at elevations greater than 3.05 meters above grade or floor level in accordance with CSA Z259, where alternate fall protection systems are not provided in accordance with Occupational Health and Safety Act and Regulations.

### All workers performing work at height and who will be required to utilize a fall arrest system must be trained in a fall protection program certified by the Workplace NL. Training must be current and valid at the time of use.

### Prior to working at height workers shall be instructed in a Contractor Safe Work Practice for working at height and associated Rescue Plan for working at heights, developed specific to the work to be performed, locations and risks.

### Maintain a list of all persons trained in WorkplaceNL certified fall protection training on site. To be combined with other training records as required in a tabular or spreadsheet format listed throughout this Section.

### Ensure regular inspections of all fall protection and fall arrest equipment are completed and that records are maintained and kept on site. Daily inspections of fall restraint and horizontal fall protection/arrest systems shall be conducted.

### Ensure that manufacturer’s specifications for engineered fall protection/arrest/restraint systems are kept on site at all times.

### Develop Working from Height Safe Work Practices specific to the Work, location and risks, and ensure the workers receive specific instruction regarding the work tasks and associated rescue plans.

### Ensure that rescue equipment for fall rescues is kept in close proximity to workers working at height.

### Where necessary the Contractor shall ensure that adequate protection from falling debris is addressed in site specific safety plans, this may include debris nets, barriers, etc.

## PERSONAL PROTECTIVE EQUIPMENT

### Ensure workers on the jobsite use personal protective equipment appropriate to the hazards identified in the SSSP and those workers are trained in the proper care, use, and maintenance of such equipment.

### PPE selections shall be based on an evaluation of the performance characteristics of the PPE relative to the requirements and limitations of the site, task-specific conditions, duration and hazards and potential hazards identified on site. PPE must also be fitted for the worker.

### Provide workers and visitors to the site with proper respiratory protection equipment.

#### No work shall be performed in an area where an airborne contaminant exceeds recommendations of the ACGIH, do not meet the appropriate standards for the specific contaminants or are not in accordance with the OHS regulations.

#### Respiratory protection shall be provided in accordance with the requirements of the Occupational Health and Safety Division, Digital Government and Service NL and these specifications.

#### Establish, implement and maintain a respirator inspection and maintenance program in accordance with the CSA standard identified in the OHS Regulations.

#### Copies of all respirator owners’ maintenance manuals shall be kept at all times at the contractor’s site office.

### Provide and maintain a supply of dermal protection equipment to allow visitors and all workers proper dermal protection.

#### Dermal protection shall be sufficient to act as a protective barrier between the skin and an airborne contaminant or hazardous material.  Dermal protection shall also be provided for all physical hazards.

#### Dermal protection equipment shall not be used after exceeding 75% of the break through time. The break through time shall be based on the contaminant which requires the least amount of time to break through the protective equipment

#### Copies of all dermal protection user specifications, owners and maintenance manuals shall be kept at all times at the contractor’s site office.

#### Establish, implement and maintain air inspection program to ensure proper dermal protection in accordance with CSA, NIOSH, U.S. EPA and manufacturer’s requirements.

### Provide all workers and up to five (5) visitors to the site with proper hearing protection.  Workers and visitors shall not be exposed to noise levels greater than 85 dB (A) over an eight hour shift without proper hearing protection, in accordance with the Hearing Conservation Program.

### Provide all workers and up to five (5) visitors to the site with CSA approved eye protection sufficient to act as a protective barrier between the eye and airborne contaminants, hazardous materials and physical hazard.

### Provide workers and up to five (5) visitors to the site with CSA approved hard hats meeting the CSA Z94.1.

### Provide high visibility apparel as defined in Occupational Health and Safety Regulations.

### Provide CSA approved safety boots meeting CSA Z195.

### Provide other personal protective equipment, as may be required by the owner, depending on duties being performed.

## TRAFFIC CONTROL

### Provide traffic control measures when working on, or adjacent to, roadways in accordance with the Traffic Control Manual, latest edition, Department of Transportation and Infrastructure.

#### This will include but is not limited to appropriate signage, traffic control persons and control vehicles.

### Ensure daily completion of the Department of Transportation and Infrastructure, Traffic Control and Signage Log. The log will be submitted monthly with the Contractor Monthly Safety Performance Form and may be inspected randomly by DTI staff for completion and accuracy.

### Complete hazard assessments for traffic control plans to identify hazards unique to the work (i.e., volume of heavy equipment, size of lanes and barriers to protect workers from traffic, additional decreases in posted speeds, etc.).

### The Contractor shall ensure that traffic control persons have completed Traffic Control Person Level I training as certified by WorkplaceNL.

### The Contractor shall ensure that a competent individual is responsible for monitoring, maintaining and adjusting traffic control plans throughout the life of the project. This individual shall:

#### Have completed Traffic Control Person Level II training as certified by WorkplaceNL.

#### Be provided with authority and resources to ensure continuous monitoring of the worksite and revision of the traffic control plan when necessary.

#### Be responsible to complete the Traffic Control and Signage Log to accompany the Contractor’s Monthly Safety Performance Form requirements.

#### Ensure compliance with Part XVI of the OHS Regulations 5/12.

## EXCAVATION SAFETY

### Protect excavations more than 1.25 metres deep against cave-ins or wall collapse by side wall sloping to the appropriate angle of repose, an engineered shoring/sheathing system or an approved trench box.

#### Provide a ladder which can extend from the bottom of the excavation to at least 0.91 metres above the top of the excavation.

### Ensure that all excavations less than 1.25 metres deep are effectively protected when hazardous ground movement may be expected.

### Design trench boxes, certified by a registered Professional Engineer, and fabricated by a reputable manufacturer. Provide the manufacturer’s Depth Certificate Statement permanently affixed. Use trench boxes in strict accordance with manufacturer’s instructions and depth certification data.

### For excavations deeper than six (6) metres, provide a certificate from a registered Professional Engineer stating that the protection methods proposed have been properly designed in accordance with accepted engineering practice. The engineer’s certificate shall verify that the trench boxes, if used, are properly designed and constructed to suit the depth and soil conditions.

### Ensure that the superintendent and every crew chief, foreperson and lead hand engaged in trenching operations or working in trenches have in his/her possession a copy of Occupational Health and Safety Regulations: Part XVII: Construction, Excavation and Demolition and Part XVIII: Excavation, Underground Work and Rock Crushing.

### Ensure that the Department of Digital Government and Service NL, OHS Division signs off on excavations greater than five (5) meters.

## BLASTING OPERATIONS

### Ensure blasting operations are carried out under the direct visual supervision of a certified Blaster either registered with the Apprenticeship and Trades Certification Division of the Department of Immigration, Skills and Labour or has been issued a certificate from completion of a program approved by Department of Digital Government and Service NL. Ensure that the certificate level is appropriate for the blasting activities which will occur. Comply with the requirements of:

#### Explosives Act.

#### Explosives Regulations.

#### Newfoundland Regulation 5/12, Occupational Health and Safety Regulations.

#### Role of certified blaster set out in section 419 of the Occupational Health and Safety Regulations 5/12.

### Store explosives in accordance with the “Explosives Act (Canada)” and transport, handle and use in the manner prescribed by the manufacturer of the substance and subject to specific regulations. An inventory of explosives shall be kept.

### Ensure that workers required to transport explosives have a valid Transportation of Dangerous Goods Training Certification in accordance with the “Act to Promote Public Safety in the Transportation of Dangerous Goods, and the “Explosives Act (Canada)”. Vehicle used to transport explosives on site shall be placarded and explosives shall be transported in containers that are lined with non-sparking material (reference section 428 of the Occupational Health and Safety Regulations 5/12 comply with section 42. Detonators shall not be placed in a magazine or daybox with other types of explosives or in a compartment of a vehicle with another type of explosive.

### Use of explosives on site shall comply with the Occupational Health and Safety Regulations 5/12 General Blasting requirements set out in Part XIX of the Regulations.

### Loaded holes shall be clearly identified with barricades put in place to prevent access to the holes. Drilling shall not be done closer to a loaded bore hole than a distance half the total depth of the hole being drilled and in no case shall drilling be conducted at a distance closer than 6.0 m from a loaded borehole. Drill cuttings shall not be used as stemming material.

### Advise the public by suitable public notices, advertisements, house to house contacts etc. for blasting operations in close proximity to areas occupied by the public.  Advise of the warning device to be sounded and the procedure to be used before detonation of individual blasts. Roads and approaches to the danger area to be guarded or barricaded to prevent anyone from entering. Loaded holes which have not been fired by the end of the day shall not be left unattended.

### Prior to detonation of a blast, give sufficient warning in every direction and ensure that all persons have reached a place of safety before the blast is fired.

### File an Emergency Response Assistance Plan with the Explosives Branch, Natural Resources Canada.

### Blaster shall:

#### Be solely responsible for implementation of the Explosives Management Program.

#### Have a valid blaster’s safety certificate from the Apprenticeship and Trades Certification Division of the Department of Immigration, Skills and Labour, and have a valid temporary Magazine License, when required issued by Natural Resources Canada, for storage and explosives.

#### Possess a thorough working knowledge of the Federal Explosives Act and Provincial Regulations.

#### Possess a specialized training in handling storage and detonation of explosives.

#### Keep a field journal concerning the blasting activities.

## CONFINED SPACE WORK

### Comply with the Newfoundland and Labrador Occupational Health and Safety Regulations.

### Ensure a hazard assessment has been conducted related to the confined space and the work to be performed within the space.

### Provide approved air monitoring equipment where workers are working in confined spaces and ensure any test equipment to be used is calibrated, in good working order and used by trained persons.

### Ensure all required PPE is provided to the workers and workers are trained in its use, care and selection.

### Develop a confined space entry (CSE) program specific to the nature of work performed and in accordance with OHS Act and Regulations and ensure supervisors and workers are trained in the confined space entry program. This shall include training on the CSE permit system, rescue plan, testing, communication equipment and all equipment and safe work procedures conducted in and around the confined space.

#### Ensure that personal protective equipment and emergency rescue equipment appropriate to the nature of the work being performed is provided and used.

### Provide and maintain training of workers through a provider certified by the Workplace NL.

### Provide Owner with a copy of an “Entry Permit” for each entry into the confined space to ensure compliance Provincial Legislation.

## HAZARDOUS materials

### Should material resembling hazardous materials (e.g. asbestos/mould) not previously identified/documented be encountered during the execution of work, stop work and notify Owner. Do not proceed until written instructions have been received from Owner.

### Unless otherwise noted the services of a recognized Environmental Consultant to provide all air monitoring and testing services required by regulatory requirements for hazardous materials abatement and repair.

## HEAVY EQUIPMENT

### Ensure mobile equipment used on jobsite is of the type specified in OHS Act and Regulations fitted with a Roll Over Protective (ROP) Structure and Falling Object Protective (FOP) Structure.

### Ensure that operators of mobile equipment have adequate instruction and are competent in the operation of mobile equipment.

### Provide certificate of training in Power Line Hazards for operators of heavy equipment.

### Obtain written clearance from the power utility where equipment is used in close proximity to (within 5.5 metres) overhead or underground power lines.

### Equip cranes with:

#### A mechanism which will effectively prevent the hook assembly from running into the top boom pulley.

#### A legible load chart.

#### A maintenance log book.

## TREE AND BRUSH CLEARING

### Ensure workers using chain saws or brush saws wear the following safety equipment:

#### CSA safety hat fitted with face screen or shield.

#### Hearing protection, e.g. ear muffs.

#### CSA approved chain saw pants.

#### CSA approved chain saw boots.

#### CSA approved eye protection.

#### Cut resistant gloves.

### Equip chain saws with a safety chain break.

### A safe work practice (SWP) must be developed, implemented and all workers trained in the SWP prior to undertaking such tasks and utilizing tree and brush clearing equipment.

## DIVING OPERATIONS

### Ensure diving operations conform to CSA Z275.2 - Occupational Safety Code for Diving Operations and CSA Z275.4 - Competency Standard for Diving Operations.

### Sampling:

#### Prior to commencing diving activities, sample water and analyze sample(s) for:

##### Fecal Coliforms (Escherichia coli).

##### Total Coliforms.

##### Any health hazard identified during the site specific hazard assessment.

##### Any parameter as directed by the Department of Digital Government and Service NL, Government of Newfoundland and Labrador.

#### Water will be designated a contaminant if the chemical concentration of a contaminant exceeds:

##### 200 fecal Coliforms (Escherichia coli) per 1000 milliliter of water.

##### 100 times the guidelines concentration established in the most recent Guidelines of Canadian Drinking Water Quality.

##### Any other criteria established by the Department of Digital Government and Service NL, Government of Newfoundland and Labrador.

#### Sample analysis is to be completed by a laboratory that is accredited by the Canadian Associates of Environmental and Analytical Laboratories (CAEAL) or other national equivalent.

#### Dive personnel must meet the minimum competency requirements of CSA 275.4.

##### The Dive supervisor(s) shall as a minimum:

###### Possess a Valid Category 1 Diving Certificate, or equivalent, for a minimum of three (3) years for the type of diving to be performed.

###### Have completed one hundred and fifty (150) hours of logged diving time for the type of diving to be performed.

###### Have completed fifty (50) hours of dive supervision for the type of diving to be performed.

##### Diver(s) shall as a minimum:

###### Possess a valid Category 1 Diving Certificate or equivalent, for the type of diving to be performed.

###### Have completed fifty (50) hours of logged dive time for the type of diving to be performed.

#### A diving operation shall be interrupted or discontinued or not commenced when:

##### Continuation of the diving operation would or is likely to compromise the safety of any person involved in the diving operation.

##### The water currents at the underwater work site are likely to compromise the safety of any person involved in the diving operation.

##### Combustible material is stored too close for safety to any diving plant and equipment used in the diving operation.

#### A diving operation shall:

##### Not be conducted in the vicinity for any other activity that might pose a danger to any person involved in the diving operation.

##### Not use any craft that has insufficient power or stability for the safe continuity of the diving operation.

##### Provide measures for making work area boundary and stopping unauthorized entry into the work area.

##### Provide adequate illumination of the dive site and the underwater work site of the diving operation.

#### Provide, at the worksite while completing diving operations, a diving operations log book that is permanently bound and has numbered pages.

##### Produce on request, any log books, records or other documentation associated with the diving operation, for inspection by Owner.

##### As a minimum, for each diving operation enter into the diving operation logbook:

###### date and time the diving operation commenced and terminated including any time the diving operation was interrupted

###### name of supervisor; names of all other persons involved

###### the procedures followed

###### the decompression table and the schedule in that the decompression table was used

###### the maximum depth, bottom time, dive time and total dive time for each dive

###### the type of diving plant and equipment and the type of breathing mixture used

###### the type of discomfort, injury or illness including decompression sickness, suffered by any person involved

###### any environmental conditions that affected or might have affected the diving operation

###### any other factors relevant to the safety to health of any person involved

#### Diving in free swim mode is not permitted at the work site.

#### Provide separate first aid supplies for dive operation. All dive team personnel shall be trained in first aid and cardiopulmonary resuscitation (CPR).

#### Provide medical oxygen for emergency response at work site. The dive supervisor shall be trained in administering medical oxygen.

## WORKPLACE VIOLENCE AND HARASSMENT

### Develop a Workplace Violence and Harassment Prevention Plan for the project that complies with the latest edition of the OHS Regulations.

## WORKING OVER OR NEAR WATER

### Where the risk of entering water is identified and other means of fall protection or rescue are not adequate to prevent the worker from entering the water, develop water rescue plans and ensure that workers on site are trained.

### Keep and maintain a list of all persons trained in water rescue on site. This list shall be combined with other training records as required in a tabular or spreadsheet format listed throughout this Section.

### Require that workers wear personal flotation devices where workers are at risk of entering the water.

### Ensure that life-saving equipment is available near entry site for water rescue. This may include life boats, throw lines, life preservers, etc.

## ACCESS, EGRESS AND WALKWAYS

### Ensure that all accesses, egresses and walkways are continuously monitored for hazards which may include slips, trips, slippery conditions and other hazards.

### Develop provisions for snow clearing of walkways, accesses and egresses.

### Ensure that all access, egress hatches, holes or other potential hazards of this nature are clearly identified to workers and adequately covered.

## RIGGING AND SLINGING

### Ensure that workers required to perform work related to rigging and slinging are trained and deemed competent in such operations and practices.

### Maintain and inspect all rigging and slinging equipment in accordance with manufacturers’ specifications, CSA Standards and OHS Regulations.

### Ensure that the working load limit of rigging and slinging equipment on site is marked and visible on the product.

### At a minimum, ensure that rigging and slinging operations meet the requirements of the OHS Act and Regulations.

### Ensure that rigging and slinging equipment identified in daily inspections or otherwise identified as damaged, worn or unacceptable to manufacturers’ specifications, appropriate standards or OHS Regulations is immediately taken out of service and destroyed.

## WORK STOPPAGE

### Give precedence to safety and health of public and site personnel and protection of environment over cost and schedule considerations of Work.

## OWNER’S STATEMENT

### The Owner shall not be responsible for injury or damage occasioned by a failure of the Contractor to adhere to the provisions of this Section.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE

END OF SECTION

| Contractor Information |
| --- |
| Contractor/Company Name |  |
| Report Prepared By |  |
| Report for Period | Beginning: | Ending: |
| Project and Location |  |
| Contact | Name | Contact Number |
| Project Manager |  |  |
| Contractor CSR |  |  |
| Site Superintendent |  |  |
| Monthly OHS Performance Indicators |
| Lagging Indicators |  |  | Leading Indicators |
| Indicate the total within reporting period above | Monthly Total |  | Indicate the total within reporting period above | Monthly Total | Records available |
| Lost Time Injuries |  |  |  | Tool Box Talks (safety specific)* |  |  |
| Working Days Lost |  |  |  | OHS Committee/Rep Meetings* |  |  |
| Return to Work Plans |  |  |  | Bi-Weekly Project Meeting |  |  |
| First Aid Incidents |  |  |  | Site Safety Orientations |  |  |
| Medical Aid Incidents |  |  |  | Weekly Site Inspections* |  |  |
| Total Hours Worked (site) |  |  |  | Hazard Reports Submitted |  |  |
| Accident /Incident reports* |  |  |  | Hazard Assessments Conducted* |  |  |
| Accident Incident Investigations Conducted* |  |  |  | Traffic Control Signage Log Completed* |  |  |
|  |  | NLCSA Certificate of Recognition (COR)* |  |  |
| OHS Division Activities |
| OHS Division Inspections |  |  | OHS Division Directives Issued* |  |  |
| Sub-Contractor Information |
| Name sub-contractors working on site | Description of work conducted by sub-contractors | Days on site | COR Certified (Y/N) |
| Training Information |
| Training conducted with staff | Brief description of training conducted with safety or work practice focus | Total staff trained | Records available (Y/N) |
| Equipment Maintenance |
| Annual equipment inspections conducted (Y/N) | All equipment passed inspection (Y/N) | Records Available (Y/N) |  | Non-Routine maintenance required? Identify equipment | List maintenance conducted |
| Report completed on: |  | Signature: |  |

Please attach information pertaining to items highlighted with an asterisk (*)

Definitions

- Accident – An undesired event resulting in death, ill health, damage or other loss.

- Accident/Incident Investigation – An investigation by the employer into the root cause of an accident or incident to identify hazards and prevent workplace accidents/incidents from recurring.

- Accident/Incident Report – all accidents and incidents must be reported, whether through an internal reporting structure or through the Workplace NL employers Form 7. All accidents of a serious nature must also be reported to the PHS Division within 24 hours (serious accidents as outlined in Section 54(3) of the OHS Act).

- First Aid Incident – An occupational injury/illness that requires first aid treatment only and does not result in loss of time from work or restricted work.

- Incident – An unplanned, undesired event that had the potential to cause injury or other damage.

- Lost-Time Injury – An injury/illness resulting in Lost Days beyond the date of injury as a direct result of the occupational injury/illness incident on the project.

- Medical Aid incident – A classification of occupational injury/illness for medical treatment beyond first aid injury where there has been no lost days, i.e., visit to a health care provider or hospital specific to the injury.

- Total Hours Worked – Total number of hours of employment (i.e., the actual worked hours) of all employees for each contractor and sub-contractor companies for the reporting period specific to the project.

- Working Days Lost – The number of calendar days that the employee is unable to work beyond the day of the injury specific to the project in which the injury occurred. Calculate total days for all employees working on the project.

| Contractor Information |
| --- |
| Contractor/Company Name |  |
| Report Prepared By |  |
| Project and Location |  |
| Contact | Name | Contact Number |
| Project Manager |  |  |
| Contractor CSR |  |  |
| Site Superintendent |  |  |
| Log No. ____ |
| Date/Time: |  | Number/Name of Signage Layout from TCM: |  |
| Condition/Placement of Signage: |  |
| Current/Expected Weather Conditions: |  | Signage/Equipment Adequate for work and Conditions (Y/N): |  |
| Deficiencies Completed Prior to Start of Work (Signage Repairs, Replacements, Upgrading, etc.) |  |
| Report Completed By: |  | Date/Time: |  |
| TI Representative: |  | Date/Time: |  |
| Log No. ____ |
| Date/Time: |  | Number/Name of Signage Layout from TCM: |  |
| Condition/Placement of Signage: |  |
| Current/Expected Weather Conditions: |  | Signage/Equipment Adequate for work and Conditions (Y/N): |  |
| Deficiencies Completed Prior to Start of Work (Signage Repairs, Replacements, Upgrading, etc.) |  |
| Report Completed By: |  | Date/Time: |  |
| TI Representative: |  | Date/Time: |  |
| Log No. ____ |
| Date/Time: |  | Number/Name of Signage Layout from TCM: |  |
| Condition/Placement of Signage: |  |
| Current/Expected Weather Conditions: |  | Signage/Equipment Adequate for work and Conditions (Y/N): |  |
| Deficiencies Completed Prior to Start of Work (Signage Repairs, Replacements, Upgrading, etc.) |  |
| Report Completed By: |  | Date/Time: |  |
| TI Representative: |  | Date/Time: |  |
| Log No. ____ |
| Date/Time: |  | Number/Name of Signage Layout from TCM: |  |
| Condition/Placement of Signage: |  |
| Current/Expected Weather Conditions: |  | Signage/Equipment Adequate for work and Conditions (Y/N): |  |
| Deficiencies Completed Prior to Start of Work (Signage Repairs, Replacements, Upgrading, etc.) |  |
| Report Completed By: |  | Date/Time: |  |
| TI Representative: |  | Date/Time: |  |

TCM: Traffic Control Manual https://www.gov.nl.ca/ti/files/publications-traffic-control-2018.pdf

# Text boxes

Spec Note: Edit section to suit project requirements. Delete references to sentences not required.