# GENERAL

## FIRES

### Fires and burning of rubbish on site not permitted.

## DISPOSAL OF WASTES

### Do not bury rubbish and waste materials on site.

### Do not dispose of waste or volatile materials, such as mineral spirits, oil or paint thinner into waterways, storm or sanitary sewers.

## DRAINAGE

### Provide temporary drainage and pumping as necessary to keep excavations and site free from water.

### Do not pump water containing suspended materials into waterways, sewer or drainage systems.

### Control disposal or runoff of water containing suspended materials or other harmful substances in accordance with local authority requirements.

## SITE CLEARING AND PLANT PROTECTION

### Protect trees and plants on site and adjacent properties where indicated.

### Wrap in burlap, trees and shrubs adjacent to construction work, storage areas and trucking lanes, and encase with protective wood framework from grade level to height of 2.0 m.

### Protect roots of designated trees to dripline during excavation and site grading to prevent disturbance or damage. Avoid unnecessary traffic, dumping and storage of materials over root zones.

### Minimize stripping of topsoil and vegetation.

### Restrict tree removal to areas indicated or designated by Owner.

## WORK ADJACENT TO WATERWAYS

### Do not operate construction equipment in waterways.

### Do not use waterway beds for borrow material.

### Do not dump excavated fill, waste material or debris in waterways.

### Design and construct temporary crossings to minimize erosion to waterways.

### Do not skid logs or construction materials across waterways.

### Avoid indicated spawning beds when constructing temporary crossings of waterways.

### Do not blast under water or within 100 m of indicated spawning beds.

## POLLUTION CONTROL

### Maintain temporary erosion and pollution control features installed under this contract.

### Control emissions from equipment and plant to local authorities emission requirements.

### Prevent sandblasting and other extraneous materials from contaminating air beyond application area, by providing temporary enclosures.

### Cover or wet down dry materials and rubbish to prevent blowing dust and debris. Provide dust control for temporary roads.

## NOTIFICATION

### Owner will notify Contractor in writing of observed non-compliance with Federal, Provincial or Municipal environmental laws or regulations, permits, and other elements of environmental protection. Contractor: after receipt of such notice, inform Owner of proposed corrective action and take such action as approved by Owner.

### Owner may issue stop order of work until satisfactory corrective action has been taken.

### No time extensions will be granted or equitable adjustments allowed to Contractor for such suspensions.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION