# GeneraL

## SUMMARY

### This Section includes general requirements for constructing field mock ups. Refer to technical sections for more product-specific mock up requirements.

### Requirements for mock ups are supplemental to requirements for samples and field samples as specified in individual technical sections.

## RELATED SECTIONS

### Section 01 33 00 – Submittal Procedures.

### Section 01 45 00 – Quality Control.

## DEFINITIONS

### Mock ups: Full-size, physical example assemblies, constructed on-site, to illustrate finishes and materials. Mock ups are used to:

#### Verify selections made under Sample submittals;

#### Demonstrate aesthetic effects and, where indicated, qualities of materials and execution;

#### Review construction, coordination, testing or operation;

#### Show interference between dissimilar materials; and

#### Demonstrate compliance with specified installation tolerances.

### Mock ups are not Samples.

## Quality Assurance

### Before installing portions of the Work requiring mock ups, build mock ups for each form of construction and finish required to comply with the following requirements, using materials indicated for the completed work:

#### Build mock ups in location and of size and profile indicated, or if not indicated, as directed by Owner.

#### Provide Owner minimum five (5) working days advance notice of dates and times when mock ups will be constructed and able to be inspected.

#### Failure to prepare mock-ups in ample time is not considered sufficient reason for an extension of Contract Time and no claim for extension by reason of such default will be allowed.

#### Allow five (5) working days for Owner’s initial review and re-review of each mock up.

#### Do not complete production of materials for final Project site until Owner’s review of mock up has been obtained.

#### Where mock up is rejected, replace, rebuild and/or modify mock up as directed by the Owner.

#### Demonstrate the proposed range of aesthetic effects and workmanship.

#### Employ supervisory personal to oversee mock up construction. Employ same workers that will be employed during the construction of the Project.

#### Unless otherwise indicated, accepted mock ups establish the standard by which the Work sill be judged.

#### Maintain mock ups during construction in an undisturbed condition as a standard of judging the completed Work.

#### Mock ups may remain part of the finished product, unless otherwise indicated.

# Products (Not used)

# Execution (Not Used)

END OF SECTION

Note: Edit Mock Up Schedule to suit project.

| Mock Up Schedule |
| --- |
| Section | Contractor Verification – Mock Up Complete | Date | Contractor Verification – Mock Up Review Requested | Date |
| 04 05 00 - Common Work Results for Masonry |  |  |  |  |
| 04 20 00.08 - Masonry for Minor Works |  |  |  |  |
| 04 21 13 - Brick Unit Masonry |  |  |  |  |
| 04 22 00 - Concrete Unit Masonry |  |  |  |  |
| 04 23 00 - Glass Unit Masonry |  |  |  |  |
| 06 40 00 - Architectural Woodwork |  |  |  |  |
| 06 40 23.13 - Plastic Laminate Finishing for Interior Architectural Woodwork |  |  |  |  |
| 07 13 26 - Self Adhered Sheet Waterproofing |  |  |  |  |
| 07 21 29 - Sprayed Insulation – Polyurethane Foam |  |  |  |  |
| 07 26 00 - Vapour Retarders |  |  |  |  |
| 07 27 00.01 - Air Barriers – Descriptive or Proprietary |  |  |  |  |
| 07 42 23 - Composite Wall Panels |  |  |  |  |
| 07 52 00 - Modified Bituminous Membrane Roofing |  |  |  |  |
| 07 54 23 - Thermoplastic Polyolefin (TPO) Roofing |  |  |  |  |
| 07 81 00 - Applied Fireproofing |  |  |  |  |
| 07 84 00 - Firestopping |  |  |  |  |
| 07 92 00 - Joint Sealants |  |  |  |  |
| 08 44 13 - Glazed Aluminum Curtain Walls |  |  |  |  |
| 08 51 13 - Aluminum Windows |  |  |  |  |
| 08 62 00 - Plastic Skylights |  |  |  |  |
| 08 80 00 - Glazing |  |  |  |  |
| 09 01 90.62 - Exterior Re-Painting |  |  |  |  |
| 09 01 90.63 - Interior Re-Painting |  |  |  |  |
| 09 21 16 - Gypsum Board Assemblies |  |  |  |  |
| 09 30 13 - Ceramic Tiling |  |  |  |  |
| 09 30 15 - Quarry and Paver Tiling |  |  |  |  |
| 09 51 13 - Acoustic Panel Ceilings |  |  |  |  |
| 09 65 16 - Resilient Sheet Flooring |  |  |  |  |
| 09 65 20 - Safety Sheet Flooring |  |  |  |  |
| 09 72 16 - Vinyl Coated Fabric Wall Covering |  |  |  |  |
| 09 80 00 - Acoustic Treatment |  |  |  |  |
| 09 91 13 - Exterior Painting |  |  |  |  |
| 09 91 23 - Interior Painting |  |  |  |  |
| 10 21 13.13 - Metal Toilet Partitions |  |  |  |  |
| 12 20 00 - Curtains and Drapes |  |  |  |  |
| 12 59 13 - Panel Hung Component System Furniture |  |  |  |  |