# GENERAL

## SECTIONS INCLUDE

### Inspection and testing, administrative and enforcement requirements.

### Tests and mix designs.

### Mock-ups.

### Mill tests.

### Equipment and system adjust and balance.

## RELATED SECTIONS

### Section 01 21 00 – Allowances.

### Section 01 33 00 – Submittal Procedures.

### Section 01 43 39 – Mock Up Requirements.

### Section 01 78 00 – Closeout Submittals.

## INSPECTION

### Allow Owner access to Work. If part of Work is in preparation at locations other than Place of Work, allow access to such Work whenever it is in progress.

### Give 48 hours notice requesting inspection if Work is designated for special tests, inspections or approvals by Owner’s instructions.

### If Contractor covers or permits to be covered Work that has been designated for special tests, inspections or approvals before such is made, uncover such Work, have inspections or tests satisfactorily completed and make good such Work.

### Owner may order any part of Work to be examined if Work is suspected to be not in accordance with Contract Documents.  If, upon examination such work is found not in accordance with Contract Documents, correct such Work and pay cost of examination and correction. If such Work is found in accordance with Contract Documents, Owner shall pay cost of examination and replacement.

## INDEPENDENT INSPECTION AGENCIES

### Independent Inspection/Testing Agencies will be engaged by Owner for purpose of inspecting and/or testing portions of Work.

### Allocated costs: to Section 01 21 00 – Allowances and Section 01 29 83 – Payment Procedures: Testing Laboratory Services.

### Provide equipment required for executing inspection and testing by appointed agencies.

### Employment of inspection/testing agencies does not relax responsibility to perform Work in accordance with Contract Documents.

### If defects are revealed during inspection and/or testing, appointed agency will request additional inspection and/or testing to ascertain full degree of defect. Correct defect and irregularities as advised by Owner at no cost to Owner. Pay costs for retesting and reinspection.

## ACCESS TO WORK

### Allow inspection/testing agencies access to Work, off site manufacturing and fabrication plants.

### Co-operate to provide reasonable facilities for such access.

## PROCEDURES

### Notify appropriate agency and Owner in advance of requirement for tests, in order that attendance arrangements can be made.

### Submit samples and/or materials required for testing, as specifically requested in specifications. Submit with reasonable promptness and in an orderly sequence so as not to cause delay in Work.

### Provide labour and facilities to obtain and handle samples and materials on site. Provide sufficient space to store and cure test samples.

## REJECTED WORK

### Remove defective Work, whether result of poor workmanship, use of defective products or damage and whether incorporated in Work or not, which has been rejected by Owner as failing to conform to Contract Documents. Replace or re-execute in accordance with Contract Documents.

### Make good other Contractor's work damaged by such removals or replacements promptly.

### If in opinion of Owner it is not expedient to correct defective Work or Work not performed in accordance with Contract Documents, Owner may deduct from Contract Price difference in value between Work performed and that called for by Contract Documents, amount of which shall be determined by Owner.

## REPORTS

### Submit 3 copies of inspection and test reports to Owner, plus electronic copies in PDF format.

### Provide copy to Subcontractor of work being inspected or tested, manufacturer or fabricator of material being inspected or tested.

### Include copy of all inspection and test reports in Commissioning Manuals.

## MOCK-UPS

### Refer to Section 01 43 39 for Mock Up Requirements.

## EQUIPMENT AND SYSTEMS

### Submit adjustment and balancing reports for mechanical, electrical and building equipment systems.

### Mechanical – coordinate with mechanical division.

### Electrical – Coordinate with electrical division.

## FIRE SEPARATIONS

### Provide fire separation labelling/stenciling as per Sections 09 91 23 – Interior Painting and 09 01 90.63 – Interior Re-Painting.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION