# GENERAL

## RELATED SECTIONS

### Section 01 52 00 - Construction Facilities.

### Section 01 56 00 - Temporary Barriers and Enclosures.

## INSTALLATION AND REMOVAL

### Provide temporary utilities controls in order to execute work expeditiously.

### Remove from site all such work after use.

## DEWATERING

### Provide temporary drainage and pumping facilities to keep excavations and site free from standing water.

## WATER SUPPLY (Edit to suit project)

### Arrange for connection with appropriate utility company and pay all costs for installation, maintenance and removal.

### Owner will provide continuous supply of potable water for construction use. Contractor is responsible for connection at the source.

## TEMPORARY HEATING AND VENTILATION (Edit to suit project)

### Pay for costs of temporary heat and ventilation used during construction, including costs of installation, fuel operation, maintenance and removal of equipment. Use of direct, fired heaters discharging waste products into work areas will not be permitted unless prior approval is given by Owner.

### Owner will provide and pay for temporary power during constructing for temporary lighting and operating of power tools, to the extent available on site. Contractor to connect to existing power supply in accordance with governing regulations and the Canadian Electrical Code, latest edition.

#### Temporary power for equipment requiring in excess of above is responsibility of Contractor.

### Construction heaters used inside building must be vented to outside or be non-flameless type. Solid fuel salamanders are not permitted.

### Provide temporary heat and ventilation in enclosed areas as required to:

#### Facilitate progress of Work.

#### Protect Work and products against dampness and cold.

#### Prevent moisture condensation on surfaces.

#### Provide ambient temperatures and humidity levels for storage, installation and curing of materials.

#### Provide adequate ventilation to meet health regulations for safe working environment.

### Maintain temperatures of minimum 10˚C and relative humidity less than 60% in areas where construction is in progress.

#### Maintain minimum temperature of 10˚C or higher where specified as soon as finished work is commenced. Maintain until acceptance of structure by Owner.

#### Maintain ambient temperature and humidity levels as required for comfort of office personnel.

### Ventilating:

#### Prevent accumulations of dust, fumes, mists, vapours or gases in areas occupied during construction.

#### Provide local exhaust ventilation to prevent harmful accumulation of hazardous substances into atmosphere of occupied areas.

#### Dispose of exhaust materials in manner that will not result in harmful exposure to persons.

#### Ventilate storage spaces containing hazardous or volatile materials.

#### Ventilate temporary sanitary facilities.

#### Continue operation of ventilation and exhaust system for time after cessation of work process to assure removal of harmful contaminants.

### Maintain strict supervision of operation of temporary heating and ventilating equipment to:

#### Conform with applicable codes and standards.

#### Enforce safe practices.

#### Prevent abuse of services.

#### Prevent damage to finishes.

#### Vent direct-fired combustion units to outside.

### Be responsible for damage to Work due to failure in providing adequate heat, humidity and protection during construction.

### Use of new or existing systems for temporary heating, ventilating or air conditioning will not be permitted.

## TEMPORARY POWER AND LIGHT

### Provide and pay for temporary power during constructing for temporary lighting, heating, site construction trailers and operating of power tools in accordance with governing regulations and the Canadian Electrical Code, latest edition.

### Arrange for connection with Utility company. Pay all costs for installation, maintenance and removal of cables, distribution and branch panel boards, poles, lighting, heating and general power receptacles as required.

### Temporary power for electric cranes and other equipment requiring in excess of above is responsibility of Contractor.

### Provide and maintain temporary lighting throughout project. Ensure level of illumination on all floors and stairs is not less than 162 lx. Temporary lighting to consist of wiring, pig tail sockets and 75 watt shatterproof incandescent lamps to provide a minimum light level of 162 lux.

### Electrical power and lighting systems installed under this contract may be used for construction requirements only with prior approval of Owner provided that guarantees are not affected.  Make good damage to electrical system caused by use under this contract.  Replace lamps which have been used for more than 3 months.

### General contractor responsible for payment of all electrical energy charges associated with temporary power up to date of substantial completion.

## FIRE PROTECTION

### Provide and maintain temporary fire protection equipment during performance of Work required by insurance companies having jurisdiction and governing codes, regulations and bylaws.

### Burning rubbish and construction waste materials is not permitted on site.

## SANITARY FACILITIES

### Provide sanitary facilities for work force in accordance with governing regulations and ordinances.

### Post notices and take precautions as required by local health authorities. Keep area and premises in sanitary condition.

### When permanent water and drain connections are completed, provide temporary water closets and urinals complete with temporary enclosures, inside building. Permanent facilities may be used on approval of Owner.

## TEMPORARY COMMUNICATION FACILITIES

### Provide and pay for temporary telephone, fax, data hook up, lines and equipment necessary for own use and use of Owner.

## SITE SIGN AND NOTICES

### Contractor is responsible for the construction of job sign frame and the installation of the plywood job sign. Timber frame shall be constructed as specified and detailed on “Job Sign Support Frame Detail”. Plywood job sign shall be as per layout on “Job Sign Detail”. These drawings documents are published at http://www.gov.nl.ca/ti/works/signs under the Project Signs Link and is to be picked up by contractor at the Sign Shop, Department of Transportation and Infrastructure, White Hills, St. John’s, Newfoundland and Labrador. Plywood job sign and timber frame shall remain the property of the Owner and shall be disposed of at the discretion of the Owner.

### Locate job sign as directed by Owner so as to ensure good visibility by passing traffic.

### Construct timber job sign frame using two (2) 140 x 140mm timber posts set vertically in concrete to a ground depth of 1000mm or below the frost line, whichever is greater. Install three (3) 38 x 89mm horizontal timber braces, all as shown on “Job Sign Support Frame Detail” published at http://www.gov.nl.ca/ti/works/signs under the Project Signs Link. Attach plywood sign to timber frame using galvanized nails. Paint timber frame with two (2) coats of white paint if using untreated timber. Backfill compact and level ground around job sign frame to the satisfaction of the Owner.

## REMOVAL OF TEMPORARY FACILITIES

### Remove temporary facilities from site when directed by Owner.

### When project is closed down at end of construction season keep temporary facilities operational until close down or removal is approved by Owner.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION