# GENERAL

## SECTION INCLUDES

### Construction aids.

### Office and sheds.

### Parking.

### Project identification.

## RELATED SECTIONS

### Section 01 35 29.06 – Health and Safety Requirements

### Section 01 51 00 - Temporary Utilities.

### Section 01 56 00 - Temporary Barriers and Enclosures.

## INSTALLATION AND REMOVAL

### Provide construction facilities in order to execute work expeditiously.

### Remove from site all such work after use.

## SCAFFOLDING

### Provide and maintain scaffolding in rigid, secure and safe manner.

### Erect scaffolding independent of walls. Remove promptly when no longer required. Refer to Section 01 35 29.06 – Health and Safety Requirements.

## HOISTING

### Provide, operate and maintain hoists cranes required for moving of workers, materials and equipment. Make financial arrangements with Subcontractors for use thereof.

### Hoists cranes shall be operated by certified operator.

## SITE STORAGE/LOADING

### Confine work and operations of employees by Contract Documents. Do not unreasonably encumber premises with products.

### Do not load or permit to load any part of Work with a weight or force that will endanger the Work.

## CONSTRUCTION PARKING

### Parking will be permitted on site provided it does not disrupt performance of work.

### Provide and maintain adequate access to project site.

### Build and maintain temporary roads where indicated or directed by Owner and provide snow removal during period of Work.

### If authorized to use existing roads for access to project site, maintain such roads for duration of Contract and make good damage resulting from Contractor’s use of roads.

## CONTRACTOR’S SITE OFFICES

### Provide office heated to 22 oC, lighted 750 lx and ventilated, of sufficient size to accommodate site meetings and furnished with drawing laydown table, fax machine, telephone, file cabinet and chair. Provide an accessible washroom within the contractor’s site office.

### Accessible washroom, meeting space and entrance to contractor’s site office to meet the accessibility requirements of the NL Accessibility Act and Regulations, and CSA B651, Accessible Design for the Built Environment.

### Provide a clearly marked and fully stocked first-aid case in a readily available location.

### Subcontractors may provide their own offices as necessary. Direct location of these offices.

## OWNER’S SITE OFFICE

### Provide temporary office for Owner.

### Inside dimensions minimum 4.8 m long x 3 m wide x 2.4 m high, with floor 0.3 m above grade, complete with 4 - 50% opening windows and one lockable door. Door and access to the Owner’s site office to meet the accessibility requirements of the NL Accessibility Act and Regulations, and CSA B651, Accessible Design for the Built Environment.

### Insulate building and provide heating system to maintain 22˚C inside temperature at -20˚C outside temperature.

### Finish inside walls and ceiling with plywood, hardboard or wallboard and paint in selected colours. Finish floor with 19mm thick plywood.

### Install electrical lighting system to provide min 750 lx using surface mounted, shielded commercial fixtures with 10% upward light component.

### Site office to have washroom facility complete with running water and sewage disposal. Maintain supply of washroom supplies. Washroom to meet the accessibility requirements of the NL Accessibility Act and Regulations, and CSA B651, Accessible Design for the Built Environment.

### Equip office with drawing laydown table, fax machine, file cabinet, two chairs, telephone, phone line for internet.

### Maintain in clean condition.

## EQUIPMENT, TOOL AND MATERIALS STORAGE

### Provide and maintain, in a clean and orderly condition, lockable weatherproof sheds for storage of tools, equipment and materials.

### Locate materials not required to be stored in weatherproof sheds on site in a manner to cause least interference with work activities.

## SANITARY FACILITIES

### Provide sanitary facilities for work force in accordance with governing regulations and ordinances.

### Post notices and take precautions as required by local health authorities. Keep area and premises in sanitary condition.

## CLEAN-UP

### Remove construction debris, waste materials, packaging material from work site daily.

### Clean dirt or mud tracked onto paved or surfaced roadways.

### Store materials resulting from demolition activities that are salvageable.

# PRODUCTS (Not Applicable)

# EXECUTION (Not Applicable)

END OF SECTION