# GENERAL

## SECTION INCLUDES

### Barriers.

### Environmental Controls.

### Traffic Controls.

### Fire Routes.

## RELATED SECTIONS

### Section 01 51 00 – Temporary Utilities.

### Section 01 52 00 – Construction Facilities.

## INSTALLATION AND REMOVAL

### Provide temporary controls in order to execute Work expeditiously.

### Remove from site all such work after use.

## HOARDING

### Erect temporary site enclosures using 38 x 89 mm construction grade lumber framing at 600 mm centres, installed on 89 x 89 mm wood posts at 2400 mm centres or 50 mm dia. steel posts at 2400 mm centres. Posts to be place in post holes filled with concrete to minimum 900 mm depth. Finish temporary site enclosures with 1200 x 2400 x 13 mm exterior grade fir plywood to CSA O121 or chain link fence fabric to Section 32 31 13 – Chain Link Fences and Gates.

### Apply plywood panels or chain link fence fabric vertically flush and butt jointed.

### Provide one lockable truck entrance gate and at least one pedestrian door as directed and conforming to applicable traffic restrictions on adjacent streets. Equip gates with locks and keys.

### Erect and maintain pedestrian walkways including roof and side covers, complete with signs and electrical lighting as required by law.

### Paint public side of site enclosure in selected colours with one coat primer to CGSB 1.189M and one coat exterior paint to CGSB 1.59. Maintain public side of enclosure in clean condition.

### Provide barriers around trees and plants designated to remain. Protect from damage by equipment and construction procedures.

## GUARD RAILS AND BARRICADES

### Provide secure, rigid guard rails and barricades around deep excavations, open shafts, open stair wells, open edges of floors and roofs.

### Provide as required by governing authorities.

## WEATHER ENCLOSURES

### Provide weather tight closures to unfinished door and window openings, tops of shafts and other openings in floors and roofs.

### Close off floor areas where walls are not finished; seal off other openings; enclose building interior work for temporary heat.

### Erect enclosures to allow access for installation of materials and working inside enclosure.

### Design enclosures to withstand wind pressure and snow loading.

## DUST TIGHT SCREENS

### Provide dust tight screens or insulated partitions to localize dust generating activities, and for protection of workers, finished areas of Work and public.

### Maintain and relocate protection until such work is complete.

## ACCESS TO SITE

### Provide and maintain access roads, sidewalk crossings, ramps and construction runways as may be required for access to Work.

### Build and maintain temporary roads where indicated or directed and provide snow removal during period on work.

### If authorized to use existing roads for access to project site, maintain such roads for duration of Contract and make good damage resulting from Contractor’s use of roads.

## PUBLIC TRAFFIC FLOW

### Provide and maintain competent signal flag operators, traffic signals, barricades and flares, lights, or lanterns as required to perform Work and protect the public.

## FIRE ROUTES

### Maintain access to property including overhead clearances for use by emergency response vehicles.

## PROTECTION FOR OFF-SITE AND PUBLIC PROPERTY

### Protect surrounding private and public property from damage during performance of Work.

### Be responsible for damage incurred.

## PROTECTION OF BUILDING FINISHES

### Provide protection for finished and partially finished building finishes and equipment during performance of Work.

### Provide necessary screens, covers, and hoardings.

### Confirm with Owner locations and installation schedule 3 days prior to installation.

### Be responsible for damage incurred due to lack of or improper protection.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION