# GENERAL

## SECTION INCLUDES

### Field engineering survey services to measure and stake site.

### Survey services to establish and confirm inverts for Work.

### Recording of subsurface conditions found.

## QUALIFICATIONS OF SURVEYOR

### Qualified registered land surveyor, licensed to practise in the Province of Newfoundland and Labrador.

## SURVEY REFERENCE POINTS

### Existing base horizontal and vertical control points are designated on drawings.

### Locate, confirm and protect control points prior to starting site work. Preserve permanent reference points during construction.

### Make no changes or relocations without prior written notice to Owner.

### Report to Owner when reference point is lost or destroyed, or requires relocation because of necessary changes in grades or locations.

### Require surveyor to replace control points in accordance with original survey control.

## SURVEY REQUIREMENTS

### Establish permanent bench marks on site, referenced to established bench marks by survey control points. Record locations, with horizontal and vertical data in Project Record Documents.

### Establish lines and levels, locate and lay out, by instrumentation.

### Stake for grading, fill placement.

### Establish pipe invert elevations.

### Stake batter boards for foundations.

### Establish foundation column locations and floor elevations.

### Establish lines and levels for mechanical and electrical work.

## EXISTING SERVICES

### Where work involves breaking into or connecting to existing services, carry out work at times directed by authorities having jurisdiction, with minimum of disturbance to pedestrian and vehicular traffic.

### Before commencing work, establish location and extent of service lines in area of Work and notify Owner of findings.

### Remove abandoned service lines within 2.0 m of structures. Cap or otherwise seal lines at cut-off points as directed by Owner.

## LOCATION OF EQUIPMENT AND FIXTURES

### Location of equipment, fixtures and outlets indicated or specified are to be considered as approximate.

### Locate equipment, fixtures and distribution systems to provide minimum interference and maximum usable space and in accordance with manufacturer's recommendations for safety, access and maintenance.

### Inform Owner of impending installation and obtain approval for actual location.

### Submit field drawings to indicate relative position of various services and equipment when required by Owner.

## RECORDS

### Maintain a complete, accurate log of control and survey work as it progresses.

### Record locations of maintained, re-routed and abandoned service lines.

## SUBMITTALS

### Submit name and address of Surveyor to Owner.

### On request of Owner, submit documentation to verify accuracy of field engineering work.

### Submit certificate signed by surveyor certifying and noting those elevations and locations of completed Work that conform and do not conform with Contract Documents.

## SUBSURFACE CONDITIONS

### Promptly notify Consultant in writing if subsurface conditions at Place of Work differ materially from those indicated in Contract Documents, or a reasonable assumption of probable conditions based thereon.

### After prompt investigation, should Owner determine that conditions do differ materially, instructions will be issued for changes in Work.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION