# GENERAL

## SECTION INCLUDES

### Requirements and limitations for cutting and patching the Work.

## RELATED SECTIONS

### Section 01 11 00 - Summary of Work.

### Section 01 33 00 - Submittal Procedures.

## SUBMITTALS

### Submit written request in advance of cutting or alteration which affects:

#### Structural integrity of any element of Project.

#### Integrity of weather-exposed or moisture-resistant elements.

#### Efficiency, maintenance, or safety of any operational element.

#### Visual qualities of sight-exposed elements.

#### Work of Owner or separate contractor.

### Include in request:

#### Identification of Project.

#### Location and description of affected Work.

#### Statement on necessity for cutting or alteration.

#### Description of proposed Work, and products to be used.

#### Alternatives to cutting and patching.

#### Effect on Work of Owner or separate contractor.

#### Written permission of affected separate contractor.

#### Date and time work will be executed.

## PREPARATION

### Inspect existing conditions, including elements subject to damage or movement during cutting and patching.

### After uncovering, inspect conditions affecting performance of Work.

### Beginning of cutting or patching means acceptance of existing conditions.

### Provide supports to assure structural integrity of surroundings; provide devices and methods to protect other portions of project from damage.

### Provide protection from elements for areas which may be exposed by uncovering work; maintain excavations free of water.

### Obtain Owner’s approval before cutting, boring or sleeving load-bearing members.

## EXECUTION

### Execute cutting, fitting, and patching including excavation and fill, to complete Work.

### Fit several parts together, to integrate with other Work.

### Uncover Work to install ill-timed Work.

### Remove and replace defective and non-conforming Work.

### Provide openings in non-structural elements of Work for penetrations of mechanical and electrical Work.

### Execute Work by methods to avoid damage to other Work, and which will provide proper surfaces to receive patching and finishing.

### Employ original installer to perform cutting and patching for weather-exposed and moisture-resistant elements, and sight-exposed surfaces.

### Cut rigid materials using masonry saw or core drill. Pneumatic or impact tools not allowed on masonry work without prior approval.

### Restore work with new products in accordance with requirements of Contract Documents.

### Fit Work to pipes, sleeves, ducts, conduit, and other penetrations through surfaces.

### At penetration of fire rated wall, ceiling, or floor construction, completely seal voids with firestopping material in accordance with Section 07 84 00 - Firestopping, full thickness of the construction element.

### Refinish surfaces to match adjacent finishes: For continuous surfaces refinish to nearest intersection; for an assembly, refinish entire unit.

### Conceal pipes, ducts and wiring in floor, wall and ceiling construction of finished areas except where indicated otherwise.

### Make cuts with clean, true, smooth edges.

### Where new work connects with existing, and where existing work is altered, cut, patch and make good to match existing work.

## WASTE MANAGEMENT AND DISPOSAL

### Separate waste materials in accordance with Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION