# General

## SECTION INCLUDES

### Text, schedules and procedures for systematic Waste Management Program for construction, deconstruction, demolition, and renovation projects, including:

#### Diversion of Materials.

#### Waste Audit (WA) - Schedule A.

#### Waste Reduction Workplan (WRW) - Schedule B.

#### Demolition Waste Audit (DWA) - Schedule C.

#### Cost/Revenue Analysis Workplan (CRAW) - Schedule D.

#### Materials Source Separation Program (MSSP).

#### Canadian Governmental Responsibility for the Environment Resources - Schedule E.

## DEFINITIONS

### Demolition Waste Audit (DWA): Relates to actual waste generated from project.

### Materials Source Separation Program (MSSP): Consists of series of ongoing activities to separate reusable and recyclable waste material into material categories from other types of waste at point of generation.

### Recyclable: Ability of product or material to be recovered at end of its life cycle and re-manufactured into new product for reuse by others.

### Recycle: Process by which waste and recyclable materials are transformed or collected for purpose of being transferred into new products.

### Recycling: Process of sorting, cleansing, treating and reconstituting solid waste and other discarded materials for purpose of using in altered form.  Recycling does not include burning, incinerating, or thermally destroying waste.

### Reuse: Repeated use of product in same form but not necessarily for same purpose.  Reuse includes:

#### Salvaging reusable materials from re-modelling projects, before demolition stage, for resale, reuse on current project or for storage for use on future projects.

#### Returning reusable items including pallets or unused products to vendors.

### Salvage: Removal of structural and non-structural materials from deconstruction/disassembly projects for purpose of reuse or recycling.

### Separate Condition: Refers to waste sorted into individual types.

### Source Separation: Acts of keeping different types of waste materials separate beginning from first time they became waste.

## MATERIALS SOURCE SEPARATION PROGRAM (MSSP)

### Prepare MSSP and have ready for use prior to project start-up.

### Implement MSSP for waste generated on project in compliance with approved methods and as reviewed by authorities having jurisdiction.

### Provide on-site facilities for collection, handling, and storage of anticipated quantities of reusable and recyclable materials.

### Provide containers to deposit reusable and recyclable materials.

### Locate containers in locations, to facilitate deposit of materials without hindering daily operations.

### Locate separated materials in areas which minimize material damage.

### Collect, handle, store on-site, and transport off-site, salvaged materials in separate condition.

#### Transport to recycling facility.

## STORAGE, HANDLING AND PROTECTION

### Unless specified otherwise, materials for removal become Contractor's property.

### Protect, stockpile, store and catalogue salvaged items.

### Separate non-salvageable materials from salvaged items. Transport and deliver non-salvageable items to approved local facility.

### Protect structural components not removed for demolition from movement or damage.

### Support affected structures. If safety of building is endangered, cease operations and immediately notify Department having jurisdiction.

### Protect surface drainage, mechanical and electrical from damage and blockage.

### Separate and store materials produced during dismantling of structures in designated areas.

### Prevent contamination of materials to be salvaged and recycled and handle materials in accordance with requirements for acceptance by designated facilities.

#### On-site source separation is recommended.

## DISPOSAL OF WASTES

### Do not bury rubbish or waste materials.

### Do not dispose of any waste into waterways, storm, or sanitary sewers.

### Remove materials from deconstruction as deconstruction/disassembly Work progresses.

### Prepare project summary to verify destination and quantities on a material-by-material basis as identified in pre-demolition material audit.

## USE OF SITE AND FACILITIES

### Execute work with least possible interference or disturbance to normal use of premises.

### Provide security measures approved by Owner.

## SCHEDULING

### Coordinate Work with other activities at site to ensure timely and orderly progress of Work.

# Products (NOT APPLICABLE)

# Execution

## APPLICATION

### Handle waste materials not reused, salvaged, or recycled in accordance with appropriate regulations and codes.

## CLEANING

### Remove tools and waste materials on completion of Work, and leave work area in clean and orderly condition.

### Clean-up work area as work progresses.

### Source separate materials to be reused/recycled into specified sort areas.

## DIVERSION OF MATERIALS

### From following list, separate materials from general waste stream and stockpile in separate piles or containers, as reviewed by Owner and consistent with applicable fire regulations.

#### Mark containers or stockpile areas.

#### Provide instruction on disposal practices.

### On-site sale or distribution of salvaged materials to third parties is not permitted.

END OF SECTION