# GENERAL

## SECTION INCLUDES

### As-built, samples, and specifications.

### Equipment and systems.

### Product data, materials and finishes, and related information.

### Operation and maintenance data.

### Spare parts, special tools and maintenance materials.

### Warranties and bonds.

### Final site survey.

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 45 00 - Quality Control.

### Section 01 71 00 - Examination and Preparation.

### Section 01 77 00 - Closeout Procedures.

### Section 01 91 13.13 - Commissioning (Cx) Requirements.

## SUBMISSION

### Prepare instructions and data using personnel experienced in maintenance and operation of described products.

### Submit one copy of completed volumes in final form 15 days prior to final inspection.

### Copy will be returned after final inspection, with Owner’s comments.

### Revise content of documents as required prior to final submittal.

### Two weeks prior to Substantial Performance of the Work, submit to the Owner, two final copies of operating and maintenance manuals.

### Ensure spare parts, maintenance materials and special tools provided are new, undamaged or defective, and of same quality and manufacture as products provided in Work.

### If requested, furnish evidence as to type, source and quality of products provided.

### Defective products will be rejected, regardless of previous inspections. Replace products at own expense.

### Pay costs of transportation.

## FORMAT

### Organize data in the form of an instructional manual.

### Binders: vinyl, hard covered, 3 'D' ring, loose leaf 219 x 279 mm with spine and face pockets.

### When multiple binders are used, correlate data into related consistent groupings. Identify contents of each binder on spine.

### Cover: Identify each binder with type or printed title 'Project Record Documents'; list title of project and identify subject matter of contents.

### Arrange content under Section numbers and sequence of Table of Contents.

### Provide tabbed fly leaf for each separate product and system, with typed description of product and major component parts of equipment.

### Text: Manufacturer's printed data, or typewritten data.

### Drawings: provide with reinforced punched binder tab. Bind in with text; fold larger drawings to size of text pages.

### Provide CAD files in DWG format on CD. Also provide electronic files in PDF format.

## CONTENTS - EACH VOLUME

### Table of Contents: provide title of project; names, addresses, and telephone numbers of Consultant and Contractor with name of responsible parties; schedule of products and systems, indexed to content of volume.

### For each product or system:

#### List names, addresses and telephone numbers of subcontractors and suppliers, including local source of supplies and replacement parts.

### Product Data: mark each sheet to clearly identify specific products and component parts, and data applicable to installation; delete inapplicable information.

### Drawings: supplement product data to illustrate relations of component parts of equipment and systems, to show control and flow diagrams.

### Typewritten Text: as required to supplement product data. Provide logical sequence of instructions for each procedure, incorporating manufacturer's instructions specified in Section 01 45 00 - Quality Control.

### Training: Refer to Section 01 91 13.13 – Commissioning (Cx) Requirements.

## AS-BUILTS AND SAMPLES

### In addition to requirements in General Conditions, maintain at the site for Owner one record copy of:

#### Contract Drawings.

#### Specifications.

#### Addenda.

#### Change Orders and other modifications to the Contract.

#### Reviewed shop drawings, product data, and samples.

#### Field test records.

#### Inspection certificates.

#### Manufacturer's certificates.

### Store record documents and samples in field office apart from documents used for construction. Provide files, racks, and secure storage.

### Label record documents and file in accordance with Section number listings in List of Contents of this Project Manual. Label each document "PROJECT RECORD" in neat, large, printed letters.

### Maintain record documents in clean, dry and legible condition. Do not use record documents for construction purposes.

### Keep record documents and samples available for inspection by Owner.

## RECORDING ACTUAL SITE CONDITIONS

### Record information on set of blue line opaque drawings, provided by Owner.

### Provide felt tip marking pens, maintaining red color pens for recording information.

### Record information concurrently with construction progress. Do not conceal Work until required information is recorded.

### Contract Drawings and shop drawings: legibly mark each item to record actual construction, including:

#### Measured depths of elements of foundation in relation to finish first floor datum.

#### Measured horizontal and vertical locations of underground utilities and appurtenances, referenced to permanent surface improvements.

#### Measured locations of internal utilities and appurtenances, referenced to visible and accessible features of construction.

#### Field changes of dimension and detail.

#### Changes made by change orders.

#### Details not on original Contract Drawings.

#### References to related shop drawings and modifications.

### Specifications: legibly mark each item to record actual construction, including:

#### Manufacturer, trade name, and catalogue number of each product actually installed, particularly optional items and substitute items.

#### Changes made by Addenda and change orders.

### Other Documents: submit manufacturer's certifications, inspection certifications, field test records, required by individual specifications sections.

### At completion of project, provide all recorded information on print drawings. Transfer recorded information to AutoCAD files in DWG format. Submit DWG files, also with electronic files in PDF format as part of the Closeout Submittals.

## FINAL SURVEY

### Submit final site survey certificate certifying that elevations and locations of completed Work are in conformance, or non-conformance with Contract Documents.

## EQUIPMENT AND SYSTEMS

### Each Item of Equipment and Each System: include description of unit or system, and component parts. Give function, normal operation characteristics, and limiting conditions. Include performance curves, with engineering data and tests, and complete nomenclature and commercial number of replaceable parts.

### Panel board circuit directories: provide electrical service characteristics, controls, and communications.

### Include installed colour coded wiring diagrams.

### Operating Procedures: include start-up, break-in, and routine normal operating instructions and sequences. Include regulation, control, stopping, shut-down, and emergency instructions. Include summer, winter, and any special operating instructions.

### Maintenance Requirements: include routine procedures and guide for trouble-shooting; disassembly, repair, and reassembly instructions; and alignment, adjusting, balancing, and checking instructions.

### Provide servicing and lubrication schedule, and list of lubricants required.

### Include manufacturer's printed operation and maintenance instructions.

### Include sequence of operation by controls manufacturer.

### Provide original manufacturer's parts list, illustrations, assembly drawings, and diagrams required for maintenance.

### Provide installed control diagrams by controls manufacturer.

### Provide Contractor's coordination drawings, with installed colour coded piping diagrams.

### Provide charts of valve tag numbers, with location and function of each valve, keyed to flow and control diagrams.

### Provide list of original manufacturer's spare parts, current prices, and recommended quantities to be maintained in storage.

### Include test and balancing reports

### Additional requirements: As specified in individual specification sections.

## MATERIALS AND FINISHES

### Building Products, Applied Materials, and Finishes: include product data, with catalogue number, size, composition, and colour and texture designations. Provide information for re-ordering custom manufactured products.

### Instructions for cleaning agents and methods, precautions against detrimental agents and methods, and recommended schedule for cleaning and maintenance.

### Moisture-protection and Weather-exposed Products: include manufacturer's recommendations for cleaning agents and methods, precautions against detrimental agents and methods, and recommended schedule for cleaning and maintenance.

### Additional Requirements: as specified in individual specifications sections.

## SPARE PARTS

### Provide spare parts, in quantities specified in individual specification sections.

### Provide items of same manufacture and quality as items in Work.

### Deliver to site location as directed; place and store.

### Receive and catalogue all items. Submit inventory listing to Owner. Include approved listings in Maintenance Manual.

### Obtain receipt for delivered products and submit prior to final payment.

## MAINTENANCE MATERIALS

### Provide maintenance and extra materials, in quantities specified in individual specification sections.

### Provide items of same manufacture and quality as items in Work.

### Deliver to site location as directed; place and store.

### Receive and catalogue all items. Submit inventory listing to Owner. Include approved listings in Maintenance Manual.

### Obtain receipt for delivered products and submit prior to final payment.

## SPECIAL TOOLS

### Provide special tools, in quantities specified in individual specification section.

### Provide items with tags identifying their associated function and equipment.

### Deliver to project site place and store.

### Receive and catalogue all items. Submit inventory listing to Owner. Include approved listings in Maintenance Manual.

## STORAGE, HANDLING AND PROTECTION

### Store spare parts, maintenance materials, and special tools in manner to prevent damage or deterioration.

### Store in original and undamaged condition with manufacturer's seal and labels intact.

### Store components subject to damage from weather in weatherproof enclosures.

### Store paints and freezable materials in a heated and ventilated room.

### Remove and replace damaged products at own expense and to satisfaction of Owner.

## WARRANTIES AND BONDS

### Develop warranty management plan to contain information relevant to Warranties.

### Submit warranty management plan to Owner’s approval.

### Warranty management plan to include required actions and documents to assure that Owner receives warranties to which it is entitled.

### Provide plan in narrative form and contain sufficient detail to make it suitable for use by future maintenance and repair personnel.

### Assemble approved information in binder and submit upon acceptance of work. Organize binder as follows:

#### Separate each warranty or bond with index tab sheets keyed to Table of Contents listing.

#### List subcontractor, supplier, and manufacturer, with name, address, and telephone number of responsible principal.

#### Obtain warranties and bonds, executed in duplicate by subcontractors, suppliers, and manufacturers, within ten days after completion of the applicable item of work.

#### Except for items put into use with Owner's permission, leave date of beginning of time of warranty until the Date of Substantial Performance is determined.

#### Verify that documents are in proper form, contain full information, and are notarized.

#### Co-execute submittals when required.

#### Retain warranties and bonds until time specified for submittal.

### Include information contained in warranty management plan as follows:

#### Roles and responsibilities of personnel associated with warranty process, including points of contact and telephone numbers within the organizations of Contractors, subcontractors, manufacturers or suppliers involved.

#### Listing and status of delivery of Certificates of Warranty for extended warranty items, to include roofs, HVAC balancing, pumps, motors, transformers, and commissioned systems such as fire protection, alarm systems, sprinkler systems, lightning protection systems.

#### Provide list for each warranted equipment, item, feature of construction or system indicating:

##### Name of item.

##### Model and serial numbers.

##### Location where installed.

##### Name and phone numbers of manufacturers or suppliers.

##### Names, addresses and telephone numbers of sources of spare parts.

##### Warranties and terms of warranty: include one-year overall warranty of construction. Indicate items that have extended warranties and show separate warranty expiration dates.

##### Cross-reference to warranty certificates as applicable.

##### Starting point and duration of warranty period.

##### Summary of maintenance procedures required to continue warranty in force.

##### Cross-Reference to specific pertinent Operation and Maintenance manuals.

##### Organization, names and phone numbers of persons to call for warranty service.

##### Typical response time and repair time expected for various warranted equipment.

#### Procedure and status of tagging of equipment covered by extended warranties.

#### Post copies of instructions near selected pieces of equipment where operation is critical for warranty and/or safety reasons.

### Respond in a timely manner to oral or written notification of required construction warranty repair work.

### Written verification will follow oral instructions. Failure to respond will be cause for the Owner to proceed with action against Contractor.

## PRE-WARRANTY CONFERENCE

### Meet with Owner to develop understanding of requirements of this section. Schedule meeting prior to contract completion, and at time designated by Owner.

### Owner will establish communication procedures for:

#### Notification of construction warranty defects.

#### Determine priorities for type of defect.

#### Determine reasonable time for response.

## WARRANTY TAGS

### Tag, at time of installation, each warranted item. Provide durable, oil and water resistant tag approved by Owner.

### Leave date of acceptance until project is accepted for occupancy.

### Indicate following information on tag:

#### Type of product/material.

#### Model number.

#### Serial number.

#### Contract number.

#### Warranty period.

#### Inspector's signature.

#### Construction Contractor.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION (NOT APPLICABLE)

END OF SECTION