# General

## Section Includes:

### This Section specifies roles and responsibilities of Commissioning Training.

## Related Sections:

### Section 01 78 00 – Closeout Submittals.

### Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Section 01 91 13.16 – Commissioning (Cx) Forms.

## TRAINEES

### Trainees: personnel selected for operating and maintaining this facility including, but not limited to, Facility Manager, building operators, maintenance staff, security staff, and technical specialists as required.

### Trainees may be available for training during any stage of construction.

## INSTRUCTORS

### The Cx Manual will contain:

#### Descriptions of systems.

#### Instruction on design philosophy, design criteria, and design intent.

### Contractor and certified factory-trained manufacturers' personnel: to provide instruction on the following:

#### Start-Up, operation, shut-down and maintenance of equipment, components and systems.

#### Control features and reasons for, results of, implications on associated systems of adjustment of set points of control and safety devices.

#### Instructions on servicing, maintenance and adjustment of systems, equipment and components.

#### Training to be completed after Installation and Performance Verification are completed.

## TRAINING OBJECTIVES

### Training to be detailed and of sufficient duration to ensure:

#### Safe, reliable, cost-effective, energy-efficient operation of systems in normal and emergency modes under all conditions.

#### Effective on-going inspection, measurements of system performance.

#### Proper preventive maintenance, diagnosis, trouble-shooting and maintenance.

#### Ability to update documentation.

#### Ability to operate equipment and systems under emergency conditions until appropriate qualified assistance arrives.

## TRAINING MATERIALS

### Instructors to be responsible for content and quality. Provide copies for all those in attendance.

### Training materials to include:

#### "As-Built" Contract Documents.

#### Operating Manual.

#### Maintenance Manual.

#### Testing, adjusting and balancing and performance verification reports where applicable.

### Owner will review training manuals.

### Training materials to be in a format that permits future training procedures to the same degree of detail with or without the instructor.

## SCHEDULING

### Contractor to include in schedule time for training. Provide a detailed commissioning schedule indicating all Cx tasks and training.

### Deliver training during regular working hours, training sessions to be determined in Commissioning meetings.

### Training to be completed prior to Substantial Completion.

## RESPONSIBILITIES

### Be responsible for:

#### Implementation of training activities,

#### Coordination among instructors,

#### Quality of training, training materials,

### Owner will evaluate training and materials.

### Upon completion of training, provide written report, signed by Instructors, witnessed by Owner. Include list of those in attendance. The Cx manual will provide templates for these submittals.

## TRAINING CONTENT

### Training to include demonstrations by Instructors using the installed equipment and systems.

### Content includes:

#### Review of facility and occupancy profile.

#### Functional requirements.

#### System philosophy, limitations of systems and emergency procedures.

#### Review of system layout, equipment, components and controls.

#### Equipment and system start-up, operation, monitoring, servicing, maintenance and shut-down procedures.

#### System operating sequences, including step-by-step directions for starting up, shut-down, operation of valves, dampers, switches, adjustment of control settings and emergency procedures.

#### Maintenance and servicing.

#### Trouble-shooting diagnosis.

#### Inter-Action among systems during integrated operation.

#### Review of O&M documentation.

### Provide specialized training as specified in relevant Technical Sections of the construction specifications.

# Products (Not applicable)

# Execution (not applicable)

END OF SECTION