# GENERAL

## SUMMARY

### Section includes descriptions for demolishing, salvaging, recycling and removing site work items identified for removal in whole or in part, and for backfilling trenches and excavations resulting from site demolition activities.

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures

### Section 01 35 29.06 - Health and Safety Requirements

### Section 01 35 43 - Environmental Procedures

### Section 01 45 00 - Quality Control

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 31 23 33.01 - Excavating, Trenching and Backfilling.

## SUBMITTALS

### Shop drawings

#### Submit for approval drawings, diagrams or details showing sequence of demolition work and supporting structures and underpinning, where required by authorities having jurisdiction.

#### Submit drawings stamped and signed by qualified professional engineer licensed in Province of Newfoundland and Labrador, Canada.

### Hazardous Materials: provide description of Hazardous Materials and Notification of Filing with proper authorities prior to beginning of Work as required.

### Submit plan indicating:

#### Descriptions of and anticipated quantities of materials to be salvaged, reused, recycled and landfilled.

#### Detailed sequence of selective site demolition and removal work, with starting and ending dates for each activity.

#### Number and location of dumpsters.

#### Anticipated frequency of tippage.

#### Interruption of utility services.

#### Coordination for shutoff, capping, and continuation of utility services.

#### Locations of temporary partitions and means of egress.

### Submit copies of certified weigh bills, bills of landing from authorized disposal sites and reuse and recycling facilities for material removed from upon request from Owner.

### Proposed Dust Control and Noise Control:

#### Submit statement or drawing that indicates measures proposed for use, proposed locations, and proposed time frame for their operation.

### Qualification Data:

#### Submit information for companies and personnel indicating their capabilities and experience to perform work of this Section including; but not limited to, lists of completed projects with project names and addresses, for work of similar complexity and extent.

## ADMINISTRATIVE REQUIREMENTS

### Coordinate with Owner for the material ownership including the following:

#### Except for items or materials indicated to be reused, salvaged, reinstalled, or otherwise indicated to remain Owner's property. Demolished materials shall become Contractor’s property and shall be removed from Project site.

#### Historic items, relics, and similar objects including, but not limited to, cornerstones and their contents, commemorative plaques and tablets, antiques, and other items of interest or value to Owner that may be encountered during demolition remain Owner’s property:

##### Carefully remove and salvage each item or object in a manner to prevent damage and deliver promptly to Owner.

##### Coordinate with Owner, who will establish special procedures for removal and salvage operations.

### Convene pre-installation meeting one week prior to beginning work of this section to:

#### Verify project requirements.

#### Review installation and substrate conditions.

#### Verify existing site conditions adjacent to demolition work.

#### Coordinate with other construction sub trades.

#### Arrange for site visit with Owner to examine existing site conditions adjacent to demolition work, prior to start of Work.

### Hold project meetings every month.

#### Ensure key personnel, site supervisor, project manager, subcontractor representatives attend.

### Scheduling:

#### Employ necessary means to meet project time lines without compromising specified minimum rates of material diversion.

#### Notify Owner in writing when unforeseen delays occur.

## DELIVERY, STORAGE AND HANDLING

### Protect existing items designated to remain and items designated for salvage. In event of damage to such items, immediately replace or make repairs to approval of Owner and at no cost to Owner.

### Remove and store materials to be salvaged, in manner to prevent damage.

### Store and protect in accordance with requirements for maximum preservation of material.

## SITE CONDITIONS

### In all circumstances ensure that demolition work does not adversely affect adjacent water courses groundwater and wildlife, or contribute to excess air and noise pollution.

### Do not dispose, of waste or volatile materials such as mineral spirits, oil, petroleum based lubricants, or toxic cleaning solutions into watercourses, storm or sanitary sewers.  Ensure proper disposal procedures are maintained throughout project.

### Do not pump water containing suspended materials into watercourses, storm or sanitary sewers, or onto adjacent properties.

### Control disposal or runoff of water containing suspended materials or other harmful substances in accordance with local authorities.

### Protect trees, plants and foliage on site and adjacent properties where indicated.

### Prevent extraneous materials from contaminating air beyond application area, by providing temporary enclosures during demolition work.

### Cover or wet down dry materials and waste to prevent blowing dust and debris. Control dust on all temporary roads.

### Conduct selective site demolition so Owner's operations will not be disrupted.

#### Provide not less than three (3) working days’ notice to Owner of activities that will affect operations.

#### Maintain access to existing walkways, exits, and other adjacent occupied or used facilities. Closing or obstructing walkways, exits, or other occupied or used facilities without written permission from Owner is not permitted.

### Owner assumes no responsibility for Selective Site elements being demolished.

#### Conditions existing at time of inspection for bidding purpose will be maintained by Owner as far as practical.

#### Before selective site demolition, remove, protect and store salvaged items as directed by Owner.

## EXISTING CONDITIONS

### Prior to start of any demolition work remove contaminated or hazardous materials as defined by authorities having jurisdiction from site and dispose of at designated disposal facilities.

### Site elements that will be demolished are based on their condition on date that tender is accepted.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION

## EXAMINATION

### Survey existing conditions and correlate with requirements indicated to determine extent of selective site demolition required.

### Owner does not guarantee that existing conditions are the same as those indicated in Project Record Documents.

### Inventory and record the condition of items being removed and salvaged.

### When unanticipated mechanical, electrical, or structural elements are encountered, investigate and measure the nature and extent of the element. Promptly submit a written report to Owner.

### Perform an engineering survey of condition of adjacent buildings to determine whether removing any site element might result in structural deficiency or unplanned collapse of any portion of structure or adjacent structures during selective site demolition operations.

### Locate and protect utilities. Preserve active utilities traversing site in operating condition.

### Notify and obtain approval of utility companies before starting demolition.

## PREPARATION

### Temporary Erosion and Sedimentation Control:

#### Provide temporary erosion and sedimentation control measures to prevent soil erosion and discharge of soil-bearing water runoff or airborne dust to adjacent properties and walkways.

#### Inspect, repair, and maintain erosion and sedimentation control measures during demolition.

#### Remove erosion and sedimentation controls and restore and stabilize areas disturbed during removal after completion of demolition work.

### Protection of in-place conditions:

#### Prevent movement, settlement or damage of adjacent structures, services, walks, paving, trees, landscaping, adjacent grades properties, parts of existing building to remain.

##### Provide bracing, shoring and underpinning as required.

##### Repair damage caused by demolition as directed by Owner.

#### Support affected site elements and, if safety of site element being demolished, adjacent structures, or services appears to be endangered, take preventative measures, stop Work and immediately notify Owner.

#### Prevent debris from blocking surface drainage system, elevators, mechanical and electrical systems which must remain in operation.

### Surface Preparation:

#### Disconnect electrical and service lines within the site to be demolished.

#### Disconnect and cap designated mechanical services.

#### Septic Tanks:

##### Pump out buried septic tanks, left in place. Fill with sand.

##### Remove tanks within area of new construction or under paved areas and slabs.

## REMOVAL OF HAZARDOUS WASTES

### Remove contaminated or dangerous materials defined by authorities having jurisdiction, relating to environmental protection, from site and dispose of in safe manner to minimize danger at site or during disposal.

## REMOVAL OPERATIONS

### Remove items as indicated.

### Do not disturb items designated to remain in place.

### Removal of Pavements, Curbs and Gutters

#### Square up adjacent surfaces to remain in place by saw cutting or other method approved by Owner.

#### Protect adjacent joints and load transfer devices.

#### Protect underlying and adjacent granular material.

### When removing asphalt pavement for subsequent incorporation into hot mix asphalt concrete paving, prevent contamination with base course aggregates.

### When removing pipes under existing or future pavement area, excavate at least 300mm below pipe invert.

### Decommission water wells and monitoring wells in accordance with Provincial guidelines and regulations.

### Removal from site

#### Interim removal of stockpiled material will be required by Owner, if it is deemed to interfere with operations of Owner or other contractors.

### Sealing

#### .1	Seal pipe ends and walls of manholes or catch basins as indicated. Securely plug to form watertight seal.

### Backfill

#### .1	Backfill in areas as indicated

## RESTORATION

### Restore areas and existing works outside areas of demolition to match conditions of adjacent, undisturbed areas.

### Use soil treatments and procedures which are not harmful to health, are not injurious to plants, and do not endanger wildlife, adjacent water courses or ground water.

## CLEAN UP

### Upon completion of work, remove debris, trim surfaces and leave work site clean.

### Use cleaning solutions and procedures which are not harmful to health, are not injurious to plants, and do not endanger wildlife, adjacent water courses or ground water.

END OF SECTION