# GENERAL

## SUMMARY

### This Section includes:

#### Demolition and removal of selected portions of interior building components and finishes.

#### Repair procedures for selective demolition operations.

### This section does not include:

#### Removal of hazardous materials or asbestos abatement.

#### Demolition of exterior building components or structural elements.

#### Mechanical or electrical equipment, except as required to make minor modifications to allow the work to be completed.

## RELATED SECTIONS

### Section 01 11 00 – Summary of Work

### Section 01 35 29.06 - Health and Safety Requirements

### Section 01 35 43 - Environmental Procedures

### Section 01 52 00 – Construction Facilities

### Section 01 56 00 - Temporary Barriers and Enclosures

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal

### Section 02 41 13- Selective Site Demolition.

## REFERENCES

### American National Standards Institute (ANSI)

#### ANSI A10.8, Safety Requirements for Scaffolding.

### CSA Group (CSA)

#### CSA S350, Code of Practice for Safety in Demolition of Structures.

### National Fire Protection Association (NFPA)

#### NFPA 241 13, Standard for Safeguarding Construction, Alteration, and Demolition Operations

## DEFINATIONS

### Demolish: Detach items from existing construction and legally dispose of them off site, unless indicated to be removed and salvaged or removed and reinstalled.

### Remove and Salvage: Detach items from existing construction and deliver them to Owner.

### Remove and Reinstall: Detach items from existing construction, prepare them for reuse, and reinstall them where indicated.

### Existing to Remain: Existing items of construction that are not removed and that are not otherwise indicated as being removed, removed and salvaged, or removed and reinstalled.

### Hazardous Substances: Dangerous substances, dangerous goods, hazardous commodities and hazardous products may include asbestos, mercury and lead, PCB s, poisons, corrosive agents, flammable substances, radioactive substances, or other material that can endanger human health or wellbeing or environment if handled improperly as defined by the Federal Hazardous Products Act (RSC 1985) including latest amendments.

## ADMINISTRATIVE REQUIREMENTS

### Except for items or materials indicated to be reused, salvaged, reinstalled, or otherwise indicated to remain Owner’s property. Demolished materials shall become Contractor’s property and shall be removed from Project site.

### Coordinate selective demolition work so that work of this Section adheres to aesthetic criteria established by the Drawings and specified dimensions with all elements in planes as drawn, maintaining their relationships with all other building elements.

### Historic items, relics, and similar objects including, but not limited to, cornerstones and their contents, commemorative plaques and tablets, antiques, and other items of interest or value to Owner that may be encountered during selective demolition remain Owner’s property:

#### Carefully remove and salvage each item or object in a manner to prevent damage and deliver promptly to Owner.

#### Coordinate with Owner, who will establish special procedures for removal and salvage.

### Pre Demolition Meeting: Convene pre-installation meeting one (1) week prior to beginning work of this Section, with Owner to:

#### Confirm extent of salvaged and demolished materials.

#### Review Contractor’s demolition plan:

##### Verify existing site conditions adjacent to demolition work.

##### Coordination with other construction sub trades.

## ACTION AND INFORMATION SUBMITTALS

### Provide the following submittals before starting any work of this Section:

#### Schedule of Selective Demolition Activities:

##### Detailed sequence of selective demolition and removal work, with starting and ending dates for each activity.

##### Coordinate with Owner ongoing site operations, and limit the number of interruptions during regular business hours.

##### Interruption of utility services.

##### Coordination for shutoff, capping, and continuation of utility services.

##### Use of elevator and stairs.

##### Locations of temporary partitions and means of egress, including for others affected by selective demolition operations.

##### Coordination with Owner continuing occupancy of portions of existing building and of partial occupancy of completed Work.

### Demolition Plan: Submit a plan of demolition area indicating extent of temporary facilities and supports, methods of removal and demolition prepared by a professional engineer in accordance with requirements of Authority Having Jurisdiction, and as follows:

#### Proposed Noise Control and Dust Control Measures: Submit statement or drawing that indicates the measures proposed for use, proposed locations, and proposed time frame for their operation. Owner reserves the right to make modifications where proposed methods interfere with the Owner’s ongoing operation.

#### Inventory: Submit a list of items that have been removed and salvaged after selective demolition is complete.

## SITE CONDITIONS

### Owner will occupy portions of building immediately adjacent to selective demolition area:

#### Conduct selective demolition so that Owner’s operations will not be disrupted.

#### Provide not less than 72 hours’ notice to Owner of activities that will affect Owner’s operations.

### Maintain access to existing means of egress, walkways, corridors, exits, and other adjacent occupied or used facilities:

#### Do not close or obstruct means of egress, walkways, corridors, exits, or other occupied or used facilities without written acceptance from authorities having jurisdiction.

### Discovery of Hazardous Substances:

#### It is not expected that Hazardous Substances will be encountered in the Work. Immediately notify Owner if materials suspected of containing hazardous substances are encountered.

### Hazardous Substances:

#### Hazardous Substances are present in building to be selectively demolished. A report on the presence of Hazardous Substances is attached as an information document to this Specification for review and use. Examine report to become aware of locations where hazardous materials are present. Coordinate removal of hazardous materials as per appropriate sections of this specification.

# PRODUCTS

## TEMPORARY SUPPORT STRUCTURES

### Design temporary support structures required for demolition work and underpinning and other foundation supports necessary for the project using a qualified professional engineer registered or licensed in Province of Newfoundland and Labrador.

## DESCRIPTION

### This section of the Work includes, but is not necessarily limited to, the following:

#### Demolition, removal completely from site, and disposal of all identified components, materials, equipment and debris.

#### Selective demolition to allow new walls, bulkheads, ceilings and other materials to meet existing construction as indicated.

#### All material from demolition shall be removed from site immediately with no salvage, selling, sorting or burning permitted on site.

#### Retain items indicated on drawings for re use in new construction.

## DEBRIS

### Make all arrangements for transport and disposal of all demolished materials from the site.

## EQUIPMENT

### Provide all equipment required for safe and proper demolition of the building interiors indicated.

## REPAIR MATERIALS

### Use repair materials identical to existing materials:

#### If identical materials are unavailable or cannot be used for exposed surfaces, use materials that visually match existing adjacent surfaces to the fullest extent possible.

#### Use a material whose installed performance equals or surpasses that of existing material.

#### Comply with material and installation requirements specified in individual Specification Sections.

### Floor Patching and Levelling Compounds: Cement based, trowelable, self levelling compounds compatible with specified floor finishes; gypsum based products are not acceptable for work of this Section.

### Concrete Unit Masonry: Lightweight concrete masonry units, and mortar, cut and trimmed to fit existing opening to be filled. Provide standard hollow core units, square end units and bond beam units as indicated on drawings.

### Gypsum Board Patching Compounds: Joint compound to ASTM C475/C475M, bedding and finishing types thinned to provide skim coat consistency to patch and prepare existing gypsum board walls ready for new finishes in accordance with Section 09 21 16 – Gypsum Board Assemblies.

### Hoarding and Dust Screens: Refer to Sections 01 35 99 – Dust Control Procedures and 01 56 00 - Temporary Barriers and Enclosures for stud framing and gypsum board sheathing materials.

## EXISTING MATERIALS

### Items to be retained for re use in new construction include, but are not limited to the following: (Note: List to be complied below)

# EXECUTION

## EXAMINATION

### Verify that utilities have been disconnected and capped.

### Survey existing conditions and correlate with requirements indicated to determine extent of selective demolition required.

### Inventory and record the condition of items to be removed and reinstalled and items to be removed and salvaged.

### Notify the Owner where existing mechanical, electrical, or structural elements conflict with intended function or design:

#### Investigate and measure the nature and extent of conflict and submit a written report to Owner.

#### Owner will issue additional instructions or revise drawings as required to correct conflict.

### Perform surveys as the work progresses to detect hazards resulting from selective demolition activities.

## UTILITY SERVICES

### Coordinate existing services indicated to remain and protect them against damage during selective demolition operations.

### Locate, identify, disconnect, and seal or cap off indicated utilities serving areas to be selectively demolished.

#### Arrange to shut off affected utilities with utility companies.

#### If utility services are required to be removed, relocated, or abandoned, before proceeding with selective demolition provide temporary utilities that bypass area of selective demolition and that maintain continuity of service to other parts of building.

#### Cut off pipe or conduit in walls or partitions to be removed. Cap, valve, or plug and seal remaining portion of pipe or conduit after bypassing.

#### Cut off pipe or conduit to a minimum of 25 mm below slab, and remove concrete mound. Patch concrete using cementitious grout.

### Coordinate with Mechanical and Electrical Divisions for shutting off, disconnecting, removing, and sealing or capping utilities.

### Do not start selective demolition work until utility disconnecting and sealing have been completed and verified in writing.

## PREPARATION

### Identify and mark all equipment and materials identified to be retained by Owner or to be re used in subsequent construction. Separate and store items to be retained in an area away from area of demolition and protect from accidental disposal.

### Post warning signs on electrical lines and equipment that must remain energized to serve other areas during period of demolition.

### Confirm that all electrical and telephone service lines entering buildings are not disconnected.

### Do not disrupt active or energized utilities crossing the demolition site.

### Provide and maintain barricades, warning signs, protection for workmen and the public during the full extent of the Work. Read drawings carefully to ascertain extent of protection required.

### Mark all materials required to be re used, store in a safe place until ready for re installation.

### Adjust all junction boxes, receptacles and switch boxes flush with new wall construction where additional layers to existing construction are indicated.

### Remove permanent marker lines used or found on exposed surfaces and at surfaces indicated for subsequent finish materials. Mechanically remove permanent marker lines and associated substrates where permanent marker lines occur and patch surface. Sealing or priming over permanent marker lines is not acceptable.

## CONCRETE SLAB REINFORCING

### Locate location of reinforcing steel in concrete slabs prior to cutting or coring using non destructive, non ionizing radio frequency locators.

### Core concrete slabs to avoid reinforcing steel, electrical conduit or water pipes; adjust core location and coordinate with Engineer where slab features interfere with core drilling.

### Notify the Owner immediately for further instructions where coring or cutting will damage existing slab features.

## SELECTIVE DEMOLITION

### Demolish and dismantle work in a neat and orderly manner and in strict accordance with all regulations.

### At end of each day s work, leave Work in safe condition so that no part is in danger of toppling or falling.

### Demolish in a manner to minimize dusting and to prevent migration of dust.

### Selling or burning of materials on the site is not permitted.

### Remove concrete bases by cutting and chipping, take precautions against slab cracking and degradation. Grind edges smooth, fill and make level with self levelling grout.

### Fill all openings in concrete block walls with concrete masonry units, coursing to match existing, prepare ready to receive new finishes to match existing.

#### Provide bond beams in new openings cut into existing concrete masonry unit walls.

#### Provide finished end masonry units to patch and repair for new jamb sections in existing concrete masonry unit walls.

### Fill all openings in gypsum board walls with gypsum board and steel framing to match existing, skim coat to make wall smooth and even.

### Demolish existing carpet, resilient flooring and adhesive remnants as follows:

#### Vacuum existing carpet thoroughly, prior to removal, using vacuum equipped with power head/sweeper.

#### Apply fine mist water spray to carpet as required to minimize dust generation during removal. Avoid spraying near electrical outlets.

#### Demolish existing carpet and resilient floor finishes, remove and dispose of off site.

#### Remove adhesive to the greatest extent possible using scrapping tools and as follows:

##### Do not use solvent based cleaners to remove adhesive remnants.

##### Lightly shot blast or grind floor using machine designed for purpose to remove adhesive remnants.

##### Vacuum floor ready for application of skim coating.

##### Repair all slab depressions and damage with cementitious patching compound.

##### Skim coat floor with minimum 1 mm thick cementitious floor underlayment compatible with new flooring materials.

#### Floor substrate shall be smooth, free from ridges and depressions, and adhesive remnants that could telegraph through resilient flooring materials and carpets.

### Demolish existing ceramic tile finishes. Remove setting bed or adhesive to the greatest extent possible using mechanical scrapping tools and as follows:

#### Saw cut edge of tile for clean and even transition joint between existing tile to remain and new flooring materials

#### Lightly shot blast or grind floor to remove remnants of setting materials

#### Vacuum floor ready for application of skim coating

#### Repair all slab depressions and damage with cementitious patching compound. Skim coat floor with minimum 1 mm thick cementitious floor underlayment compatible with new flooring materials

### Demolish completely all ceiling panels and grid as indicated.

### Remove all wall coverings scheduled for demolition. Patch and repair wall surfaces with skim coat of gypsum board joint compound leaving wall surfaces smooth and even ready for new wall finishes.

### Patch and repair all walls, floor and ceilings damaged during demolition with material matching adjacent walls, prepare ready for new finishes.

### Patch and repair all radiation cabinets, mechanical equipment and electrical fixtures damaged or exposed during demolition to match adjacent finished surfaces.

## PATCHING AND REPAIRING

### Floors and Walls:

#### Where walls or partitions that are demolished extend from one finished area into another, patch and repair floor and wall surfaces in the new space.

#### Provide a level and smooth surface having uniform finish colour, texture, and appearance.

#### Remove existing floor and wall coverings and replace with new materials, if necessary, to achieve uniform colour and appearance.

#### Patch with durable seams that are as invisible as possible.

#### Provide materials and comply with installation requirements specified in other Sections of these Specifications.

#### Where patching occurs in a painted surface, apply primer and intermediate paint coats over patch and apply final paint coat over entire unbroken surface containing patch. Provide additional coats until patch blends with adjacent surfaces.

#### Where feasible, test and inspect patched areas after completion to demonstrate integrity of installation.

### Ceilings: patch, repair, or re hang existing ceilings as necessary to provide an even plane surface of uniform appearance.

## PROTECTION

### Prevent debris from blocking drainage inlets and systems and ground draining, and protect material and electrical systems and services that must remain in operation.

### Arrange demolition and shoring work so that interference with the use of adjoining areas by the Owner and users is minimized.

### Maintain safe access to and egress from occupied areas adjoining.

### Provide and maintain fire prevention equipment and alarms accessible during demolition.

## CLEANING

### Promptly as the Work progresses, and on completion, clean up and remove from the site all rubbish and surplus material. Remove rubbish resulting from demolition work daily.

### Maintain access to exits clean and free of obstruction during removal of debris.

### Keep surrounding and adjoining roads, lanes, sidewalks, municipal rights of way clean and free of dirt, soil or debris that may be a hazard to vehicles or persons.

END OF SECTION