# General

## RELATED REQUIREMENTS

### Section 01 11 00 - Summary of Work.

### Section 01 35 29.06 - Health and Safety Requirements.

### Section 01 35 43 - Environmental Procedures.

### Section 01 52 00 - Construction Facilities.

### Section 01 56 00 - Temporary Barriers and Enclosures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

## REFERENCE STANDARDS

### CSA International

#### CSA S350, Code of Practice for Safety in Demolition of Structures.

### National Research Council Canada (NRC)

#### National Building Code of Canada, Latest Edition.

#### National Fire Code of Canada, Latest Edition.

## SITE CONDITIONS

### If material resembling spray or trowel-applied asbestos or other designated substance be encountered, stop work, take preventative measures, and notify Owner immediately. Do not proceed until written instructions have been received.

### Notify Owner before disrupting access or services.

### Structures to be demolished to be based on their condition on date that tender is accepted.

### Salvage items as identified by Owner. Remove, protect and store salvaged items as directed by Owner. Deliver to Owner as directed.

## WASTE MANAGEMENT AND DISPOSAL

### Separate waste materials in accordance with Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

# Products (Not APPLICABLE)

# Execution

## EXAMINATION

### Inspect building and/or site with Owner and verify extent and location of items designated for removal, disposal, alternative disposal, recycling, salvage and items to remain.

### Locate and protect utilities. Preserve active utilities traversing site in operating condition.

### Notify and obtain approval of utility companies before starting demolition.

### Disconnect, cap, plug or divert, as required, existing public utilities within the property where they interfere with the execution of the work, in conformity with the requirements of the authorities having jurisdiction. Mark the location of these and previously capped or plugged services on the site and indicate location (horizontal and vertical) on the record drawings. Support, shore up and maintain pipes and conduits encountered.

#### Immediately notify Owner and utility company concerned in case of damage to any utility or service, designated to remain in place.

#### Immediately notify Owner should uncharted utility or service be encountered, and await instruction in writing regarding remedial action.

## PREPARATION

### Temporary Erosion and Sedimentation Control:

#### Provide temporary erosion and sedimentation control measures to prevent soil erosion and discharge of soil-bearing water runoff or airborne dust to adjacent properties and walkways, according to: requirements of authorities having jurisdiction.

#### Inspect, repair, and maintain erosion and sedimentation control measures during demolition.

#### Remove erosion and sedimentation controls and restore and stabilize areas disturbed during removal after completion of demolition work.

### Protection of In-Place Conditions:

#### Prevent movement, settlement, or damage to adjacent utilities, and parts of building and landscaping features, structures, to remain in place. Provide bracing and shoring required.

#### Keep noise, dust, and inconvenience to occupants to minimum.

#### Protect building systems, services and equipment.

#### Provide temporary dust screens, covers, railings, supports and other protection as required.

#### Do Work in accordance with Section 01 35 29.06- Health and Safety Requirements]

### Demolition/Removal:

#### Remove items as indicated.

#### Removal of Pavements, Curbs and Gutters:

##### Square up adjacent surfaces to remain in place by saw cutting or other method approved by Owner.

##### Protect adjacent joints and load transfer devices.

##### Protect underlying and adjacent granular materials.

#### Remove parts of existing building to permit new construction.

#### Trim edges of partially demolished building elements to tolerances as defined by Owner to suit future use.

## CLEANING

### Progress Cleaning: clean in accordance with Section 01 74 00 - Cleaning.

#### Leave Work area clean at end of each day.

### Final Cleaning: upon completion remove surplus materials, rubbish, tools and equipment.

END OF SECTION