# GENERAL

## RELATED SECTIONS

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 03 30 00 - Cast-in-Place Concrete.

## REFERENCES

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-25.20, Surface Sealer for Floors.

### Canadian Standards Association (CSA)

#### CSA-A23.1/A23.2, Concrete Materials and Methods of Concrete Construction/Methods of Test and Standard Practices for Concrete.

## PERFORMANCE REQUIREMENTS

### Product quality and quality of work in accordance with Section 01 61 00 - Common Product Requirements.

### Submit written declaration that components used are compatible and will not adversely affect finished flooring products and their installation adhesives.

## SUBMITTALS

### Provide manufacturer's printed product literature and data sheets for concrete finishes and include product characteristics, performance criteria, physical size, finish and limitations.

### Submit WHMIS SDS - Safety Data Sheets. WHMIS SDS acceptable to Labour Canada and Health and Welfare Canada for concrete floor treatment materials. Indicate VOC content.

### Include application instructions for concrete floor treatment.

## ENVIRONMENTAL REQUIREMENTS

### Temporary lighting:

#### Minimum 1200 W light source, placed 2.5 m above floor surface, for each 40 sq m of floor being treated.

### Electrical power:

#### Provide sufficient electrical power to operate equipment normally used during construction.

### Work area:

#### Make the work area water tight protected against rain and detrimental weather conditions.

### Temperature:

#### Maintain ambient temperature of not less than 10°C from 7 days before installation to at least 48 hours after completion of work and maintain relative humidity not higher than 40% during same period.

### Moisture:

#### Ensure concrete substrate is within moisture limits prescribed by flooring manufacturer.

### Safety:

#### Comply with requirements of Workplace Hazardous Materials Information System (WHMIS) regarding use, handling, storage, and disposal of hazardous materials.

### Ventilation:

#### Ventilate area of work as directed by Owner by use of approved portable supply and exhaust fans.

#### Ventilate enclosed spaces in accordance with Section 01 51 00 - Temporary Utilities.

#### Provide continuous ventilation during and after coating application.

# PRODUCTS

## CHEMICAL HARDENERS

### Type 1- Sodium silicate.

### Water: potable.

## SEALING COMPOUNDS

### Surface sealer: to CAN/CGSB-25.20, Type 2 - water based.

### Surface sealers may not be manufactured or formulated with aromatic solvents formaldehyde halogenated solvents mercury lead cadmium hexavelant chromium and their compounds.

## WET CURE

### Clear polyethylene film to ASTM C171, minimum thickness 0.15 mm.

## MIXES

### Mixing, ratios and application in accordance with manufacturer’s instructions.

## JOINT SEALANT

### Joint sealants to Section 07 92 00 – Joint Sealants.

# EXECUTION

## EXAMINATION

### Verify that slab surfaces are ready to receive work and elevations are as indicated on drawings by manufacturer.

## PREPARATION OF EXISTING SLAB

### Rub exposed sharp edges of concrete with carborundum to produce 3 mm radiused edges unless otherwise indicated.

### Saw cut control joints to CSA-A23.1/A23.2, 24 hours maximum after placing of concrete.

### Use mechanical stripping to remove chlorinated rubber or existing surface coatings.

### Use protective clothing, eye protection, respiratory equipment during stripping of chlorinated rubber or existing surface coatings.

## APPLICATION

### After floor treatment is dry, seal control joints and joints at junction with vertical surfaces with sealant.

### Apply floor treatment in accordance with Sealer manufacturer's written instructions.

### Clean overspray. Clean sealant from adjacent surfaces.

## PROTECTION

### Protect finished installation in accordance with manufacturer's instructions.

END OF SECTION