# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 43 39 – Mock Up Requirements.

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 04 05 00 - Common Work Results for Masonry.

### Section 04 05 13 - Masonry Mortar and Grout.

### Section 04 05 19 - Masonry Anchorage and Reinforcing.

### Section 04 05 23 - Masonry Accessories.

## REFERENCES

### American Society for Testing and Materials (ASTM).

#### ASTM C126, Standard Specification for, Facing Brick (Solid Masonry Units Made of Clay or Shale).

### Brick Industry Association (BIA).

#### Technical Note No. 20, Cleaning Brick Masonry.

### Canadian Standards Association (CSA)

#### CAN/CSA A82, Fired Masonry Brick Made From Clay or Shale.

#### CAN3-A165 Series, CSA Standards on Concrete Masonry Units.

#### CAN/CSA A371, Masonry Construction for Buildings.

## SUBMITTALS

### Product Data

#### Submit manufacturer's printed product literature, specifications and data sheet.

### Samples

#### Two of each type of masonry unit specified.

### Manufacturer's Instructions

#### Submit manufacturer's installation instructions.

## QUALITY ASSURANCE

### Mock up

#### .1	Construct mock-up in accordance with Section 01 43 39 – Mock Up Requirements.

#### .2	Construct mock-up 10 m 2  minimum of brick unit masonry in area designated by Owner before proceeding with brick unit masonry work.

### Test reports: certified test reports showing compliance with specified performance characteristics and physical properties.

### Certificates:  product certificates signed by manufacturer certifying materials comply with specified performance characteristics and criteria and physical requirements.

### Pre-installation meeting:  conduct pre-installation meeting to verify project requirements manufacturer’s instructions and manufacturer’s warranty requirements.

## QUALIFICATIONS

### Manufacturer: company specializing in manufacturing products of this section with minimum 10 years experience.

### Installer: company specializing in performing work of this section approved by manufacturer. Minimum 5 years experience.

### Design structural installations under direct supervision of Professional Engineer experienced in structural design of brick masonry installation and registered in the Province of Newfoundland and Labrador.

# PRODUCTS

## MANUFACTURED UNITS

### Face brick.

#### Burned clay brick: to CAN/CSA A82.

##### Type: FBX.

##### Grade: SW.

##### Size: Modular.

##### Colour and texture: to match approved sample.

### Back-up brick.

#### Burned clay brick: to CAN/CSA A82.

##### Type: II.

##### Grade: same as face brick.

##### Size: same as face brick.

## ACCESSORIES

### Brick Ties: to Section 04 05 19 – Masonry Anchorage and Reinforcing.

### Reinforcement: to Section 04 05 19 – Masonry Anchorage and Reinforcing.

### Connectors: to Section 04 05 19 – Masonry Anchorage and Reinforcing.

### Flashing: to Section 04 05 23 - Masonry Accessories.

### Mortar and Mortar Mixes: to Section 04 05 13 - Masonry Mortar and Grout.

### Grout and grout mixes:  to Section 04 05 13 - Masonry Mortar and Grout.

## Cleaning Compounds

### Use VOC products to limits listed in Section 01 35 21 - LEED® Requirements.

### Compatible with substrate and acceptable to masonry manufacturer for use on products.

### Cleaning compounds compatible with brick masonry units and in accordance with manufacturer's written recommendations and instructions.

# EXECUTION

## MANUFACTURER'S INSTRUCTIONS

### Compliance: comply with manufacturer's written data, including product technical bulletins, product catalogue installation instructions, product carton installation instructions, and data sheets.

## Preparation

### Protect adjacent finished materials from damage due to masonry work.

## INSTALLATION

### Do masonry work in accordance with CSA-A371 and CSA-A179, and as defined and specified in Section 04 05 00 – Common Work Results for Masonry.

## CLEANING

### Perform cleaning as soon as possible after installation to remove construction and accumulated environmental dirt.

### Clean unglazed clay masonry: 10 m² area of wall designated by Owner mock up panel specified in Section 04 05 00 - Common Work Results for Masonry as directed below and leave for one week. If no harmful effects appear and after mortar has set and cured, protect windows, sills, doors, trim and other work, and clean brick masonry as follows.

#### Remove large particles with wood paddles without damaging surface. Saturate masonry with clean water and flush off loose mortar and dirt.

#### Scrub with solution of 25 ml trisodium phosphate and 25 ml household detergent dissolved in 1 L of clean water using stiff fibre brushes, then clean off immediately with clean water using hose. Alternatively, use proprietary compound recommended by brick masonry manufacturer in accordance with manufacturer's directions.

#### Repeat cleaning process as often as necessary to remove mortar and other stains.

#### Use acid solution treatment for difficult to clean masonry as described in Technical Note No.20 by the Brick Institute Association.

### Clean concrete brick masonry as work progresses.

#### Allow mortar droppings on masonry to partially dry then remove by means of trowel, followed by rubbing lightly with small piece of brick and finally by brushing.

### Upon completion of installation, remove surplus materials, rubbish, tools and equipment barriers.

END OF SECTION