# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 61 00 - Common Product Requirements.

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 06 40 00 - Architectural Woodwork.

### Section 06 40 23.13 - Plastic Laminate Finishing for Interior Architectural Woodwork.

### Section 06 41 93 - Cabinet and Miscellaneous Hardware.

### Section 09 91 23 - Interior Painting.

## REFERENCES

### American National Standards Institute (ANSI)

#### ANSI A208.1, Particleboard.

#### ANSI A208.2, Medium Density Fibreboard (MDF).

#### ANSI/HPVA HP-1, American National Standard for Hardwood and Decorative Plywood.

### Architectural Woodwork Manufacturers Association of Canada (AWMAC) and Architectural Woodwork Institute (AWI)

#### Architectural Woodwork Quality Standards, 2nd Edition.

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-11.3, Hardboard.

### Canadian Standards Association (CSA)

#### CSA B111, Wire Nails, Spikes and Staples.

#### CSA O121, Douglas Fir Plywood.

#### CAN/CSA O141, Softwood Lumber.

#### CSA O151, Canadian Softwood Plywood.

#### CSA O153, Poplar Plywood.

### National Lumber Grades Authority (NLGA)

#### Standard Grading Rules for Canadian Lumber.

## QUALITY ASSURANCE

### Lumber by grade stamp of agency certified by Canadian Lumber Standards Accreditation Board (CLSAB).

### Plywood, particleboard, OSB and wood based composite panels to CSA and ANSI standards.

### Wood fire rated frames and panels: listed and labelled by an organization accredited by Standards Council of Canada to CAN4-S104 and CAN/ULC-S105.

## SUBMITTALS

### Indicate details of construction, profiles, jointing, fastening and other related details.

### Indicate materials, thicknesses, finishes and hardware.

## DELIVERY, STORAGE, AND HANDLING

### Deliver, handle, store and protect materials in accordance with Section 01 61 00 - Common Product Requirements.

### Protect materials against dampness during and after delivery.

### Store materials in ventilated areas, protected from extreme changes of temperature or humidity.

# PRODUCTS

## LUMBER MATERIAL

### Softwood lumber: unless specified otherwise, S4S, moisture content 19% or less in accordance with following standards:

#### CAN/CSA-O141.

#### NLGA Standard Grading Rules for Canadian Lumber.

#### AWMAC custom premium grade, moisture content as specified.

### Machine stress-rated lumber is acceptable.

### Hardwood lumber: moisture content 10 % or less in accordance with following standards:

#### National Hardwood Lumber Association (NHLA).

#### AWMAC custom grade, moisture content as specified.

## PANEL MATERIAL

### Panel materials to be urea-formaldehyde free.

### Douglas fir plywood (DFP): to CSA O121, standard construction.

### Canadian softwood plywood (CSP): to CSA O151, standard construction.

### Hardwood plywood: to ANSI/HPVA HP-1.

### Poplar plywood (PP): to CSA O153, standard construction.

### Hardboard: to CAN/CGSB-11.3.

### Medium density fibreboard (MDF): to ANSI A208.2, density 640-800 kg/m3.

### Decorative overlaid composite panels.

#### Decorative overlay, heat and pressure laminated with suitable resin to 12.7 mm thick particleboard MDF core.

#### Overlay bonded to both faces where exposed two sides, and when panel material require surface on one side only, reverse side to be overlaid with a plain (buff) balancing sheet.

#### Edge finishing: matching melamine and polyester overlay edge strip with self-adhesive.

## ACCESSORIES

### Nails and staples: to CSA B111; galvanized to CAN/CSA-G164 for exterior work, interior humid areas and for treated lumber; plain finish elsewhere.

### Wood screws: plain, type and size to suit application.

### Splines: wood

### Adhesive: recommended by manufacturer.

### Use least toxic sealants, adhesives, sealers, and finishes necessary to comply with requirements of this section.

# EXECUTION

## INSTALLATION

### Do finish carpentry to Quality Standards of the Architectural Woodwork Manufacturers Association of Canada (AWMAC), except where specified otherwise.

### Scribe and cut as required, fit to abutting walls, and surfaces, fit properly into recesses and to accommodate piping, columns, fixtures, outlets, or other projecting, intersecting or penetrating objects.

### Form joints to conceal shrinkage.

## CONSTRUCTION

### Fastening.

#### Position items of finished carpentry work accurately, level, plumb, true and fasten or anchor securely.

#### Design and select fasteners to suit size and nature of components being joined. Use proprietary devices as recommended by manufacturer.

#### Set finishing nails to receive filler. Where screws are used to secure members, countersink screw in round cleanly cut hole and plug with wood plug to match material being secured.

#### Replace items of finish carpentry with damage to wood surfaces including hammer and other bruises.

### Standing and running trim.

#### Butt and cope internal joints of baseboards to make snug, tight, joint. Cut right angle joints of casing and base with mitred joints.

#### Fit backs of baseboards and casing snugly to wall surfaces to eliminate cracks at junction of base and casing with walls.

#### Make joints in baseboard, where necessary using a 45° scarf type joint.

#### Install door and window trim in single lengths without splicing.

### Stairs.

#### Install stairs to location and details as indicated.

### Shelving.

#### Install shelving on shelf brackets, where indicated.

### Hardware.

#### Install cabinet and miscellaneous hardware as indicated.

### Panelling:

#### Secure panelling and perimeter trim using adhesive recommended for purpose by manufacturer. Fill nail holes caused by temporary fixing with filler matching wood in colour.

#### Secure panelling and perimeter trim using concealed fasteners.

#### Secure panelling and perimeter trim using counter sunk screws plugged with matching wood plugs.

### Handrails, wall rails and bumper rails.

#### Install handrails, wall rails and bumper rails in locations indicated.

#### Make joints hair line, dowelled and glued.

#### Install support brackets as required.

#### Install brackets at ends and at 600 mm on centre minimum at intermediate spacings.

#### Install metal backing plates between studs at bracket locations to ensure proper support for brackets and bolts or self-tapping screws.

#### Secure using counter sunk screws plugged with matching wood plugs.

## TOUCHUP AND PROTECTION

### Fill and retouch all nicks, chips and scratches in factory finishes and substrate materials to AWS standards. Replace damaged items that cannot be repaired to AWS standards.

### Protect installed products and components from damage during construction.

### Repair damage to adjacent materials caused by finish carpentry installation.

### Leave work to be site finished ready for finishing by Section 09 91 23 – Interior Painting.

END OF SECTION