# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 61 00 - Common Product Requirements.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 06 20 00 - Finish Carpentry.

### Section 06 40 00 - Architectural Woodwork.

## REFERENCES

### American National Standards Institute (ANSI) / Builders Hardware Manufacturers Association (BHMA)

#### ANSI/BHMA A156.9, Cabinet Hardware.

#### ANSI/BHMA A156.11, Cabinet Locks.

#### ANSI/BHMA A156.16, Auxiliary Hardware.

#### ANSI/BHMA A156.18, Materials and Finishes.

## SUBMITTALS

### Product Data:

#### Submit manufacturer's printed product literature, specifications and data sheet.

### Hardware List:

#### Submit contract hardware list.

#### Indicate specified hardware, including make, model, material, function, finish and other pertinent information.

### Manufacturer's Instructions:

#### Submit manufacturer's installation instructions.

### Closeout Submittals:

#### Provide maintenance data, parts list, and manufacturer's instructions for incorporation into maintenance manual specified in Section 01 78 00 - Closeout Submittals.

## DELIVERY, STORAGE, AND HANDLING

### Deliver, store, handle and protect materials in accordance with Section 01 61 00 - Common Product Requirements.

### Store cabinet hardware in locked, clean and dry area.

### Package items of hardware including fastenings, separately or in like groups of hardware, label each package as to item definition and location.

# PRODUCTS

## HARDWARE ITEMS

### Use one manufacturer's product for all similar items.

## CABINET HARDWARE

### Cabinet hardware: to ANSI/BNMA A156.9, designated by letter B and numeral identifiers listed in Hardware Schedule indicated on drawings.

#### Hinges:  European style hinge with 110° swing of operation for face frame construction cabinets.

#### Pulls: surface mounted pull.

#### Knobs: surface mounted knob.

#### Latches: elbow latch.

#### Catches: friction catch.

#### Shelf rests and standards: adjustable shelf standards, with open shelf rests.

#### Shelf brackets and standards: vertical slotted shelf standard, with shelf brackets.

#### Drawer slides: side mounted drawer slides.

#### Track and guides for sliding panels: surface or recessed mounted with anti-friction inserts.

### Cabinet locks: to ANSI/BNMA A156.11, designated by letter E and numeral identifiers listed in Hardware Schedule.

#### Door or drawer locks: half mortised into back of door or drawer

#### Cylinders: key to keying system as directed

## FASTENINGS

### Supply screws, bolts, expansion shields and other fastening devices required for satisfactory installation and operation of hardware.

### Exposed fastening devices to match finish of hardware.

### Use fasteners compatible with material through which they pass.

## KEYING

### Cabinet locks to be as keyed alike in a room or as directed. Submit keying schedule for approval.

### Provide keys in duplicate for every type of lock in this Contract.

### Stamp keying code numbers on keys and cylinders.

# EXECUTION

## MANUFACTURER'S INSTRUCTIONS

### Compliance: comply with manufacturer's written data, including product technical bulletins, product catalogue installation instructions, product carton installation instructions, and data sheets.

## INSTALLATION

### Install hardware to standard hardware location dimensions in accordance with manufacturer's recommendations and to project design requirements.

## ADJUSTING

### Lubricate hardware and other moving parts, as recommended by manufacturer.

### Adjust cabinet door hardware to provide tight fit at contact points with frames.

## CLEANING

### Perform cleaning after installation to remove construction and accumulated environmental dirt.

### Clean hardware with damp rag and approved non-abrasive cleaner, and polish hardware in accordance with manufacture's instructions.

### Remove protective material from hardware items where present.

### Upon completion of installation, remove surplus materials, rubbish, tools and equipment barriers.

## DEMONSTRATION

### Keying System Setup:

#### Set up key control system with file key tags, duplicate key tags, numerical index, alphabetical index and key change index, label shields, control book and key receipt cards.

### Designated Staff Briefing.

#### Brief designated staff regarding:

##### Proper care, cleaning, and general maintenance of projects complete hardware.

##### Description, use, handling, and storage of keys.

### Demonstrate operation, operating components, adjustment features, and lubrication requirements.

END OF SECTION