# General

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 78 00 - Closeout Submittals.

### Section 06 40 00 - Architectural Woodwork.

## references

### American National Standards Institute (ANSI)

#### ANSI Z124.3, Plastic Lavatories.

#### ANSI Z124.6, Plastic Sinks.

## SUMMARY

### This section includes the following horizontal and trim solid surface product types:

#### Counters

#### Vanity Tops

## SUBMITTALS

### Submit duplicate samples: sample size 300 x 300 mm or 300 mm long unless specified otherwise.

### Submit duplicate colour samples of acrylic solid surfacing for colour selection.

## Delivery, STorage and handling

### Protect against dampness and damage during and after delivery.

### Store in ventilated areas, protected from extreme changes of temperature or humidity.

## WARRANTY

### Provide a written guarantee, signed and issued in the name of the owner, by the Solid Surface Manufacturer, stating that the solid surface material is free from manufacturer’s defects and will remain free from defects for a period of ten (10) years from the date of Certificate of Substantial Completion.

### Warranty to be non-prorated.

# Products

## MATERIALS

### Solid Acrylic components:

#### Cast, nonporous, filled polymer, not coated, laminated or of composite construction with through body colours meeting ANSI Z124.3 or ANSI Z124.6, having minimum physical and performance properties specified.

#### Superficial damage to a depth of 0.25 mm shall be repairable by sanding and/or polishing.

### Thickness: 13 mm.

## Fabrication

### Shop assembly:

#### Fabricate components to greatest extent practical to sizes and shapes indicated, in accordance with approved shop drawings and manufacturer’s printed instructions and technical bulletins.

### Form joints between components using manufacturer’s standard joint adhesive without conspicuous joints.

#### Reinforce with strip of solid acrylic material, 50 mm wide.

### Provide factory cutouts for plumbing fittings and accessories as indicated on drawings.

### Rout and finish component edges with clean, sharp returns.

# Execution

## EXamination

### Examine substrates and conditions, with fabricator present for compliance with requirements for installation tolerances and other conditions affecting performance of work.

### Proceed with installation only after unsatisfactory conditions have been corrected.

## installation

### Install components plumb, level and rigid, scribed to adjacent finishes, in accordance with approved shop drawings and product data.

#### Provide product in largest pieces available.

#### Form field joints using manufacturer’s recommended adhesive, with joints inconspicuous in finished work.

##### Exposed joints/seams shall not be allowed.

#### Reinforce field joints with solid surface strips extending a minimum of 25 mm on either side of the seam with the strip being the same thickness as the top.

#### Cut and finish component edges with clean, sharp returns.

#### Rout Radii and contours to template.

#### Anchor securely to base cabinets or other supports.

#### Align adjacent countertops and form seams to comply with manufacturer’s written recommendations using adhesive in colour to match countertop.

#### Carefully dress joints smooth, remove surface scratches and clean entire surface.

#### Install countertops with no more than 3.0 mm sag, bow or other variation from a straight line.

## Cleaning

### Keep components clean during installation.

### Remove adhesives, sealants and other stains.

## repair

### Repair or replace damaged work which cannot be repaired to Owner satisfaction.

END OF SECTION