# GENERAL

## SECTION INCLUDES

### Materials and installation for, mineral fibre, cellulose and polystyrene loose fill insulations for manual or blowing applications in horizontal or vertical surfaces.

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 51 00 - Temporary Utilities.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 07 26 00 – Vapour Retarders.

## REFERENCES

### American Society for Testing and Materials, (ASTM)

#### ASTM C516, Standard Specification for Vermiculite Loose Fill Thermal Insulation.

#### ASTM C549, Standard Specification for Perlite Loose Fill Insulation.

### Canadian General Standards Board (CGSB)

#### CAN/CGSB 51.34, Vapour Barrier, Polyethylene Sheet for Use in Building Construction.

### Canadian Standards Association (CSA)

#### CSA B149 PACKAGE, Consists of B149.1, Natural Gas and Propane Installation Code and B149.2, Propane Storage and Handling Code.

### National Research Council Canada (NRC) / Institute for Research in Construction (IRC) - Canadian Construction Materials Centre (CCMC)

#### CCMC, Registry of Product Evaluations.

### Underwriters' Laboratories of Canada (ULC)

#### CAN/ULC-S702, Thermal Insulation, Mineral Fibre, for Buildings (Supersedes CSA A101).

## QUALITY ASSURANCE

### Provide 2 copies of Certification of Coverage and Application Chart in accordance with Appendix A, CAN/ULC – S702, to Owner certified by Applicator’s signature that the information is correct.

## SUBMITTALS

### Submit proof of manufacturer's CCMC Listing and listing number to Owner.

### Manufacturer's Instructions: Provide to indicate special handling criteria, installation sequence and cleaning procedures.

### Submit product data sheets for system materials. Include product characteristics, performance criteria, and limitations.

### Submit WHMIS SDS –Safety Data Sheets. Include VOC content.

## SITE ENVIRONMENTAL REQUIREMENTS

### Apply insulation only when surfaces and ambient temperatures are within manufacturers' prescribed limits.

### Safety: Comply with requirements of Workplace Hazardous Materials Information System (WHMIS) regarding use, handling, storage, and disposal of insulation materials.

### Ventilation:

#### Ventilate area of work as directed by Owner by use of approved portable supply and exhaust fans.

#### Ventilate enclosed spaces.

#### Provide continuous ventilation during and after insulation application. Run ventilation system 24 hours per day during installation; provide continuous ventilation for 3 days after completion of insulation installation.

### Protection

#### Provide temporary enclosures to prevent dust from contaminating air beyond application area.

#### Protect adjacent surfaces and equipment from damage by fall-out, and dust.

# PRODUCTS

## MATERIALS

### Mineral fibre insulation: to CAN/ULC-S702, asbestos-free mineral fibre.

#### Type 5 - blowing wool, suitable for application by means of pneumatic equipment.

### Vapour retarder: in accordance with Section 07 26 00 - Vapour Retarder.

# EXECUTION

## INSPECTION

### Ensure that wall cavity is not obstructed.

## LOOSE GRANULAR INSTALLATION

### Pneumatically place loose granular insulation above ceiling between joists to provide minimum thermal resistance value RSI as indicated.

### Ensure ceiling areas exposed to outside air are insulated.

### Ensure unobstructed air circulation to eave vents.

### Install baffles as indicated to prevent insulation from spilling over top of exterior wall and causing blockage of soffit vents, and to prevent displacement of insulation by wind entering vents.

### Keep insulation minimum 75 mm from heat emitting devices such as recessed light fixtures, and minimum 50 mm from sidewalls of CAN4-S604 type A chimneys and CSA B149.1 and CSA B149.2 type B and L vents.

## CLEANING

### Remove insulation material spilled during installation and leave work area ready for application of wall board.

END OF SECTION