# GENERAL

## RELATED WORK

### Section 01 33 00 – Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

### Section 07 62 00 – Sheet Metal Flashing and Trim.

### Section 07 92 00 - Joint Sealants.

## REFERENCES

### American Society of Mechanical Engineers (ASME)

#### ASME B18.6.3, Machine Screws, Tapping Screws, and Metallic Drive Screws (Inch Series).

### American Society for Testing and Materials (ASTM)

#### ASTM A653/A 653M, Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy Coated (Galvannealed) by the Hot-Dip Process.

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-41.24, Rigid Vinyl Siding, Soffits and Fascia.

#### CAN/CGSB-51.32, Sheathing, Membrane, Breather Type.

### Canadian Standards Association (CSA)

#### CSA B111, Wire Nails, Spikes and Staples.

## SUBMITTALS

### Product Data: Submit manufacturer's printed product literature, specifications and data sheet.

#### Submit two copies of WHMIS MSDS - Material Safety Data Sheets. Indicate VOC's for caulking materials during application and curing.

### Submit duplicate 300 x 300 mm samples of siding material, of colour and profile specified.

### Shop drawings to indicate dimensions, siding profiles, attachment methods, schedule of wall elevations, trim and closure pieces, soffits, fascia, and related work.

### Submit manufacturer’s installation instructions.

## Warranty

### Provide a lifetime limited, non-prorated warranty, signed and issued in the name of the Owner, stating vinyl siding is free from manufacturer’s defects which result in chipping, cracking, flaking, peeling, splitting or blistering, and will resist denting due to its high impact resistance. Warranty to be from the date of Substantial Completion.

### Provide workmanship guarantee for a period of 2 (two) years from the date of Substantial Completion.

# PRODUCTS

## MATERIALS

### Rigid vinyl: extruded polyvinylchloride to CAN/CGSB-41.24 wood grain or embossed finish, vertical bevel profile, 2 x 100 mm wide x maximum permissible length, of colour selected by Owner.

### Accessories: internal corners, external corners, cap strip, drip cap, undersill trim, starter strip and window/door trim of extruded plastic, same material and colour as siding, with nailing strip pre-punched.

### Exterior wall sheathing membrane: to CAN/CGSB-51.32 spunbonded olefin type as indicated.

### Fasteners: nails to CSA B111, screws to ASME B18.6.3 aluminum purpose made.

### Galvanized steel sheet: commercial grade to ASTM A652M with Z275 zinc coating.

### Aluminum sheet: mill finish plain utility sheet, 0.80 mm thick.

# EXECUTION

## INSTALLATION

### Install one layer sheathing membrane horizontally by nailing lapping edges 75 mm.

### Install metal sill as indicated.

### Install window/door opening flashings, starter strips, inside corners, edgings, drip and cap.

### Install siding sequentially from starter strip up, in accordance with manufacturer/fabricators written instructions.

### Install exterior corners, fillers and closure strips with carefully formed and profiled work.

### Maintain joints in exterior panels, true to line, tight fitting, hairline joints.

### Seal junctions with dissimilar materials with sealant. Do work in accordance with Section 07 92 00 - Joint Sealants.

### Attach components in manner not restricting thermal movement. Conceal fasteners where possible.

## CLEANING

### Upon completion of installation, remove surplus materials, rubbish, tools and equipment barriers.

END OF SECTION