# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

### Section 07 52 00 - Modified Bituminous Membrane Roofing.

### Section 07 61 00 - Sheet Metal Roofing.

### Section 07 62 00 - Sheet Metal Flashing and Trim.

### Section 07 92 00 - Joint Sealants.

## REFERENCES

### The Aluminum Association Inc. (AA)

#### Aluminum Sheet Metal Work in Building Construction.

#### AA DAF45, Designation System for Aluminum Finishes.

### American Society for Testing and Materials (ASTM International)

#### ASTM A653/A653M, Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process.

#### ASTM A792/A792M, Standard Specification for Steel Sheet, 55% Aluminum-Zinc Alloy-Coated by the Hot-Dip Process.

#### ASTM D523, Standard Test Method for Specular Gloss.

#### ASTM D822, Standard Practice for Filtered Open-Flame Carbon-Arc Exposures of Paint and Related Coatings.

### Canadian General Standards Board (CGBS)

#### CAN/CGSB-37.5, Cutback Asphalt Plastic Cement.

### Canadian Standards Association (CSA International)

#### CSA B111, Wire Nails, Spikes and Staples.

## SUBMITTALS

### Submit duplicate 50 x 50 mm samples of each type of sheet metal material, colour and finish.

### Clearly indicate bending, folding, jointing, fastening installation details.

## DELIVERY and STORAGE

### Store products off ground and under cover in a dry, well ventilated enclosure.

### Stack pre-formed material in manner to prevent twisting, bending and rubbing.

### Provide protection for galvanized and pre-coated surfaces.

### Prevent contact of dissimilar metals during storage. Protect from acids, flux, and other corrosive materials and elements.

# PRODUCTS

## MATERIALS

### Sheet aluminum 0.64 mm thick.  Color as selected by Owner.

### Trough size:  125 mm wide.

### Trough Supports:  continuous aluminum with a perforated aluminum cover that covers the complete trough to prevent debris from getting stuck in the trough and downpipe.

### Downpipes:  0.64 mm thick aluminum.

### Downpipe straps:  0.72 mm thick aluminum.

### Sealant:  As per Section 07 92 00 – Joint Sealants.

### Elbows and tees:  aluminum same as trough.

## FABRICATION

### Fabricate sheet aluminum work in accordance with Aluminum Association Aluminum Sheet Metal Work in Building Construction.

### Fabricate eavestrough in continuous length up to a maximum length of 12 metres.

### Form eavestrough to an Ogee profile, 125 mm wide and a 305 mm girth.

# EXECUTION

## INSTALLATION

### Install trough supports/debris catchers to provide a continuous slope to drain all water from the trough.

### Cut opening in the trough to receive the downpipes.

### Install the trough and snap in to the supports (no exposed screws or nails permitted).  Install elbows and tees as required.  Provide for expansion joints to prevent warping where required.

### Install aluminum downpipes to a distance of 1.5 metres from the grade.  Install aluminum straps 1200 mm o.c designed to match the pipe profile and fasten to building with aluminum or stainless steel screws.

### Install sewer type downpiping from the aluminum downpiping to a point 300 mm above the grade.  Install aluminum straps designed to suit the pipe profile and fasten to the wall with aluminum or stainless steel screws.

### Install sealant as required to ensure all joints are watertight.

### When work is completed, provide a water test to ensure there are no leaks and that all the water runs from the trough.

## CLEANING

### On completion and verification of performance of installation, remove surplus materials, excess materials, rubbish, tools and equipment.

### Leave works areas clean, free from grease, finger marks and stains.

END OF SECTION