General

## RELATED SECTION

### Section 01 33 00 - Submittal Procedures

### Section 01 61 00 - Common Product Requirements

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal

### Section 01 78 00 - Closeout Submittals

### Section 04 21 13 - Brick Masonry

### Section 09 21 16 - Gypsum Board Assemblies

### Section 09 30 13 - Ceramic Tiling

### Section 09 30 15 - Quarry and Paver Tiling

## SHOP DRAWINGS

### Submit catalogue details for each type of door illustrating profiles, dimensions and methods of assembly.

## SAMPLES

### Submit one sample of each type of hand entry access door.

### Submit one 300 x 300 mm corner sample of each type of body entry door.

## CLOSEOUT SUBMITTALS

### Provide maintenance data for cleaning and maintenance of stainless steel finishes for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

## waste management and disposal

### Separate and recycle waste materials in accordance with Section 01 74 21 – Construction/Demolition Waste Management and Disposal, and with the Waste Reduction Workplan.

### Remove from site and dispose of all packaging materials at appropriate recycling facilities.

### Collect and separate for disposal, paper, plastic, polystyrene, corrugated cardboard, packaging material in appropriate on-site bins for recycling in accordance with Waste Management Plan.

### Divert unused metal materials from landfill to metal recycling facility as approved by Owner.

## DELIVERY, STORAGE AND HANDLING

### Deliver, store and handle materials in accordance with Section 01 61 00 - Common Product Requirements.

### Apply temporary protective coating to finished surfaces. Remove coating after erection. Do not use coatings that will become hard to remove or leave residue.

### Leave protective covering in place until final cleaning of building.

Products

## ACCESS DOORS

### Sizes: Except as indicated otherwise, to be minimum sizes as follows:

#### For body entry: 600 x 600 mm.

#### For hand entry: 300 x 300 mm.

### Construction: Rounded safety corners, concealed hinges, screwdriver latch, anchor straps, able to open 180o.

### Materials

#### Tiled or marble surfaces and other special areas: Stainless steel with brushed satin or polished finish as directed by Owner.

#### Other areas: Prime coated steel.

## EXCLUSIONS

### Lay-in tile ceilings: use unobtrusive identification locators.

Execution

## INSTALLATION

### Installation:

#### Tiled or marble surfaces: to Section 09 30 13 - Ceramic Tiling.

#### Masonry Surfaces:  to be specified in other Divisions.

#### Drywall surfaces: to Section 09 21 16 - Gypsum Board Assemblies.

## LOCATION

### Location: Ensure that equipment is within view and accessible for operating, inspecting, adjusting, servicing without using special tools.

END OF SECTION