# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 43 39 – Mock Up Requirements.

### Section 01 61 00 - Common Product Requirements.

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 09 30 13 - Ceramic Tiling.

## REFERENCES

### American National Standards Institute (ANSI)/Ceramic Tile Institute (CTI)

#### ANSI/CTI A108.1, Specification for the Installation of Ceramic Tile.

### American Society for Testing and Materials (ASTM)

#### ASTM C136, Test Method for Sieve Analysis of Fine and Coarse Aggregates.

#### ASTM C207, Specification for Hydrated Lime for Masonry Purposes.

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-8.1, Sieves, Testing, Woven Wire, Metric.

#### CAN/CGSB-51.34, Vapour Barrier, Polyethylene Sheet, for Use in Building Construction.

#### CGSB 71-GP-29M, Adhesive, Elastomeric, for Installation of Quarry Tiles.

#### CGSB 71-GP-30M, Adhesive, Epoxy and Modified Mortar Systems, for Installation of Quarry Tiles.

#### CAN/CGSB-75.1, Tile, Ceramic.

### Canadian Standards Association (CSA)

#### CAN/CSA-A3000, Cementitious Materials Compendium (Consists of A5, A8, A23.5, A362, A363, A456.1, A456.2, A456.3).

### Terrazzo, Tile and Marble Association of Canada (TTMAC)

#### Tile Installation Manual.

## SUBMITTALS

### Submit proof of manufacturer's CCMC Listing and listing number to Owner.

### Manufacturer's Instructions: Provide to indicate special handling criteria, installation sequence, cleaning procedures.

### Submit duplicate 600 x 600 mm sample panels of each colour, texture, size and pattern of quarry tile.

### Adhere tile samples to 11 mm thick plywood and grout joints to represent project installation.

## DELIVERY, STORAGE AND HANDLING

### Deliver, store, handle and protect materials in accordance with Section 01 61 00 - Common Product Requirements.

### Deliver, store and handle products in manner to avoid damage.

### Have materials delivered to job site just prior to installation.

### Deliver products to job site in manufacturer's unopened cartons with labels intact and legible.

### Keep cartons dry and protected from vandalism and away from heavy traffic areas.

### Store cartons in upright position.

## ENVIRONMENTAL REQUIREMENTS

### Safety: Comply with requirements of Workplace Hazardous Materials Information System (WHMIS) regarding use, handling, storage, and disposal of materials.

### Ventilation

#### Provided continuously during and after installation. Run system during installation.

### Temperature.

#### Maintain ambient temperature of not less than 12o C from 72 hours before installation until fully cured.

## MAINTENANCE

### Extra Materials.

#### Provide maintenance materials in accordance with Section 01 78 00 – Closeout Submittals.

#### Provide minimum 2 % of each type and colour of quarry tile required for project maintenance use. Store where directed.

#### Maintenance material to be of same production run as installed material.

## MOCK-UP

### Construct mock-ups in accordance with Section 01 43 39 – Mock Up Requirements.

## QUALITY ASSURANCE

### Provide certificate of quality compliance from tile manufacturer.

### Provide certificate of quality compliance form tile installer upon satisfactory completion of installation.

# PRODUCTS

## TILES AND PAVERS

### Quarry tile: to CAN/CGSB-75.1, Type 4, Class MR 2, size as indicated on drawings, slip resistant face, square edges, colour as selected by Owner. Matching coved base, size as indicated on drawings.

## MORTAR AND ADHESIVE MATERIALS

### Cement: to CAN/CSA A3000.

### Sand:

#### Crushed or pit run consisting of hard durable particles free from clay lumps, cementation, organic material, frozen material and other deleterious materials.

#### Gradations to be within limits specified when tested to ASTM C136. Sieve sizes to CAN/CGSB-8.1.

| Sieve Designation | % Passing |
| --- | --- |
| 4.75 mm | 100 |
| 2.36 mm | 95-100 |
| 1.18 mm | 60-100 |
| 0.600 mm | 35-80 |
| 0.300 mm | 15-50 |
| 0.150 mm | 2-15 |
| 0.075 mm | 0-5 |

#### Hydrated lime: to ASTM C207.

#### Latex additive: formulated for use in cement mortar.

#### Water: potable and free of minerals which are detrimental to mortar and grout mixes.

#### Dry set mortar water retentive cement mortar, to ANSI A108.1

#### Elastomeric adhesive: to CGSB 71-GP-29M.

#### Epoxy adhesive: to CGSB 71-GP-30M, Type 1.

#### Modified Mortar adhesive: to CGSB 71-GP-30M, Type 2.

#### Colour pigment: non fading mineral oxides, unaffected by lime or cement and which will not stain tile.

## GROUT

### Thin set system grout.

### Grout preparation: to manufacturer's instructions.

## ACCESSORIES

### Floor sealer: to CAN/CGSB 25.20, Type 1.

### Protective coating: to tile and grout manufacturer's recommendations.

### Sealants: Section 07 92 00 – Joint Sealants.

# EXECUTION

## WORKMANSHIP

### Do tile work in accordance with TTMAC Tile Installation Manual, except where specified otherwise.

### Apply thin set mortar bed to clean and sound surfaces.

### Fit tile units around corners, fitments, fixtures, drains and other built-in objects. Maintain uniform joint appearance. Make cut edges smooth and even.

### Maximum surface tolerance: 1:800.

### Make joints between tiles uniform and approximately 6 mm wide, plumb, straight, true, even and with adjacent units flush. Align patterns.

### Lay out units so perimeter tiles are minimum ½ size.

### Sound tiles after setting and replace hollow sounding units to obtain full bond.

### Make internal angles square, external angles bullnosed.

### Construct base 100 mm high with bullnosed top edge.

### Use bullnose edged tiles at termination of wall tiles, except where tiles butt projecting surface or differing plane.

### Install divider strips at junction of tile flooring and dissimilar material.

### Clean installed tile surfaces after installation cured.

### Keep building expansion joints free of mortar or grout.

### Use slip resistant tiles in designated area.

## SETTING SYSTEM

### Install tile and bases on substrate in accordance with TTMAC details.

## CONTROL JOINTS

### Provide control joints 6.0 mm wide at 5000 mm intervals each way in all heated areas.

### Provide control joints around perimeter of large areas, around columns, in locations where area changes direction and where tile abuts other hard material. Place control joints directly over subfloor expansion/control joints.

### Fill joints with sealant.

## FLOOR SEALER AND PROTECTIVE COATING

### Apply 2 coats in accordance with manufacturer's printed instructions.

## PROTECTION OF FINISHED WORK

### Protect new floors from time of final set of adhesive until final inspection.

### Prohibit traffic on floor for 48 hours after installation.

## COMMISSIONING

### Train user staff in the care and cleaning of tile and in the application of sealers.

### Train user staff in the repair and/or replacement of damaged tiles, using sample previously submitted.

END OF SECTION