# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 43 39 – Mock Up Requirements.

### Section 01 51 00 - Temporary Utilities.

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

## REFERENCES

### Canadian General Standards Board (CGSB)

#### CGSB 41-GP-30M, Wall Coverings, Vinyl-Coated Fabrics.

### Underwriters Laboratories of Canada (ULC)

#### CAN/ULC-S102, Method of Test for Surface Characteristics of Building Materials and Assemblies.

## SUBMITTALS

### Submit WHMIS MSDS - Material Safety Data Sheets. WHMIS acceptable to Labour Canada, and Health and Welfare Canada for vinyl-coated fabric wall coverings and adhesives. Indicate VOC content.

### Submit duplicate 280 x 215mm samples of each colour and texture of wall coverings together with complete written description, including total fabric weight, name of fabric backing, tensile strength, tear strength and fire rating and fire detection characteristics.

### Before commencing application, prepare wall and apply sample of each texture wall covering from current production run of materials selected to show evidence there are no roller marks or other imperfections which may occur during manufacturing process of wall coverings to three full wall panels, for Owner approval.

## MOCK-UPS

### Construct mock-ups in accordance with Section 01 43 39 – Mock Up Requirements.

### Apply vinyl-coated wall covering of each finish and decorative effect to 10 m²area of surface to be covered. Approximately three full wall panels.

## CLOSEOUT SUBMITTALS

### Provide maintenance data for vinyl-coated fabric wall covering in accordance with Section 01 78 00 - Closeout Submittals.

## ENVIRONMENTAL REQUIREMENTS

### Temperature: Maintain air temperature and structural base temperature at wall covering installation area above 20°C for 72 hours before, during and 72 hours after installation.

### Ventilation:

#### Ventilate enclosed spaces in accordance with Section 01 51 00 - Temporary Utilities.

#### Provide continuous ventilation during and after coating application.

# PRODUCTS

## MATERIALS

### Wall covering: to CGSB 41-GP-30M, Type 2, pretrimmed 1380 mm width, colour as selected by Owner. Surface burning characteristics in accordance with CAN/ULC-S102.

### Sealer: type recommended by covering manufacturer.

### Sizing: type recommended by covering manufacturer.

### Adhesive: as recommended by covering manufacturer.

# EXECUTION

## PREPARATION

### Unwrap wall covering when ventilation conditions are accelerated, and allow to acclimatize in installation area for 24 hours before application.

### Prepare surfaces according to covering manufacturer's instructions.

### Work penetrating substrate to be completed before installing covering.

### Seal and size surfaces to receive covering.

## INSTALLATION

### Installation sequence:

#### Use rolls in consecutive numerical sequence of manufacture.

#### Place panels consecutively in exact order they are cut from roll; including spaces above or below windows, doors or similar penetrations.

#### Reverse alternate strips except on match patterns.

### Trim additional salvage where required to achieve colour and pattern match at seams.

### Apply adhesive to fabric back and/or substrate, as recommended by manufacturer.

### Hang non-matched patterns by overlapping edges and double cutting through both thicknesses with metal back-up strip to prevent cutting substrate.

### Wrap fabric 150 mm beyond inside and outside corners. No cutting at corners permitted, unless pattern or colour changes.

### No horizontal seams permitted.

### Install covering before installation of plumbing fixtures, electrical equipment casings, bases and cabinets.

### Remove excess adhesive as work progresses and leave clean.

### Leave completed work smooth, clean, without wrinkles, gaps, overlaps or air pockets.

## CLEANING

### Clean surfaces to covering manufacturer's written instructions.

## PROTECTION

### Protect finished surfaces and exterior corners from damage until final inspection.

## SCHEDULES

### See finish schedule for colours and locations.

## commissioning

### Instruct Owner on cleaning, provide data on approved cleaning agents.

END OF SECTION