# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

### Section 06 20 00 - Finish Carpentry.

### Section 09 91 23 - Interior Painting.

### Section 10 11 16 - Markerboards.

## REFERENCES

### Aluminum Association (AA)

#### DAF 45, Designation System for Aluminum Finishes.

### American National Standards Institute (ANSI)

#### ANSI A135.4, Hardboard Standard.

#### ANSI A208.1, Particleboard.

#### ANSI A208.2, Medium Density Fiberboard for Interior Use.

### Underwriter’s Laboratories of Canada (ULC)

#### CAN/ULC-S102, Surface Buring Characteristics of Building Materials and Assemblies.

#### CAN/ULC-S706, Standard for Wood Fibre Insulating Boards for Buildings.

## SUBMITTALS

### Indicate location, type, size, panel arrangement, backing, hardware, anchor or mounting details, frame or trim and accessories.

### Submit duplicate 300 x 300 mm sample of each type of tackboard and 300 mm long sample of each type of trim.

### Submit manufacturer's printed product literature, specifications and data sheet.

#### Submit two copies of WHMIS SDS - Safety Data. Indicate VOC's:

##### For caulking materials during application and curing.

##### For adhesives.

### Submit manufacturer’s installation instructions.

## REGULATORY REQUIREMENTS

### Surface burning characteristics of materials: listed and labeled by an organization accredited by Standards Council of Canada.

# PRODUCTS

## MATERIALS

### Utility sheet aluminum: plain, 1.5 mm minimum thickness.

### Laminating adhesive: to manufacturer's standard.

### Mounting adhesive: to manufacturer's standard.

### Anchor clips, brackets and fasteners: concealed type recommended by manufacturer selected by Owner for fixed mounting.

### Facings:

#### Natural cork tackboards: single layer natural cork fine grain sheet, 6.0 mm thick, natural colour.

### Core:

#### Fibreboard: to CAN/ULC-S706, Type II, natural color.

### Backing:

#### Fibreboard to CAN/ULC-S706, Type II.

## COMPONENTS

### Extruded aluminum: Aluminum Association alloy AA6063-T5. Minimum 1.5 mm wall thickness.

### Tackboard trim and framing: perimeter trim or frame, map rail with cork insert, of manufacturer's standard sections appropriate for installation conditions.

## FABRICATION

### Fabricate tackboard panels to sizes indicated.

### Install trim on panels in factory. Make mitres and joints to hair-line fit, free of rough edges with concealed brackets to reinforce and hold joints tight and flush. No exposed fasteners permitted.

### Overlap trim 6.0 mm onto panels. Provide closed ends for open-end extrusions.

### Factory fit assemblies too large for shipment to site in one piece, disassemble for delivery and site assembly.

## FINISHES

### Aluminum trim finishes.

#### Finish exposed surfaces of aluminum components in accordance with Aluminum Association Designation System for Aluminum Finishes.

#### Clear anodic finish: designation AA-M32, C 12, C 22 A 31.

#### Appearance and properties of anodized finishes designated by the Aluminum Association as Architectural Class 1, Architectural Class 2, and Protective and Decorative.

# EXECUTION

## MANUFACTURER'S INSTRUCTIONS

### Compliance: comply with manufacturer's written data, including product technical bulletins, product catalogue installation instructions, product carton installation instructions, and data sheets.

## INSTALLATION

### Install tackboards in accordance with manufacturer's instructions, parallel to floor with uniform vertical surface plumb and level, to provide rigid, secure surface.

### Mechanical attachment:

#### To concrete or solid masonry use lag screw and expansion bolts or screws and fibre plugs as appropriate for stresses involved.

#### To hollow masonry use toggle bolts or equivalent.

#### To wood or sheet metal use screws. Secure into framing members in stud walls.

## CLEANING

### Perform cleaning after installation to remove construction and accumulated environmental dirt.

### Clean surfaces after installation using manufacturer's recommended cleaning procedures.

### Clean aluminum with damp rag and approved non-abrasive cleaner.

### Upon completion of installation, remove surplus materials, rubbish, tools and equipment barriers.

END OF SECTION