# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

## REFERENCES

### Aluminum Association (AA)

#### AAI DAF45, Designation System for Aluminum Finishes.

### Canadian General Standards Board (CGSB)

#### CGSB 41-GP-6M, Sheets, Thermosetting Polyester Plastics, Glass Fibre Reinforced.

### Canadian Standards Association (CSA)

#### CSA W47.2, Certification of Companies for Fusion Welding of Aluminum.

#### CSA W59.2, Welded Aluminum Construction.

### The Master Painters Institute (MPI)

#### Architectural Painting Specification Manual.

## SUBMITTALS

### Submit representative sample of each type of sign, sign image and mounting method, including, but not limited to graphic, cast letters, sign box installation method, channel letters and wall plates fixed mounting installation method.

### Indicate materials, thicknesses, sizes, finishes, colours, construction details, removable and interchangeable components, mounting methods, schedule of signs.

### Submit drawn-to-scale details for individually fabricated or incised lettering indicating word and letter spacing.

### Submit representative sample of each type sign, sign image and mounting method.

### Submit manufacturer’s printed product literature panel signage or components, specifications and datasheet and include product characteristics, performance criteria, physical size, finish and limitations.

### Submit manufacturer’s installation instructions and special handling criteria, installation sequence and cleaning procedures.

## MAINTENANCE DATA

### Provide maintenance data for illuminated signs for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

## Quality assurance

### Welding Certification in accordance with CSA W47.2.

# PRODUCTS

## MATERIALS

### Aluminum extrusions: to AA 6063-T5 or AA 6006-T5.

### Sheet aluminum: utility quality.

### Prefinished sheet aluminum: plain utility sheet with manufacturer applied baked enamel finish 0.25 mm thick on face and 0.0076 mm thick on back.

### Casting aluminum: CSA HA Series - HA.9-SG7ON-T6.

### Acrylic sheet: polymethylmethacrylate (PMMA) cast sheet suitable for intended use in sign fabrication, colours as indicated.

### Engraving sheet: lamicoid 3.2 mm thick plastic sheet, white core.

### Self-stick foam tape: 1.6 mm thick, 352.4 kg/m3 density polyurethane open-cell foam tape for sign purposes, with synthetic self-stick adhesive on both sides. Width:  to suit sign sizes.

### Adhesives, paints, sealants and solvents for acrylic sheet: type recommended by sheet manufacturer for applicable condition.

### Acrylic top-coat: clear, non-yellowing, exterior grade, satin finish, acrylic polyester resin protective coating, compatible with acrylic surface of type recommended by sheet manufacturer.

### Bituminous paint: to MPI, EXT 5.4D.

## SIGN GRAPHICS

### Sign graphics to be well defined, arranged for balanced appearance, and properly word and letter spaced.

### Cut and spray process: mask surfaces, accurately cut-out image, then spray apply uniform coating to obtain opaque finish.

### Silk screen process: apply multi colour photographic produced silk screen printed images to back side of transparent sign faces; face side of opaque sign faces.

### Engraving: apply sign images using pantograph mechanical engraving machine to obtain incised letters as detailed or specified.

### Self-stick vinyl film: individual letters and numerals and symbols die cut from 0.1 mm thick black integral colour, matte finish, exterior grade PVC film, with self-stick adhesive backing.

### Decals: silk screened or printed images on 0.038 mm, clear matte finish, mylar film, with self-stick adhesive backing. Protect image with laminated film overlay of same material as decal base.

## CUT-OUT LETTERS

### Cut letters and symbols from coloured acrylic.

### Helvetica typeface, upper and lower case; sizes and thicknesses as indicated. Make corners square cut.

## WALL PLATES

### Plastic wall plates:

#### Fabricate from colour acrylic sheet 3.2 mm. Sizes as indicated.

#### Sign graphics: apply by engraving.

### Metal wall plates:

#### Fabricate from sheet aluminum sign plates, minimum 3.2 mm thick, with colour anodized finish. Sizes as indicated.

#### Sign graphics: apply by engraving.

### Cast Aluminum Letters: (exterior):

#### Supply and install cast aluminum letters 250 mm high in upper case Helvetica Bold. Lettering to read “name of Building”, Finish color to be as selected by Owner.

### Interchangeable mounting: supply wall plates with approved type, semi-concealed, retaining holders that permit quick but vandal-resistant interchange of sign face. No exposed fasteners permitted. Exposed portions to match sign face.

### Fixed mounting: prepare wall plates for fixing by surface fasteners with rosette covers.  Include back-up plates for fixing to uneven surfaces where required.

### Bracket mounting: fabricate brackets for wall projecting or ceiling suspended sign plates as detailed: of clear acrylic 4.8 mm thick.

## DOOR PLATES

### Fabricate sign faces of color acrylic sheet.  Sizes as indicated.

### Sign graphics: apply by engraving, with 25 mm high letters. Signs to be mounted on outside of doors.

### Interchangeable mounting: supply door plates with approved type, semi-concealed, retaining holders that permit quick but vandal-resistant interchange of sign face. No exposed fasteners permitted. Exposed portions to match sign face.

### Fixed mounting: use self-stick foam tape.

### Mounting on transparent surfaces: use self-stick foam tape. Include blank back-up plate for opposite side.

### Washroom pictographs: cut-out figures without backgrounds.

## NUMBER PLATES

### Fabricate number plates for doors of engraving sheet. Size as indicated.

### Engrave 9.5 mm high, single line numerals incised to expose contrasting coloured core.

## GENERAL FABRICATION REQUIREMENTS

### Fabricate signs in accordance with details, specifications and shop drawings.

### Build units square, true, accurate to size, free from visual or performance defects.

### Accurately fit and securely join sections to obtain tight, closed joints.

### Allow for thermal movement without distortion of components.

### Exposed fasteners permitted only where indicated or approved by Owner and to be inconspicuous and same finish and colour as base material, or as noted.

### Polish exposed edges of plastic and metal to smooth, slightly convex profile.

### Apply bituminous paint to aluminum in contact with dissimilar metals, concrete or masonry.

### Manufacturer's nameplates on sign surface locations visible in completed work not acceptable.

# EXECUTION

## INSTALLATION

### Erect and secure signs plumb and level at elevations indicated.

### Comply with sign manufacturer's installation instructions and approved shop drawings.

### Mechanical attachment:

#### To concrete or solid masonry use lag screws and expansion bolts or screws and fibre plugs, as appropriate for stresses involved.

#### To hollow masonry use toggle bolts or equivalent.

#### To steel use bolts with nut and lock washers, self-tapping screws, welding, as appropriate for stresses and metal thicknesses.

#### To wood use screws.

#### Secure into framing members behind stud walls or above ceilings.

#### Mechanical fasteners on exterior to be non-staining, non-ferrous type.

#### Fabricate special fasteners as required for installation conditions.

#### Mechanical fasteners and methods of attachment subject to Owner’s approval. Obtain Owner’s approval before fixing to structural steel.

### Adhesive attachment:

#### Use self-stick adhesive foam tape to manufacturer's instructions to adequately fix sign and prevent "rocking". Keep tape maximum 1.6 mm from edges.

## CLEANING

### Leave signs clean. Remove debris from interior of sign boxes.

### Touch up any damaged finishes.

## Commissioning

### Instruct Owner on care and cleaning.

END OF SECTION