# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 61 00 - Common Product Requirements.

### Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 05 50 00 - Metal Fabrications.

### Section 10 28 10 - Toilet and Bath Accessories.

## REFERENCES

### American Society for Testing and Materials (ASTM)

#### ASTM A480/480M, Standard Specification for General Requirements for Flat-Rolled Stainless and Heat-Resisting, Sheet, and Strip.

### Canadian General Standards Board (CGSB)

#### CAN/GCSB - 71.20, Adhesive, Contact, Brushable.

### Canadian Standards Association (CSA)

#### CSA-B651, Accessible Design for the Built Environment.

## SUBMITALS

### Indicate fabrication details, plans, elevations, hardware, and installation details.

### Submit duplicate 300 x 300 mm samples of panel showing finish on both sides, two finished edges and core construction.

### Submit duplicate representative samples of each hardware item, including brackets, fastenings and trim.

## CLOSEOUT SUBMITTALS

### Provide maintenance data for plastic laminate for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

## STORAGE AND PROTECTION

### Deliver, store, handle and protect materials in accordance with Section 01 61 00 - Common Product Requirements.

### Protect finished laminated plastic surfaces during shipment and installation. Do not remove until immediately prior to final inspection.

# PRODUCTS

## MATERIALS

### Laminated plastic toilet partitions to CAN3-A172 self-supporting, 19 mm thick with solid color finish on both sides.

### Core material: particle board to CAN3 0188.1, sanded both faces, 15.8 mm thick.

### Laminated plastic adhesive: to CAN/CGSB 71-20.

### Stainless steel sheet metal: to ASTM A480/480M, Type 304 with brushed finish.

### Sealer: water resistant sealer or glue as recommended by laminate manufacturer.

### Headrails: 57 mm x 57 mm clear anodized, extruded aluminum, anti grip design.

### Pilaster: solid laminate plastic panels 19 mm thick to sizes indicated.

### Attachment: stainless steel tamper proof type screws and bolts.

## COMPONENTS

### Hinges:

#### Heavy duty, non-lubricating, nylon bushings.

#### Material/finish: chrome plated non-ferrous casting.

#### Swing: inward and outward.

#### Return movement: gravity.

#### Adjustable to hold door open at any angle up to 90°.

#### Emergency access feature.

### Latch set: surface mounted, combination latch, door-stop, keeper and bumper, chrome plated non-ferrous with emergency access feature.

### Wall and connecting brackets: chrome plated non-ferrous extrusion or casting.

### Coat hook: combination hook and rubber door bumper, chrome plated non-ferrous.

### Door pull: Barrier-free type suited for outswinging doors, chrome plated non-ferrous.

## FABRICATION

### Doors, panels and screens: 19 mm thick, composite plastic laminate panels, to sizes indicated.

### Pilasters: 19 mm thick, constructed same as door, to sizes indicated

### Laminate plastic to core material ensuring core and laminate profiles coincide to provide continuous support and bond over entire surface.

### Finish edges of composite laminated plastic panels with laminated plastic strip. Chamfer exposed edges uniformly at approximately 20°.

### Provide formed and closed edges for doors, panels and pilasters. Miter and weld corners and grind smooth.

### Provide internal reinforcement at areas of attached hardware and fittings. Temporarily mark location of reinforcement for grab bars and benches.

# EXECUTION

## INSTALLATION

### Ensure supplementary anchorage, if required, is in place.

### Do work in accordance withCSA-B651.

## ERECTION

### Partition erection.

#### Install partitions secure, plumb and square.

#### Leave 12 mm space between wall and panel or end pilaster.

#### Anchor mounting brackets to masonry or concrete surfaces using screws and shields: to hollow walls using bolts and toggle type anchors.

#### Attach panel and pilaster to brackets with through type sleeve bolt and nut.

#### Provide for adjustment of floor variations with screw jack through steel saddles made integral with pilaster. Conceal floor fixings with stainless steel shoes.

#### Provide templates for locating threaded studs through finished ceilings.

#### Equip each door with hinges, latch set, and each stall with coat hook mounted on door, mounting heights 1550 mm. Adjust and align hardware for proper function. Set door open position at 30° to front. Install door bumper, door mounted.

#### Equip outswinging doors with door pulls on outside of door in accordance with CSA-B651, Accessible Design for the Built Environment.

#### Install misc. hardware and grab bars.

### Floor supported and overhead braced partition erection.

#### Attach pilasters to floor with pilaster supports and level, plumb, and tighten installation with levelling device.

#### Secure pilaster shoes in position.

#### Secure headrail to pilaster face with not less than two fasteners per face.

#### Set tops of doors parallel with overhead brace when doors are in closed position.

### Screen erection.

#### Provide urinal stall screens consisting of panel, pilaster and headrail as indicated.

#### Anchor screen panels to walls with 3 panel brackets and pilaster complete with floor shoes, anchored to floor.

## ADJUSTING

### Adjust doors and locks for optimum, smooth operating condition.

### Lubricate hardware and other moving parts.

## CLEANING

### Perform cleaning after installation to remove construction and accumulated environmental dirt.

### Clean surfaces after installation using manufacturer's recommended cleaning procedures.

### Clean aluminum with damp rag and approved non-abrasive cleaner.

### Clean and polish hardware and stainless components.

### Upon completion of installation, remove surplus materials, rubbish, tools and equipment barriers.

END OF SECTION