# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 05 50 00 - Metal Fabrications.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

### Section 06 20 00 - Finish Carpentry.

## REFERENCES

### American Society for Testing and Materials (ASTM)

#### ASTM E90, Standard Test Method for Laboratory Measurement of Airborne-Sound Transmission Loss of Building Partitions and Elements.

#### ASTM-E336, Standard Method for Measurement of Airborne Sound Insulation in Buildings.

### Underwriters Laboratories of Canada (ULC)

#### CAN/ULC-S102.2, Method of Test for Surface Burning Characteristics of Flooring, Floor Coverings, and Miscellaneous Materials and Assemblies.

## DESIGN REQUIREMENTS

### Design and fabricate accordion folding partitions with minimum STC of 50 tested to ASTM E90.

### Use vinyl fabric for covering with maximum:

#### flame spread: 25

#### fuel contributed: 35

#### smoke developed: 50, when tested to CAN/ULC-S102.2.

## SUBMITTALS

### Indicate head and jamb conditions, opening sizes, anchorage clearances, hardware, finish pattern and colour.

### Submit duplicate 300 x 200 mm samples of vinyl fabric covering for each selected folding partition cover.

### Submit test reports indicating compliance with design criteria regarding sound transmission and fire hazard classification.

## CLOSEOUT SUBMITTALS

### Provide operation and maintenance data for accordion folding partitions for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

# PRODUCTS

## MATERIALS

### Accordion folding partitions.

### Finish: heavy-duty vinyl with woven fiber backing. Vinyl to have a Class “A” flame spread rating to ASTM E-84.

### Frame: arrange steel members to provide vertical or horizontal pantograph movement as standard with manufacturer.

## COMPONENTS

### Suspension system.

#### Provide steel track and trolleys designed to support weight of partition for surface installation.

#### Provide threaded steel rods and nuts type hangers and stabilizers.

### Hardware.

#### Pull bar, draw latches, screws and installation hardware: manufacturer's standard. Hardware finish selected from manufacturer's standard finishes.

#### Install keyed latch to accept master keyed cylinder.

#### Provide pendant pull.

## ACCESSORIES

### Sweeps: vinyl strips at head to conceal track.

### Sound seals: vinyl or rubber gaskets at jambs. Double sweep-strips at top and bottom.

### Air release: provide a series of 10 mm holes in lead post moulding to assist release of air trapped with partition during operation.

### Ceiling guard: aluminum or integral track and ceiling guard.

### Provide pivot switches where indicated.

# EXECUTION

## INSTALLATION

### Level tracks and fasten securely to header.

### Install partition in accordance with manufacturer's printed instructions.

### Touch up damaged finishes, repair damage to partitions to match original finish.

### Clean folding partition system and protect from damage.

### Adjust and leave partitions in smooth operating conditions.

## COMMISSIONING

### Train user staff in care, cleaning and operation of accordion folding partition.

### Field Test assembly for flanking noise.

### Provide field sound performance report as requested by Owner.

END OF SECTION