# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 05 50 00 - Metal Fabrications.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

### Section 06 20 00 - Finish Carpentry.

## REFERENCES

### American Society for Testing and Materials (ASTM)

#### ASTM E90, Standard Test Method for Laboratory Measurement of Airborne-Sound Transmission Loss of Building Partitions and Elements.

#### ASTM E336, Standard Method for Measurement of Airborne Sound Insulation in Buildings.

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-11.3, Hardboard.

### Canadian Standards Association (CSA)

#### CSA 0115, Hardwood and Decorative Plywood.

#### CSA 0151, Canadian Softwood Plywood.

### Underwriters Laboratories of Canada (ULC)

#### CAN/ULC-S102, Surface Burning Characteristics of Building Materials and Assemblies.

## DESIGN REQUIREMENTS

### Design and fabricate folding partitions with minimum STC of 50 tested to ASTM E90.

### Use vinyl fabric for covering with maximum:

#### flame spread: 25;

#### fuel contributed: 35;

#### smoke developed: 50, when tested to CAN/ULC-S102.

## SUBMITTALS

### Indicate installation requirements including dimensions, head and jamb conditions, track layout, stacking arrangement, switching, hardware, finish and colour, operating mechanism, and location.

### Submit duplicate 300 x 300 mm samples of partition finish for each colour selected.

### Submit test data indicating compliance with design criteria regarding sound transmission and fire hazard classification.

## CLOSEOUT SUBMITTALS

### Provide operation and maintenance data for folding partitions, hardware for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

# PRODUCTS

## MATERIALS

### Panel core: steel skin and acoustical insulation core with manufacturer’s standard fabrication.

### Panel finish: reinforced vinyl, pressure bonded to steel skin.

## COMPONENTS

### Overhead suspension system.

#### Track: manufacturer's standard cold rolled steel channel housing designed to support partitions.

##### Equip track with separate brackets for hanger attachment.

##### Provide threaded steel rods and nuts type hangers and stabilizers.

#### Trolley: steel wheels with ball bearings, equipped with thrust bearing and steel pendant bolt at each wheel assembly for height adjustment.

### Hardware.

#### Equip partition with manufacturer's standard hardware. Hardware finish selected from manufacturer's standard finishes.

#### Install keyed latch to accept master keyed cylinder.

### Sound seals.

#### Provide fixed sound seals to manufacturer's standard.

#### Use head and floor fixed sweep strip type floor and head seals.

#### Design retractable seals to secure panel in position.

#### Use manufacturer's standard astragal inserts for jamb and panel joint seal.

## ACCESSORIES

### Provide manufacturer's standard closure panel, with lever operator.

# EXECUTION

## INSTALLATION

### Secure and level track.

### Install folding partitions in accordance with manufacturer's printed instructions.

### Touch up damaged finishes, repair damage to partitions to match original finish.

### Clean folding partition system and protect from damage.

### Adjust and leave partitions in smooth operating condition.

## SITE TESTS

### Acoustic field testing: have field sound performance certified by an independent acoustical consultant in accordance with ASTM E336.

## COMMISSIONING

### Train user staff in care, cleaning and operation of folding panel partitions.

### Field test sound performance of assembly of reports as requested by Owner.

END OF SECTION