# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

### Section 08 80 00 - Glazing.

## REFERENCES

### American Society for Testing and Materials (ASTM)

#### ASTM  A167, Standard Specification for Stainless and Heat-Resisting Chromium-Nickel Steel Plate, Sheet and Strip.

#### ASTM B456, Standard Specification for Electrodeposited Coatings of Copper Plus Nickel Plus Chromium and Nickel Plus Chromium.

#### ASTM A653/A653M Standard Specification for Steel Sheet, Zinc-coated (Galvanized) or Zinc-Iron Alloy Coated (Galvannealed) by the Hot-dip Process.

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-12.5, Mirrors, Silvered.

### Canadian Standards Association (CSA)

#### CAN/CSA-B651, Barrier-Free Design.

## SUBMITTALS

### Indicate size and description of components, base material, surface finish inside and out, hardware and locks, attachment devices, description of rough-in-frame, building-in details of anchors for grab bars.

### Samples to be returned for inclusion into work.

## CLOSEOUT SUBMITTALS

### Provide maintenance data for toilet and bath accessories for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

# PRODUCTS

## MATERIALS

### Sheet steel: commercial quality to ASTM A653/A653M with ZF001 designation zinc coating.

### Stainless steel sheet metal: to ASTM A167, Type 304 with BA finish.

### Stainless steel tubing: Type 304, commercial grade, seamless welded, 1.2 mm wall thickness.

### Fasteners: concealed screws and bolts hot dip galvanized, exposed fasteners to match face of unit. Expansion shields fibre, lead or rubber as recommended by accessory manufacturer for component and its intended use.

## COMPONENTS

### Toilet tissue dispenser: single roll type, surface mounted, chrome plated steel frame, capacity of 500 sheets double ply roll, roll under spring tension for controlled delivery.

### Paper towel dispenser: for double fold paper towels, 525 sheet capacity stainless steel cabinet, hinged front panel, lock and key, surface mounted.

### Combination towel dispenser/waste receptacle: recessed wall unit, approximately 330 mm wide, 1400 mm high, 92 mm deep. Interior of 0.8 mm galvanized steel, exterior of 0.8 mm stainless steel. Suitable for dispensing folded paper towels. Removable rigid molded plastic waste receptacle, lockable access door with continuous full height stainless steel hinge.

### Soap dispenser: liquid pushup-type corrosion-resistant black ABS valve with stainless steel spring, translucent polyethylene 1.0 L capacity tank, vandal-resistant chrome plated ABS bracket and collar, surface mounted.

### Feminine napkin/tampon dispenser:  stainless steel, surface mounted unit, minimum capacity is napkins and 20 tampons, key locked, continuous hinge front panel.

### Hand dryer:  listed under re-examination service of ULC and CSA approved:

#### Mounting:  surface

#### Wall box:  1.4 mm steel

#### Cover:  white enamel.

#### Motor:  universal type, 1/10 HP, 7500 RPM, resilient mounting, sealed, lubricated bearings, fuse protected, 120 V, 15 A.

#### Fan:  double inlet centrifugal type, dynamically balanced, directly mounted on motor shaft, 57 l/s.

#### Heating element:  protected by an automatic, resetting circuit breaker, isolated from nozzle.

#### Electronic dryer:  power controlled by in admitting, receiving electronic control device positioned to dryer as when hands are placed under nozzle.  Operation to continue for no more than seconds of continued use.

#### Nozzle:  stainless steel, fixed.

### Recessed soap holder:  recessed, stainless steel, 158 x 158 mm soap tray, extended lip and steel back plate.

### Feminine napkin disposal bin:   disposal bin: stainless steel surface mounted unit, continuous hinged door, self closing, embossed with "napkin disposal".

### Shower curtain: anti-bacterial fire resistive self extinguishing vinyl laminated fabric shower curtain. Provide curtain hold-back hook and chain at each curtain.

### Shower rods: 25 mm dia x 1.2 mm wall thickness stainless steel tubing of required length with satin chrome finished flanges, 12 shower curtain hooks and curtain hold-back hook and chain. Shower rod material and anchorage to withstand downward pull of 0.9 kN.

### Shower/Dressing Area Seat: 8 mm thick water resistant, ivory color, solid phenolic.  Frame and mounting brackets 304 stainless steel with self-locking mechanism.  Size 455 mm wide and projects from wall 400 mm. Mounting height 430 mm from top of seat to floor.

### Grab bars: 32 mm dia x 1.2 mm wall tubing of stainless steel, 38 mm diameter wall flanges, concealed screw attachment, flanges welded to tubular bar, provided with steel back plates and all accessories. Knurl/peened bar at area of hand grips. Grab bar material and anchorage to withstand downward pull of 2.2 kN.

### Robe hook:  stainless steel with 50 mm projection.

### Medicine cabinet: swing door cabinet, surface mounted, glass adjustable shelves, toothbrush holder, mirror. Cabinet completely reversible.

#### Size: 355 x 460 x 90 mm.

#### Cabinet: 0.5 mm thick steel.

#### Mirror: plate glass, 6mm to CAN/CGSB-12.5, stainless steel frame.

#### Hinges: 1mm stainless steel piano type, with 105° internal stop.

#### Latch: magnetic

#### Shelves: 5.0 mm glass, rolled edges.

### Hat and Coat Hook: Stainless steel with 50 mm projections.

### Mirror: Plate glass 4.0 mm to CAN/CGSB-12.5, Stainless steel frame, electrolytically copper plated and guaranteed against silver spoilage for 10 years, concealed fasteners for mounting.

### Diaper changing station: surface mounted, wall unit, polyethylene insert, moulded-in steel-on-steel hinge assembly, mounded-in integral support mechanism, minimum 864 mm wide x 533 mm high, liner dispenser, safety belt, safety instructions, graphic illustration, labeled with universally accepted symbol.

### Watercloset backrest: 13 mm solid core plastic laminate backrest, measuring 102 x 254 mm, with chamfered edges and rounded edges, mounted to 32 mm diameter Type 304 stainless steel tubing. Concealed vandal-resistant mounting roses for concealed flange installation. Supplied with stainless steel mounting screws.

## FABRICATION

### Weld and grind joints of fabricated components flush and smooth. Use mechanical fasteners only where approved.

### Wherever possible form exposed surfaces from one sheet of stock, free of joints.

### Brake form sheet metal work with 1.5 mm radius bends.

### Form surfaces flat without distortion. Maintain flat surfaces without scratches or dents.

### Back paint components where contact is made with building finishes to prevent electrolysis.

### Hot dip galvanize concealed ferrous metal anchors and fastening devices to CSA G164.

### Shop assemble components and package complete with anchors and fittings.

### Deliver inserts and rough-in frames to job site at appropriate time for building-in. Provide templates, details and instructions for building in anchors and inserts.

### Provide steel anchor plates and components for installation on studding and building framing.

## FINISHES

### Chrome and nickel plating: to ASTM B456, satin or polished finish.

### Manufacturers brand names on face of units not acceptable.

# EXECUTION

## INSTALLATION

### Install and secure accessories rigidly in place as follows:

#### Stud walls: install steel back-plate to stud prior to plaster or drywall finish. Provide plate with threaded studs or plugs.

#### Hollow masonry units or existing plaster/drywall: use toggle bolts drilled into cell/wall cavity.

#### Solid masonry or concrete: use bolt with lead expansion sleeve set into drilled hole.

#### Toilet/shower compartments: use male/female through bolts.

### Install grab bars on built-in anchors provided by bar manufacturer.

### Use tamper proof screws/bolts for fasteners.

### Install mirrors in accordance with Section 08 80 00 - Glazing.

## TESTING

### Proof test grab bars to manufacturers specifications.

### Provide certificate of test results.

## SCHEDULE

### Locate accessories where indicated. Exact locations determined by Owner.

### Toilet tissue dispenser: one in each toilet compartment.

### Paper towel dispenser: one in each washroom.

### Combination towel dispenser/waste receptacles: one in each public washroom where indicated.

### Soap dispenser: one at each single wash basin and.

### Feminine napkin/tampon dispenser:  one in each female washroom.

### Hand dryer:  two in each washroom.

### Recessed soap holder:  one at each bathtub and shower.

### Feminine napkin disposal bin: one in each female toilet compartment.

### Shower rod and curtain: one at each bathtub with shower head and one at each shower compartment.

### Grab bar: two in each handicapped toilet compartment and one in each bathtub enclosure.

### Robe hook: one in each shower stall or bathtub.

### Medicine cabinets: where indicated

### Hat & Coat Hook: one in each male and female toilet compartment.

### Diaper changing station: one in each unisex washroom.

### Watercloset backrest: one at each tankless watercloset. Coordinate location and installation with mechanical and location of watercloset flush valve.

## commissioning

### Instruct Owner on cleaning and maintenance.

END OF SECTION