# General

## Related Sections

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

## References

### American National Standards Institute (ANSI)

#### ANSI/NFPA 10, Portable Fire Extinguishers.

### Underwriters' Laboratories of Canada (ULC)

#### CAN/ULC-S508, Rating and Fire Testing of Fire Extinguishers and Class "D" Extinguishing Media.

## SUBMITALS

### Submit manufacturer’s technical data for each type of fire extinguisher and safety blanket.

## Closeout Submittals

### Provide maintenance data for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

## Waste Management and Disposal

### Separate and recycle waste materials in accordance with municipal regulations.

# Products

## Water Pump Tank Extinguishers

### Stored water tank type, manual pump and handle with discharge hose and nozzle, stainless steel tank construction, ULC labelled for A class protection. 9.1 L size.

## Water Pressurized Extinguishers

### Stored pressure type, squeeze-grip operated, of stainless steel construction, ULC labelled for A class protection. 9.1 L size.

## Multi-Purpose Dry Chemical Extinguishers

### Stored pressure rechargeable type with hose and shut-off nozzle, ULC labelled for A, B and C class protection. Sizes 9 and 14 kg or as indicated on drawings.

## CARBON DIOXIDE

### Extinguishers insulated handle, hose and horn discharge assembly, self-closing lever or squeeze-grip operation, fully charged, ULC labelled for B and C class protection. Sizes 4.5, 6.8 and 9.0 kg or as indicated on drawings.

## Dry Chemical Extinguishers (Class D)

### Stored pressure rechargeable type with hose and shut-off nozzle, ULC labelled for D class protection. Size 13.6 kg.

## Extinguisher Brackets

### Type recommended by extinguisher manufacturer.

## Cabinets

### Flush, surface or semi-recessed type as indicated, constructed of 1.6 mm thick steel, 180o opening door of 2.5 mm thick steel with latching device.

### Cabinet to maintain fire resistive rating of construction in which they occur.

### Cabinet door: with 5.0 mm thick full clear safety glass panel.

### Finish:

#### Tub: prime coated with finish painted with a hand-baked matte black enamel.

#### Door and frame: No.4 satin finish 304 stainless steel.

## Identification

### Identify extinguishers in accordance with recommendations of ANSI/NFPA 10 and CAN/ULC-S508.

### Attach bilingual tag or label to extinguishers, indicating month and year of installation. Provide space for service dates.

## Fire Safety Blankets

### 1800 x 1800 mm of silicone coated fibre glass in metal container.  Metal container to be marked Fire Safety Blankets.

# Execution

## Installation

### Install or mount extinguishers in cabinets or on brackets as indicated.

### Install fire safety blankets as indicated.

END OF SECTION