# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 06 10 53 – Miscellaneous Rough Carpentry.

## REFERENCES

### Canadian General Standards Board (CGSB)

#### CAN/CGSB-44.40, Steel Clothing Locker.

## SUBMITTALS

### Indicate type and class of locker, thicknesses of metal, fabricating and assembly methods, tops, rods, hooks, shelves, bases, trim, numbering, filler panels, end/back panels, doors, handles, ventilation method, finishes.

### Submit duplicate 50 x 50 mm samples of colour and finish on actual base metal.

# PRODUCTS

## MANUFACTURED UNITS

### Lockers: to CAN/CGSB-44.40, Type 1-Single full-height locker, Type 2 - Double tier locker

#### Material Sizes: hinges 2.0 mm, frame 1.6 mm, door 1.0 mm, top 0.85 mm, top and sides 0.70 mm. Width, height and depth dimensions as indicated on drawings.

#### Assembly types: knock down construction for onsite assembly using pop rivet fastening.

#### Top: flat where bulkheads or ventilation chase spaces are installed, sloped elsewhere. Provide perforated tops for ventilation into bulkhead where required.

#### Doors: one-piece double-wall envelope construction door, door swing out.

#### Door handle: recessed handle steel with bright chromium finish.

#### Finish ends where lockers are exposed to match fronts.

#### Base: steel.

## ACCESSORIES

### Locking system: padlocks supplied by others.

### Unobstructed ventilation through two sets of louvers.

### Options: To CAN/CGSB-44.40, steel end panels, (where locker ends are exposed) number pates, manufacturer’s standards, coat hooks-metal chromium finish, one book shelf per locker, width equal to locker width, depth to be 16 mm short of locker depth, two (2) per double locker, one (1) per single wide locker, single and double lockers as per drawings.

# EXECUTION

## INSTALLATION

### Assemble and install lockers in accordance with manufacturer's written instructions.

### Securely fasten lockers to grounds and nailing strips.

### Install finished end panels to exposed ends of locker banks.

### Install locker numbers

### Install coat hooks at heights as required for following users (Primary, Elementary, Junior and Senior High.)

#### Primary: 1040 mm

#### Elementary:  1219 mm

#### Junior High:  1370 mm

#### Senior High:  1395 mm

## LOCATION

### Location and layout as per plans.

## ADJUSTING

### Adjust metal lockers for correct function and operation in accordance with manufacturer’s written instructions.

### Lubricate moving parts to operate smoothly and fit accurately.

END OF SECTION