# GENERAL

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

## REFERENCES

### National Fire Protection Association (NFPA):

#### NFPA – Flammable and combustible Liquids code.

### Underwriters Limited of Canada (ULC).

## SUBMITTALS

### Indicate cabinet type, thickness of metal, finishes, anchoring and support systems.

### Submit manufacturer’s printed product literature, specifications and data sheet.

### Submit manufacturer’s installation instructions.

# PRODUCTS

## FLAMABLE AND COMBUSTIBLE LIQUID STOAGE CABINET

### Cabinet to meet requirements of NFPA 30 and be ULC approved.

### Cabinet to be provided with grounding wire connections.

### Cabinet to be constructed of 1.2 mm steel, double wall construction, with 50 mm thick fire proof insulating metal sandwiched between inner and outer walls.

### Door sill to be raised 50 mm above bottom of cabinet to form liquid tight joint.

### Cabinet to be supplied with four (4) adjustable leveling feet.

### Cabinet to be double door style with three (3) point lock on door.

### Cabinet to be provided with NPS 2 threaded vents one on each side at top and bottom of cabinet to enable continuous cabinet ventilation.  Each vent to be covered internally with a fire baffle.

### Cabinet to be supplied complete with adjustable satin coat galvanized shelves to permit storing of various sizes of containers.

### Cabinet to be painted with yellow safety enamel with red letters, warning: “Flammable –KEEP FIRE AWAY” in English and French.

### Cabinet to be individually cartoned.

### Capacity and dimensions: as indicated.

## ACid/corrosive storage cabinet

### Cabinets to be ULC approved.

### Cabinet to be constructed of 1.2 mm steel, double wall construction with 40 mm air space.

### Door sill to be raised 50 mm above bottom of cabinet to form liquid tight joint.

### Cabinet to be supplied with four (4) adjustable leveling feet.

### Cabinet to be double door style with three (3) point lock on door.

### Cabinet to be provided with NPS 2 threaded vents, one on each side at top and bottom of cabinet to enable continuous cabinet ventilation.  Each vent to be covered internally with a fire baffle.

### Cabinet to be provided with grounding wire connections.

### Cabinet to be supplied complete with adjustable galvanized shelves fitted with removable chemically inert high-density polyethylene spill-catcher trays.

### Cabinet floor to be fitted with removable spill catcher tray assembly as specified above.

### Cabinet to be painted with corrosive-resistant blue enamel epoxy and have white letters, warning:  “CAUTION – CORROSIVES”, in English and French.

### Cabinet to be individually cartoned.

### Capacity and dimensions: as indicated.

# EXECUTION

## general

### Supply and install type and quantities as indicated.

## Commissioning

### Instruct Owner in operation, adjustments, cleaning and maintenance.

END OF SECTION