# GENERAL

## SCOPE

### Supply and install microwave, washer, dryer, refrigerator range and compact kitchen unit as shown on the drawings and specified herein.

## RELATED SECTIONS

### Section 01 61 00 – Common Product Requirements.

## SUBMITTALS

### Submit manufacturer’s printed product literature, specifications and data sheet.

## DELIVERY, STORAGE AND HANDLING

### Deliver handle, store and protect equipment in accordance with Section 01 61 00 - Common Product Requirements.

### Deliver equipment only after interior finishes are complete.

## WARRANTY

### Provide manufacturers standard warranty for all appliances listed.

# PRODUCTS

## APPLIANCES

### Refrigerator: 17.7 cu. ft. with 5.0 cu. ft. freezer, frost free, two door, 3 glass shelves, 2 crisper drawers with glass cover, 1 meat compartment, covered dairy compartment, ice maker kit, 4 adjustable door bins, white finish.  Size approximately 760 x 760 x 1676 mm high.

### Upright freezer:  16.7 cu. ft with 230 kg. storage capacity, 2 lower baskets, 4 full width wire shelves, 6 door shelves, interior light, frost free, white finish, approximate dimensions:  760 x 760 x 1690 mm high.

### Range: standard clean oven, oven light, oven window, bottom storage drawer, easy lift off oven door, appliance outlet, broil element and broil pan, 2 flat rocks, electronic delay/cook/off timer, white finish with block console.  Size approximately 760 x 650 x 1200 mm high.

### Built-in wall oven:  self-cleaning, dual radiant system. Six pass elements, convection baking system, interior oven light, porcelain broiler pan. 3 oven racks, convection roasting rack, electronic oven control, electronic clock, electronic temperature display, automatic oven (delay cook, off) ,child resistant lockout, automatic oven shut-off, automatic set, F o  or C o  programmable, integrated oven pad (touch pad), reversible side swing oven door with see through window , 240/208 volts white finish.

### Electric Cooktop:  brushed chrome cooktop, multi-warp coil (2-200 mm, 1-150 mm) lift up cooktop with support rod, chrome dip bowls and spill control top, 240/208 volts, 22.3/19.2 amps @ 240/208 volts armored electrical cable, colour chrome.

### Chest Freeze: 12.2 cu. ft. with adjustable temperature control, heavy duty storage baskets, interior light, handle with lock.  Size approximately 1200 x 1200 x 600 x 900 mm high.

### Under Counter Refrigerator: 4.2 cu. ft. with manual defrost, reversible door, 3 slide out plastic coated wire shelves, full width freezer compartment, door shelves, white finish and molded work top.  Size approximately 500 x 500 x 800 mm high.

### Microwave: 1.3 cu. ft, 1000 watts, recessed turntable system, 3 quick sensor categories, 2 sensor reheat categories, 3 auto weight defrost categories, 9 auto sensor cooking categories, 10 power levels , white finish.  Size approximately 500 x 450 x 300 mm high.

### Washer: 2.45 cu. ft capacity, 3 wash/rinse  temperatures, 3 water levels, self cleaning lint filter, ½ h.p. long life motor, 110 volt, white cabinet and console.  Size approximately 5600 x 625 x 1125 mm high.

### Dryer: 5.9 cu .ft. Capacity, side swing door, 3 temperature switch plus timed air, 7 cycle, top mounted filter, 220 volt, white cabinet and console. Size approximately 750 x 600 x 1125 mm high.

### Combination washer/dryer:

#### Dryer features:  side wign door 5.9 cu. Ft. drum capacity, 6 drying cycles and of cycle signal, front-mounted list screen, gentle heat system. 3 temperature settings.

#### Washer features:  2.5 cu. Ft basket capacity, 6 cycles, and gentle wash system. Self-cleaning lint filter, 3 wash/rinse temperature combinations, 2 wash/spin speed combinations, 4 water levels.

#### Dimensions approximately 700 x 820 x 1850 mm high.

#### Colour white.

### Range Hood: 220 cfm with twin blower wheel, light,  variable speed 110 motor, vented to the outside, washable aluminum grease filters, epoxy finished steel hood, color: white on white size approximately 760 x 450 x 150 mm high, ducting with exterior roof or wall cap.

### Compact Kitchen Unit: Integral countertop with cabinet frame manufactured of high pressure laminate bonded to 19 mm exterior grade plywood. Cabinet doors and drawer fronts manufactured of high pressure laminate bonded to 16 mm particle board. 1.3 mm steel sink with acid-resistant porcelain finish, 355 mm W x 476 mm L x 140 mm D, c/w standard 89 mm drain. Acid-resistant porcelain electric cooktop with two (2) burner elements. Refrigerator to be integral part of kitchen unit, c/w one-piece ABS inner liner, ABS door liner, chrome wire shelving, interior light, automatic cold control with 7 settings, 1/10 HP motor compressor. Size of unit approximately 914 mm W x 1016 mm H x 610 mm D.

# EXECUTION

## INSTALLATION

### Install appliances in correct locations as per manufacturer’s instructions and make connections.

### Check appliance to ensure proper operation.

### Appliances having any damage or scratches will not be accepted.

## COMMISSIONING

### Train staff in operation, cleaning and maintenance of domestic equipment provided under this section.

END OF SECTION