# GeneraL

## SUMMARY

### This Section includes requirements for selective demolition and removal of heating, ventilation and air conditioning systems, controls and automated automation components, and related mechanical components and incidentals required to complete work described in this Section.

## RELATED SECTIONS

### Section 01 74 00 – Cleaning.

### Section 01 74 21 – Construction / Demolition Waste Management and Disposal

### Section 23 08 02 – Cleaning and Start-up of Mechanical Piping Systems.

## REFERENCE STANDARDS

### CSA Group (CSA)

#### CSA S350, Code of Practice for Safety in Demolition of Structures.

## DEFINITIONS

### Demolish: Detach items from existing construction and legally dispose of items off site, unless indicated as removed and salvaged, or removed and reinstalled.

### Remove: Planned deconstruction and disassembly of electrical items from existing construction including removal of conduit, junction boxes, cabling and wiring from electrical component to panel taking care not to damage adjacent assemblies designated to remain; legally dispose of items off site, unless indicated as removed and salvaged, or removed and reinstalled.

### Remove and Salvage: Detach items from existing construction and deliver them to Owner ready for reuse.

### Remove and Reinstall: Detach items from existing construction, prepare them for reuse, and reinstall them where indicated.

### Existing to Remain: Existing items of construction that are not removed and that are not otherwise indicated as being removed and salvaged, or removed and reinstalled.

### Hazardous Substances: Dangerous substances, dangerous goods, hazardous commodities and hazardous products may include asbestos, mercury and lead, PCB's, poisons, corrosive agents, flammable substances, radioactive substances, or other material that can endanger human health or wellbeing or environment if handled improperly as defined by the Federal Hazardous Products Act (RSC 1985) including latest amendments.

## ADMINISTRATIVE REQUIREMENTS

### Coordination: Coordinate work of this Section to avoid interference with work by other Sections.

### Account for Owner's continued occupancy requirements during selective demolition and schedule staged occupancy and worksite activities.

## SITE CONDITIONS

### Condition of materials identified as being salvaged or demolished are based on their observed condition on date that tender is accepted.

## SALAVAGE AND DEBRIS MATERIALS

### Demolished items become Contractor's property and will be removed from Project site; except for items indicated as being reused, salvaged, or otherwise indicated to remain Owner’s property.

### Carefully remove materials and items designated for salvage and store in a manner to prevent damage or devaluation of materials

# Products

## MATERIALS

### Use only new materials required for completion or repair matching materials damaged during performance of work of this Section; new materials are required to meet assembly or system characteristics as existing systems indicated to remain and carry CSA approval labels required by the Authority Having Jurisdiction.

### Use listed fire stopping materials compatible with existing fire stopping systems where removal or demolition work affects rated assemblies, restore to match existing fire rated performance.

# Execution

## EXAMINATION

### Visit site, thoroughly examine and become familiar with conditions that may affect the work of this Section before tendering the Bid; Owner will not consider claims for extras for work or materials necessary for proper execution and completion of the contract that could have been determined by a site visit.

### Identify on-site removal of walls and ceiling to facilitate the work.

### Identify on-site testing of ductwork and equipment to facilitate the work.

## PREPARATION

### Protect systems and components indicated to remain in place during selective demolition operations and as follows:

#### Prevent movement and install bracing to prevent settlement or damage of adjacent services and parts of existing buildings scheduled to remain.

#### Notify Owner and cease operations where safety of buildings being demolished, adjacent structures or services appears to be endangered and await additional instructions before resuming demolition work specified in this Section.

#### Prevent debris from blocking drainage inlets.

#### Protect mechanical systems that must remain in operation.

#### Ensure hazardous materials are removed or abated prior to commencing demolition.

#### For components intended for relocation and reuse, remove, store, protect, clean and reinstall and connect to HVAC systems, and recommission.

### Sequence demolition work so that interference with the use of the building by the Owner and users is minimized and as follows:

#### Prevent debris from endangering the safe access to and egress from occupied buildings.

#### Notify Owner and cease operations where safety of occupants appears to be endangered and await additional instructions before resuming demolition work specified in this Section.

## EXECUATION

### Disconnect and cap gas supply and electrical services in accordance with requirements of local Authority Having Jurisdiction.

### Do not disrupt active or energized utilities without approval of the Owner.

### Erect and maintain dust proof and weather tight partitions to prevent the spread of dust and fumes to occupied building areas; remove partitions when complete.

### Demolish parts of existing building to accommodate new construction and remedial work as indicated.

### At end of each work day, leave worksite in safe condition.

### Perform demolition work in a neat and workmanlike manner:

#### Remove any tools or equipment after completion of work, and leave site clean and ready for subsequent renovation work.

#### Repair and restore damages caused as a result of work of this Section to match existing materials and finishes.

### Conduct demolition of HVAC systems in accordance with local Authority Having Jurisdiction (AHT) including the Department of Digital Government and Service NL, Engineering and Inspections Division.

## CLOSEOUT ACTIVITIES

### Arrange for legal disposal and remove demolished materials to accredited provincial landfill site or alternative disposal site (recycle centre).

END OF SECTION