# General

## related WORK

### Do the work in accordance with section 23 05 17 – Pipe Welding and local authority having jurisdiction except where specified otherwise.

### Section 22 07 19 – Plumbing Piping Insulation.

### Section 23 05 29 – Hangers and supports for HVAC Piping and Equipment.

## PRODUCT DATA

### Submit product drawings and product data in accordance with Section 01 33 00 - Submittal Procedures.

### Indicate dimensions, construction details and materials.

# Products

## DIESEL eXHAUST SYSTEM

### Provide exhaust system for new diesel generator.  Exhaust systems shall be complete with all fittings and accessories as required for a complete installation.

### Diesel generator shall be supplied and installed by Electrical Division except as otherwise indicated.  Exhaust silencer and flexible exhaust hose shall be supplied by Electrical Division, and installed by this contractor.  Coordinate installation with Electrical Division and diesel manufacturer.

### Maximum back pressure of the silencer, exhaust flex and piping not to exceed the diesel manufacturer’s recommendations.

### Exhaust piping shall be schedule 80 steel ASTM A53 or A106 c/w butt welded fittings.

# Execution

## Installation

### Install in accordance with manufacturer’s instructions and as specified.

## Diesel Exhaust Systems

### Installation to be in accordance with manufacturer’s recommendations.

### Coordinate exhaust pipe sizes and connection to diesels with Electrical Division.

### Insulate pipe and muffler with type A-2 insulation.

## COMMISSIONING

### After start-up, test and adjust to suit site conditions.

END OF SECTION