# General

## summary

### Section includes:

#### Supply, return and exhaust grilles and registers, diffusers and linear grilles, for commercial and residential use.

## Related Sections

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

## REFERENCES

### American Society of Heating Refrigerating and Air-Conditioning Engineers (ASHRAE).

#### ASHRAE 70, Method of Testing for Rating the Performance of Air Outlets and Inlets.

## system description

### Performance requirements:

#### Catalogued or published ratings for manufactured items: obtained from tests carried out by manufacturer or those ordered by manufacturer from independent testing agency signifying adherence to codes and standards.

## submittals

### Product Data:

#### Submit manufacturer's printed product literature, specifications and datasheet in accordance with Section 01 33 00 - Submittal Procedures. Include product characteristics, performance criteria, and limitations.

##### Submit two copies of Workplace Hazardous Materials Information System (WHMIS) Safety Data Sheets (SDS) in accordance with Section 01 33 00 - Submittal Procedures.

##### Indicate following:

###### Capacity

###### Throw and terminal velocity

###### Noise criteria

###### Pressure drop

###### Neck velocity

### Quality assurance submittals: submit following in accordance with Section 01 33 00 - Submittal Procedures.

#### Certificates: submit certificates signed by manufacturer certifying that materials comply with specified performance characteristics and physical properties.

#### Instructions: submit manufacturer's installation instructions.

## QUALITY ASSURANCE

### Health and Safety Requirements: do construction occupational health and safety in accordance with Section 01 35 29.06 - Health and Safety Requirements.

## DELIVERY, STORAGE, AND HANDLING

### Packing, shipping, handling and unloading:

#### Deliver, store and handle in accordance with Section 01 61 00 - Common Product Requirements.

#### Deliver, store and handle materials in accordance with manufacturer's written instructions.

### Waste Management and Disposal:

#### Construction/Demolition Waste Management and Disposal: separate waste materials for reuse and recycling in accordance with Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

# Products

## General

### To meet capacity, pressure drop, terminal velocity, throw, noise level, neck velocity.

### Frames:

#### Full perimeter gaskets.

#### Plaster frames where set into plaster or gypsum board.

#### Concealed fasteners.

### Concealed manual volume control damper operators as indicated.

### Colour: standard or as directed by Owner.

## Manufactured Units

### Grilles, registers and diffusers of same generic type to be product of one manufacturer.

## Supply Grilles and Registers

### See Schedule.

## Return and Exhaust Grilles and Registers

### See Schedule.

## Diffusers

### See Schedule.

## Linear Grilles

### See Schedule.

# Execution

## manufacturer’s instructions

### Compliance: comply with manufacturer's written recommendations or specifications, including product technical bulletins, handling, storage and installation instructions, and datasheet.

## Installation

### Install in accordance with manufacturers instructions.

### Install with flat head stainless steel or cadmium plated screws in countersunk holes where fastenings are visible.

### Bolt grilles, registers and diffusers, in place, in gymnasium and similar game rooms.

### Provide concealed safety chain on each grille, register and diffuser in gymnasium and similar game rooms and elsewhere.

## cleaning

### Proceed in accordance with Section 01 74 00 - Cleaning.

### Upon completion and verification of performance of installation, remove surplus materials, excess materials, rubbish, tools and equipment.

END OF SECTION