# GENERAL

## summary

### Section includes:

#### Draft barrier convectors, accessories, controls and installation

## Related work:

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal

### Section 23 09 33 – Electric and Electronic Control System for HVAC.

### Section 25 30 02 – EMCS:  Field Control Devices

## References

### Canadian Standards Association (CSA International)

#### CAN/CSA C22.2 No. 130, Requirements for Electrical Resistance Heating Cables and Heating Device Sets.

### Health Canada / Workplace Hazardous Materials Information System (WHMIS)]

#### Safety Data Sheets (SDS)

## submittals

### Product Data:

#### Submit manufacturer's printed product literature, specifications and datasheet in accordance with Section 01 33 00 - Submittal Procedures. Include product characteristics, performance criteria, and limitations.

##### Submit two copies of Workplace Hazardous Materials Information System (WHMIS) Safety Data Sheets (SDS) in accordance with Section 01 33 00 - Submittal Procedures.

#### Product data to include:

##### Suspension of heating element.

##### Physical size.

##### Thermostat control if integral.

##### Finish.

##### kW rating.

##### Cabinet thickness.

##### Cabinet surface temperature.

### Quality assurance submittals: submit following in accordance with Section 01 33 00 - Submittal Procedures.

#### Certificates: submit certificates signed by manufacturer certifying that materials comply with specified performance characteristics and physical properties.

#### Instructions: submit manufacturer's installation instructions.

### Closeout Submittals:

#### Submit operation and maintenance data in accordance with Section 01 78 00 - Closeout Submittals

## quality assurance

### Health and Safety:

#### Do construction occupational health and safety in accordance with Section 01 35 29.06 - Health and Safety Requirements.

## delivery, storage, and handling

### Packing, shipping, handling and unloading:

#### Deliver, store and handle in accordance with manufacturer's written instructions and Section 01 61 00 - Common Product Requirements.

### Waste Management and Disposal:

#### Construction/Demolition Waste Management and Disposal: separate waste materials for reuse and recycling in accordance with Section 01 74 21 - Construction/Demolition Waste Management and Disposal.

# PRODUCTS

## DRAFT BARRIER CONVECTORS

### Heaters: wattage density minimum of 900 w/m.  Element through type fitted with aluminum convector vanes and resistor wire enclosed in mineral insulation in stainless steel sheath.

### Element: locked to cabinet and supported at additional points with nylon bushings throughout length to allow for linear expansion.

### Cabinet: front inlet, top outlet, aluminum front panel 14 gauge, finished in clear anodized aluminum.  Pedestal kit (similar finish) with smooth finish on back side of heater.

### Acceptable Product:  as per heating schedule.

## CONTROLS

### Wall mounted temperature sensors: to Section 23 09 33 - Electric and Electronic Control System for HVAC or Section 25 30 02 – EMCS: Field Control Devices as indicated

### Solid state low voltage relay: to Section 23 09 33 - Electric and Electronic Control System for HVAC or Section 25 30 02 – EMCS: Field Control Devices as indicated.

# EXECUTION

## INSTALLATION

### Install draft barrier convector heaters on pedestals.

### Make power and control connections.

## FIELD QUALITY CONTROL/COMMISSIONING

### Perform tests in accordance with Section 26 05 00 – Common Work Results - Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Ensure that heaters and thermostatic controls operate correctly.

## cleaning

### Proceed in accordance with Section 01 74 00 - Cleaning.

### Upon completion and verification of performance of installation, remove surplus materials, excess materials, rubbish, tools and equipment.

END OF SECTION