# General

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 74 21 – Construction/Demolition Waste Management and Disposal.

### Section 01 78 00 - Closeout Submittals.

### Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Section 23 09 33 - Electric and Electronic Control System for HVAC.

## REFERENCES

### Canadian Standards Association (CSA International)

#### CSA C22.2 No.46, Electric Air-Heaters.

## PRODUCT DATA

### Submit product data in accordance with Section 01 33 00 - Submittal Procedures.

### Submit product data sheets for unit heaters. Include:

#### Product characteristics.

#### Performance criteria.

#### Mounting methods.

#### Physical size.

#### kW rating, voltage, phase.

#### Cabinet material thicknesses.

#### Limitations.

#### Colour and finish.

### Submit product data sheets for unit heaters.

#### Include product characteristics, performance criteria, physical size, limitations and finish.

### Manufacturer's Instructions: Provide to indicate special handling criteria, installation sequence and cleaning procedures.

## CLOSEOUT SUBMITTALS

### Provide operation and maintenance data for unit heaters for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

## WASTE MANAGEMENT AND DISPOSAL

### Separate and recycle waste materials in accordance with Section 01 74 21 – Construction/Demolition Waste Management and Disposal, and with Waste Reduction Workplan.

### Remove from site and dispose of packaging materials at appropriate recycling facilities.

### Collect and separate for disposal paper, plastic, polystyrene, corrugated cardboard, packaging material in appropriate on-site bins for recycling in accordance with Waste Management Plan.

### Divert unused metal and wiring materials from landfill to metal recycling facility approved by Owner.

### Collect, package and store existing unit heaters for either reuse, recycling or rebuilding and return to recycler in accordance with Waste Management Plan.

# Products

## UNIT HEATERS

### Unit heater: to CSA C22.2 No.46, horizontal discharge complete with adjustable louvers finished to match cabinet or vertical discharge cone type with cone diffusers as indicated.

### Fan type unit heaters with built-in high-heat limit protection, fan-delay switches.

### Fan motor: totally enclosed, permanently lubricated ball bearing type with resilient mount.

#### Built-in fan motor thermal overload protection.

### Hangers: as indicated.

### Elements: mineral insulated steel sheath with aluminum, continuous helical brazed fins.

### Cabinet: steel, 1.6 mm thick, fitted with brackets for rod or wall mounting.

#### Phosphatized and finished with 2 coats baked enamel in beige colour.

## CONTROLS

### Wall mounted thermostats: type line, low voltage or electronic, and solid state relays, Energy Star certified, to Section 23 09 33 - Electric and Electronic Control System for HVAC or Section 25 30 02 - EMCS: Field Control Devices.

# Execution

## INSTALLATION

### Suspend unit heaters from ceiling or mount on wall as indicated. Provide mounting bracket as required.

### Install thermostats in locations indicated.

### Make power and control connections.

## COMMISSIONING

### Perform tests in accordance with Section 26 05 00 – Common Work Results-Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Test cut-out protection when air movement is obstructed.

### Test fan delay switch to assure dissipation of heat after element shut down.

### Test unit cut-off when fan motor overload protection has operated.

### Ensure heaters and thermostatic controls operate correctly.

END OF SECTION