# General

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

### Section 01 78 00 - Closeout Submittals.

### Section 01 91 13.13 - Commissioning (Cx) Requirements.

### Section 26 05 00 - Common Work Results - Electrical.

### Section 26 05 34 - Conduits, Conduit Fastenings and Conduit Fittings.

### Section 27 05 14 - Communication Cables - Inside Buildings.

### Section 27 53 20 - Master TV Antenna.

## REFERENCES

### Industry Canada - Terminal Attachment Program

#### CS-03, Compliance Specification.

## SYSTEM DESCRIPTION

### Public address loudspeaker system to incorporate:

#### Voice paging.

#### Recorded music from tape and CD player.

#### Broadcast programs from AM/FM tuner.

#### Additional features as specified.

### Operations:

#### Paging:

##### Voice paging from microphone overrides broadcast or recorded music reproductions.

##### Selective area page to areas as indicated.

##### Emergency page to all areas.

#### Music:

##### Music from CD player, am/fm tuner or external source.

##### Speaker selection made via toggle switch and relay assembly.

### Systems in various configurations may be rack mounted or stand alone.

## SUBMITTALS

### Include, riser diagram, block diagram of complete public address system.

### Public address system design criteria.

## CLOSEOUT SUBMITTALS

### Provide operation and maintenance data for public address system for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

### Include:

#### Operation instructions.

#### Description of system operation.

#### Description of each subsystem operation.

#### List specifying each piece of equipment in system or subsystem by its original manufacturer name and model number.

#### Part list specifying parts used in equipment by identification numbers that are standard to electronic industry.

## TRAIning

### Arrange and pay for on-site lectures and demonstrations by system manufacturer to train operating personnel in the use and maintenance of the system.

# Products

## MATERIALS

### Conduits: to Section 26 05 34 - Conduits, Conduit Fastenings and Conduit Fittings.

### Communication conductors: as indicated, to Section 27 05 14 - Communication Cables - Inside Buildings.

### Antenna: to Section 27 53 20 - Master TV Antenna.

## COMPONENTS

### Continuous duty cycle.

### Modular system design.

### Solid state, and suitable for rack mounting.

### Maximum operating temperature: 65 degrees C.

### Finish: standard.

### Grounding conductor for system components.

## EQUIPMENT RACK

### Rack, to accommodate system components, enclosed type, steel construction with internal mounting rails, wire and cable entrances with smooth edges protected by rubber edging, four adjustable rack levelling feet.

### Metal outlet raceway with colour coded outlets wired to 120V, 60Hz supply controlled by key type locking switch.

### Louvres and ventilation apertures in sides, top, back of rack for convection ventilation.

### Racks to contain but not necessarily limited to following components.

#### Monitor panel.

#### AM/FM tuner.

#### Cassette tape recorder.

#### CD player.

#### Relay assembly.

#### Page/music selection panel.

#### Timer: program time system with battery backup.

#### Telephone paging interface equipment.

#### Patch bay.

#### Pre-amplifier mixer.

#### Power amplifiers.

#### Power supplies.

#### Installation and service connections to various panels by plug-in type terminal blocks with barriers and screw type terminals.

## MONITOR PANEL

### Monitor panel to contain VU metre, selector, 150 mm monitor speaker and volume control to provide audible and visual monitoring of sound programmes.

#### VU metre to have black scale for normal conditions, and red scale for overload conditions.

## MICROPHONE

### Microphone: close talking omni-directional, noise cancellation, dynamic type, complete with cradle, built-in preamplifier:

#### Frequency response: 100-6000 Hz.

#### Output level: approximately -55 dB.

#### Output impedance, balanced to ground, 150 ohms.

#### Housing, metal, desk mounting, finish standard.

#### Push-to-talk switch.

#### Magnetic dust shield.

## PRE-AMPLIFIER MIXER

### Modular design.

### Inputs:

#### 6 -continuously variable microphone volume controls.

#### 1-continuously variable master gain control.

#### 1-bass tone control with centre position flat and 10 dB boost to 10 dB cut either side.

#### 1-treble tone control switch with centre position flat and 10 dB boost to 10 dB cut either side.

### Mixer also to operate on 12 to 24 V DC.

### Output volts: 1 V rms at less than 1 % distortion.

### Frequency response: 30-20,000 Hz plus or minus 1 dB at full output.

### Hum and noise level: -65 dB minimum at full output.

## PATCH BAY

### Provide 2 jacks corresponding to input and output of every signal processing equipment that is installed in rack.

### Each jack wired for 'normalled' configuration.

## TELEPHONE PAGING EQUIPMENT WITH POWER SUPPLY UNITS

### Lets person select and page any area or all areas from their telephone.

#### Decodes typical dual tone multifrequencies (DTMF) for selection of area or areas for paging.

### Has facility to provide background music to areas not being paged.

### Has facility to let emergency announcement override page in zones being paged and background music in zones not being paged.

### Automatically starts page when it detects typical telephone ring signal.

### Automatically ends page when it detects absence of voice signal for specific length of time.

### Compatible power supply unit.

### Certified by Industry Canada to CS-03 for direct connection to telephone network.

## POWER BOOSTER AMPLIFIER

### Overload and output short circuit protection.

### Power output: as indicated/required at 1 % harmonic distortion over frequency range 25 to 18,000 Hz plus or minus 1 dB.

### Signal and noise level: 80 dB below rated output.

### Maximum gain: 75 dB.

### Outputs: 8 ohm, 70 V balanced or unbalanced line.

### Peak power: as indicated/required.

### Controls and indicators:

#### Volume control screwdriver adjustable.

#### AC power switch.

#### Fused primary.

#### 'on' indicator light.

### Output for emergency battery operation.

## POWER SUPPLY

### Power supply unit, well filtered, regulated, constant voltage under load.

#### Output: 24 V DC at 3 A as required.

#### Input: 120 V, 60 Hz, nominal.

#### Power consumption: as indicated in watts.

#### Fuse: 3 A, replaceable.

#### Rectifier, silicon full wave bridge.

#### Filter, choke and dual condensers.

#### Hook-up (+) (-) terminal strip with terminal screws.

#### Line cord: 2 m, 3 conductor with specially constructed strain relief.

## RECORD CHANGER

### CD capacity: 5 disc.

## AM/FM TUNER

### Controls and indicators, on front panel:

#### AM/FM tuning control.

#### Power on/off switch.

#### Interchannel hush in/out switch.

#### AM/FM selector switch.

#### Peak metre.

#### FM zero centre switch.

#### Bass, treble, volume controls.

#### Tuning metre for AM/FM.

### Receptacles on rear of panel:

#### Audio output jack.

#### AM/FM antenna connections.

### FM channel.

#### Tuning range: 87.5 to 108.5 MHz.

#### Hum and noise level: 70 dB below 100% mod.

#### Frequency response: 20 to 20,000 Hz plus or minus 0.5dB.

#### Antenna: 300 ohms balanced or 72 ohms unbalanced, as required.

#### Mono sensitivity: 15 dBf, for 20 dB quieting, 17 dB for 50 dB s/n.

#### SCA adapter.

### AM channel:

#### Tuning range: 530 to 1650 kHz.

#### Hum and noise level: 56 dB below 100% mod.

#### Frequency response: -6 dB at 4.0 kHz.

#### Usable sensitivity: 500 microvolts per metre.

#### Distortion: less than 0.3 % im at 100% mod.

## ADDITIONAL FEATURES

### Leased wire background music source.

### Tone signal generator for time and alarm signals.

### Interface with telephone PBX or Centrex as indicated/required.

### Bridging control to provide facilities between local sound source and sound control rack.

#### Three pole, three position, non-shorting type switch with positions marked '1', 'off', '2', to allow programmes to originate, remain in or terminate.

#### Volume control to provide local volume regulations of programme received from console.

#### Programme control relay.

### Notch filters for acoustic treatment.

## SOUND REPRODUCERS

### Cone type wattage as indicated.

### Ceiling or wall mounting as indicated

### Finish colour: standard.

### Outdoor, weather proof and indoor enclosures as indicated.

### Mass: standard kg.

### Acoustic treatment: standard.

### Faceplate and back box.

### Connections type plug in.

### Line transformer: 70 V primary with tapped secondary for volume adjustment.

### Frequency range: 25 – 18,000 Hz.

### Dispersion: 45 degrees.

### Impedance: 8 ohms.

### Power input to voice coil: as required.

### Power input to driver:  as required.

### Axial sensitivity: 93 at 1 with 1W input.

### If these assemblies are used as microphones, then their sensitivity to be equal to or greater than minus 60 dBs for 74 dBs SPL at 1 kHz.

# Execution

## INSTALLATION

### Install equipment in accordance with manufacturer's instructions, and as indicated.

## FIELD QUALITY CONTROL

### Perform tests in accordance with Section 26 05 00 – Common Work Results - Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Conduct intelligibility test.

END OF SECTION