# General

## REFERENCES

### Industry Canada - Terminal Attachment Program

#### CS-03, Compliance Specification.

## SYSTEM DESCRIPTION

### Personal listening system utilizing an audio source transmitted wirelessly over a FM frequency to portable FM receivers.

## SUBMITTALS

### Do not proceed with the supply of assistive listening systems until relevant product data submissions are reviewed by Owner.

### Allow ten (10) working days for Owner review of each submission.

### Contractor’s responsibility for errors and omissions in submission is not relieved by Owner’s review of submittals.

### Contractor's responsibility for deviations in submission from requirements of Contract Documents is not relieved by Owner review of submission, unless Owner gives written acceptance of specific deviations.

### Make any changes in submissions which Owner may require consistent with Contract Documents and resubmit as directed by Owner. When resubmitting, notify Owner in writing of revisions other than those requested.

## CLOSEOUT SUBMITTALS

### Provide operation and maintenance data for assistive listening system.

### Include:

#### Operation instructions.

#### Description of system operation.

#### Description of each subsystem operation.

#### List specifying each piece of equipment in system or subsystem by its original manufacturer name and model number.

#### Part list specifying parts used in equipment by identification numbers that are standard to electronic industry.

## TRAIning

### Arrange and pay for on-site lectures and demonstrations by system manufacturer to train operating personnel in the use and maintenance of the system.

# Products

## Assistive Listening System

### Transmitter:

#### High performance, stationary transmitter to the following specifications:

##### Signal-to-Noise Ratio: minimum 74 dB.

##### Frequency Response: 22 – 16000 Hz, +1, -3 dB.

##### Audio Level Controls: Push button, adjustable to 0 to -50 dB.

##### Operating Frequencies: 72 – 76 MHz.

##### Frequency Accuracy: ± 0.005% stability, 0-50° C.

##### 10 selectable wideband channels.

##### Power:

###### Input: 120 VAC, 60 Hz, 17 W.

###### Output: 24 VAC, 500 mA.

##### Audio Input: combination 3-pin XLR, ¼” TRS jack.

##### Line Output: RCA jack

### Personal Receiver:

#### Impact-resistant, single channel receiver with rechargeable nickel-metal hydride (NiMH) batteries, to the following specifications:

##### Operating Frequencies: 72 – 76 MHz, pre-tuned, adjustable.

##### Intermediate Frequency: 75 kHz.

##### FM Deviation: 75 kHz.

##### Frequency Response: 200 – 15 kHz.

##### Signal-to-Noise ratio: 65 dB at 100 µV.

##### Input Overload: 100 mV.

##### Sensitivity: 2 µV at 12 dB.

##### Audio Output: 35 mW, max. at 16 Ω.

### Accessories:

#### 12 unit receiver charger, 3 V. (One per transmitter)

#### Receiver carry case, quantity as indicated in equipment schedule.

#### System carry case, quantity as indicated in equipment schedule.

#### Heavy-duty carry case, quantity as indicated in equipment schedule.

#### Mono folding headphones. (One per receiver)

#### 3.5 mm plug, mono, 450 mm long neck loop, quantity as indicated in equipment schedule.

#### Patch cable. (One per transmitter)

#### Supply two (2) spare batteries for each receiver.

### Equipment supplied as per the following schedule:

# Execution (Not Applicable)

END OF SECTION