# General

## REFERENCES

### Industry Canada - Terminal Attachment Program

#### CS-03, Compliance Specification.

## SYSTEM DESCRIPTION

### Enhanced classroom listening system utilizing infrared wireless components to transmit teachers and students normal speaking voice to everyone in the classroom through a wide dispersion speaker.

## SUBMITTALS

### Do not proceed with the supply of enhanced classroom listening systems until relevant product data submissions are reviewed by Owner.

### Allow ten (10) working days for Owner review of each submission.

### Contractor’s responsibility for errors and omissions in submission is not relieved by Owner’s review of submittals.

### Contractor's responsibility for deviations in submission from requirements of Contract Documents is not relieved by Owner review of submission, unless Owner gives written acceptance of specific deviations.

### Make any changes in submissions which Owner may require consistent with Contract Documents and resubmit as directed by Owner. When resubmitting, notify Owner in writing of revisions other than those requested.

## CLOSEOUT SUBMITTALS

### Provide operation and maintenance data for enhanced classroom listening system.

### Include:

#### Operation instructions.

#### Description of system operation.

#### Description of each subsystem operation.

#### List specifying each piece of equipment in system or subsystem by its original manufacturer name and model number.

#### Part list specifying parts used in equipment by identification numbers that are standard to electronic industry.

## TRAIning

### Arrange and pay for on-site lectures and demonstrations by system manufacturer to train operating personnel in the use and maintenance of the system.

# Products

## enhanced classroom Listening System

### Infrared wireless speaker:

#### Speaker to have a built-in infrared receiver and 20W digital amplifier.Signal-to-Noise Ratio: minimum 74 dB.

#### Wide-dispersion acoustic structure to achieve uniform output over a 4.5 m radius.

#### Speaker to provide wide frequency range (100 Hz – 20 kHz).

#### Carrier frequency for teacher (3.1 MHz) and student (3.35 MHz).

### Infrared Wireless Tuner:

#### Frequency response optimized to reduce acoustic feedback in a 9.0 x 9.0 m classroom.

#### Mixing output terminal for assistive listening device.

#### Equalizer control for low, mid, high frequency outputs.

#### Receiver frequency for teacher (3.1 MHz) and student (3.35 MHz).

#### Inputs from 3 auxiliary devices; PC, DVD/TV, MP3.

#### Output muting by 25V line signal from school intercom system.

### Infrared Wireless Microphone:

#### Infrared wireless microphone for teacher with a carrier frequency of 3.1 MHz and one for a student with a carrier frequency of 3.35 MHz.

#### Adjustable infrared light emission intensity.

#### Transmission distance of 15 m minimum (unobstructed space).

### Accessories:

#### Battery charger for each system supplied.

#### Rechargable batteries as required for the system.

#### Battery charger to simultaneously charge the teacher and student microphones within 4 hours.

# Execution (Not Applicable)

END OF SECTION