# GENERAL

## RELATED SECTIONS

### Section 01 33 00 – Submittal Procedures.

### Section 01 78 00 – Closeout Submittals.

### Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Section 26 05 00 – Common Work Results - Electrical.

## SYSTEM DESCRIPTION

### System is to be a microprocessor based communication system providing integrated clock, program, and intercom functions.

### System to be complete with all modules and accessories to provide a functioning system.

### System c/w the following components:

#### Central control equipment located in the electrical room consisting of:

##### Modular microprocessor based controller.

##### Intercom amplifier.

##### Clock controller and power supply.

##### Tone generator.

##### Self diagnostic program.

##### Telephone modem.

##### Wall mount equipment rack.

#### Administration control centres.  Two such.

#### Digital readout in general office.

#### Am/Fm stereo tuner in general office.

#### Cassette deck in general office.

#### Five disc CD player in general office.

#### Exterior whip antenna.

#### Speakers

#### Clocks

## OPERATION AND MAINTENANCE DATA

### Provide date for incorporation into maintenance manual specified in Section 01 78 00- Closeout Submittals.

### Include description of system operation and parrs list.

## TRAINING

### Arrange and pay for on-site lectures and demonstrations by system manufacturer to train operational personnel in use and maintenance of system.

## WARRANTY

### Provide manufacturer product warranty against defects in operation, material and workmanship for a period of not less tan 2 years from date of substantial completion.

# PRODUCTS

## RELATED EQUIPMENT

### Conduit: type EMT to Section 26 05 34 – Conduits, Conduit Fastenings and Conduit Fittings.

## ADMINISTRATION CONTROL CENTRE

### Desk mounted unit with large 16 character LCD, spill proof keypad, handset, microphone, speaker, push-to-talk button.

## CLASSROOM STATIONS

### Wall mounted, recessed, c/w backbox and call switch.

### Square, steel baffle with white baked enamel finish.

## PAGING SPEAKER

### Ceiling mounted, recessed, except c/w surface backbox for speakers in gymnasium.

### Square, steel baffle with white baked enamel finish.

## REMOTE CLOCKS

### Designed to operate as secondary (corrected) clocks.

### Digital display clocks:

#### Single face unit, recess mounted in all but corridor locations.

#### Double face unit, surface mounted on wall in corridor locations.  Consists of two surface clocks on mounting bracket.

### Analog display clocks:

#### Single face unit, semi-flush mounted, synchronous, 300 mm diameter, 24 hour marking, black trim.

## SIGNALLING DEVICES

### Schedule signals within the school will be transmitted over general paging speakers.

### Exterior signals will be transmitted using 250 mm bells, 120 V c/w weatherproof back box and PVC yard hood.

## PERSONAL ALERT EQUIPMENT

### Personal Alert Transmitter.  Remote electronic device worn by teacher.

### Personal Alert Receiver.  To be located in challenging needs classroom for detection of emergency signal.

### Supply two (2) additional type N batteries for transmitter.

## WASHROOM ALERT EQUIPMENT

### Non-latching emergency call pull station with pull cord c/w interface equipment to connect to intercom system.

### Activation of emergency call pull station to send alarm to administration.

## CONDUCTORS

### Installed in conduit systems where provided.

### Where not in conduit, group conductors together in approved manner.

### Size and type as per riser on drawings for system identified.  Conductors for alternate systems (number, type and size) are to be provided at no extra cost.

### Provide support for loose conductors in accordance with Section 27 10 50 – Data System, par. 2.5.2 – Cable Management.

## UNINTERRUPTIBLE POWER SUPPLY

### Self contained, single phase unit, 120 volt input, 1500 VA rating.

### Shelf for mounting UPS unit directly below equipment rack, off floor.

## AUDIO EQUIPMENT COMPONENTS

### Cassette deck - shelf mounted dual auto reverse cassette deck with record feature.

### CD player, shelf mount player with five disk carousel.

### Tuner - shelf mount with digital tuning, AM/FM.

# EXECUTION

## INSTALLATION

### Locate intercom/clock/program control unit in electrical room and connect to 120 V ac, 60 Hz power supply through power conditioner.

### Locate classroom stations and connect to control unit.

### Locate paging speakers and connect to control unit.

### Locate administrative control centres in administration area and principal(s office and connect to control unit.

### Locate exterior signaling devices as indicated and connect to control unit.

### Locate direct read and analog clocks as indicated and connect to control unit.

### Locate whip antennae and connect to control unit.

### Locate personal alert receiver 300 mm below ceiling in challenging needs classroom.  Connect to talk back unit in classroom.

### Locate CD player, cassette deck and stereo turner in general office and connect to control unit.

## TESTS

### Perform tests in accordance with Section 26 05 00 – Common Work Results - Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Conduct intelligibility test.

END OF SECTION