# General

## RELATED SECTIONS

### Section 01 33 00 - Submittal Procedures.

## REFERENCES

### Canadian Standards Association (CSA)

#### CAN/CSA-B72, Installation Code for Lightning Protection Systems.

#### CAN/CSA-S37, Antennas, Towers, and Antenna-Supporting Structures.

## SUBMITTALS

### Indicate:

#### Dimensioned template of antenna base.

#### Dimensioned template of guy anchor bases.

#### Dimensions of structural members.

#### Type and location of guy fastenings on tower.

#### Location of guy anchor bases and antenna base.

#### Method of fastening antenna array to antenna tower.

#### Location of obstruction lights.

#### Painting pattern to meet Transport Canada (TC) regulations for aircraft obstructions.

#### Lightning protection.

# Products

## ANTENNA TOWER

### Tower: to CAN/CSA-S37, height as indicated steel guyed and self-supporting designed for:

#### Wind load: as required for site location.

#### Antenna array load: as required.

#### Ice load:  as required.

#### Dead load of system: as required

#### Vertical and horizontal components of guy stresses.

### Tower lightning protection: to CAN/CSA-B72.

## ANTENNA GUYS

### Guys: galvanized steel wire strand 5 mm diameter.

## ANTENNA ARRAY

### Minimum signal levels of:

#### VHF -TV- Channels 2 - 13, + 6 dBmV.

#### UHF -TV- Channels 14 - 83, O dBmV.

#### FM - 88 to 108 MHz, - 6 dBmV.

## ANTENNA AMPLIFIER

### VHF type, solid state, frequency range 54-216 MHz, minimum gain 33.0 dB.

## OBSTRUCTION LIGHTS

### Obstruction lights to TC standards.

## WIRING

### Underground services located as indicated.

## FABRICATION

### Shop fabricate tower and array.

### Prepare for shipment to site in suitable length sections.

## PAINTING

### Paint tower structure international orange and white to meet TC regulations for aircraft obstructions.

# Execution

## INSTALLATION

### Mount antenna tower on antenna base in accordance with manufacturer's instructions.

### Install guys.

### Install antenna array on top of tower.

### Connect antenna array to antenna amplifier using coaxial cable.

### Connect antenna amplifier to coaxial cable system.

### Connect obstruction lights to power supply.

### Optimize reception by making adjustments in height and direction for each antenna.

### Install lightning protection in accordance with CAN/CSA-B72.

## FIELD QUALITY CONTROL

### Megger test lightning protection system resistance to ground. Resistance value of system network: 10 ohms or less.

END OF SECTION