# GENERAL

## DESCRIPTION OF SYSTEM

### Complete system of conduit raceways, outlet boxes, outlet assemblies, coverplates distribution amplifier, splitters/attenuators and coaxial cable as described herein.

## WORK INCLUDED IN THIS CONTRACT

### Provision of all raceway systems indicated.

### Provision of all cable and terminations as indicated.

### Provision of sectional boxes for television outlets

### Provision of distribution amplifier, A/V modulator, splitter/attenuators as described.

## Related sections

### Section 01 33 00 – Submittal Procedures.

### Section 01 78 00 – Closeout Submittals.

### Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Section 26 05 00 – Common Work Results – Electrical.

### Section 26 05 34 – Conduits, Conduit Fastenings and Conduit Fittings.

## TRAINING

### Arrange and pay for on-site lectures and demonstrating by system manufacturer to train designated personnel in the use and maintenance of the system.

## Warranty

### Ensure equipment installed is warranted by the manufacturer to be free of defects in operation, material and workmanship for a period of one (1) year from date of Substantial Completion.

# PRODUCTS

## OUTLETS

### Outlets complete with one (1) G/F connector mounted in stainless steel wall plate.

## DISTRIBUTION SPLITTERS/ATTENUATORS

### Professional quality splitter blocks with multiple taps, number to suit application.  Attenuation rating to suit application.

## AMPLIFIER

### Broadband RF amplifier for CATV signal boost. Wall mount at CATV equipment board in electrical room.

## AUDIO/VIDEO MODULATOR

### Rack mounted A/V modulator for broadcast of school activities onto unused CATV channel.  Locate at CATV equipment board in electrical room.

## CHANNEL FILTER

### Rack mounted channel elimination filter to enable broadcast of school services over CATV system.

## EQUIPMENT RACK

### Wall mounted equipment rack to house A/V modulator and amplifier, sized to accommodate equipment installed.

## COAXIAL CABLE

### Coaxial cable: 75 ohm, RG-6/U type, riser rated for -30° C to + 80° C.

## AV INPUT

### Provide one combination input for audio and video on one plate located in the library and connected to the input of the system AV modulator.  Exact location to be determined on site.

### Conductors: one RG59 coaxial cable, two 2-conductor shielded cable. Conductors to be run in conduit throughout.

### Provide jacks on plate for connection of coaxial and stereo audio cables.

## CABLE SUPPORT

### Provide support for coaxial cables in accordance with Section 27 10 50 – Data Systems, par. 2.5 – Cable Management.

# EXECUTION

## INSTALLATION

### Install conduit raceways, as indicated.

### Install 19 mm x 24 mm x 2400 mm plywood backboard.

### Install one run of cable from each outlet to splitters as indicated.  Install trunk cable in corridor.

### Run distribution cables from splitter locations to TV plywood backboard.

### Install amplifier, A/V modulator and splitter/attenuators.

## field QUALITY ontrol

### Perform tests in accordance with Section 26 05 00 – Common Work Results - Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

END OF SECTION