# GENERAL

## DESCRIPTION OF WORK

### This section covers the provision of power for door locks and conduit for 24 VDC hardware wiring.

### Door lock equipment and card access equipment provided by the door hardware supplier.

### Low voltage (24VDC) wiring supplied & installed by the door hardware supplier.

## Related Sections

### Section 08 71 00 – Door Hardware.

### Section 26 05 34 – Conduits, Conduit Fastenings and Conduit Fittings.

## EQUIPMENT SUPPLIED BY DIVISION 26

### Provide all 120 VAC wiring in conduit system for power supply as indicated.

### Provide an empty conduit system with pull cords for installation of 24VDC wiring by door hardware supplier, as indicated.

## COORDINATION

### Co-ordinate with door hardware supplier to ensure that equipment, boxes, wiring and conduit are located correctly.

## CONNECTION TO FIRE ALARM PANEL

### Where scheduled, door power supplies shall be wired to normally closed contacts in the fire alarm panel to release door locks on activation of fire alarm.

## CERTIFICATE OF COMPLIANCE

### Provide a letter of verification stating that the system has been checked out and is operational in advance of the Substantial Completion inspection.

# PRODUCTS (NOT APPLICABLE)

# EXECUTION

## EXECUTION

### Install 120 VAC power to door power supplies.

### Install empty conduit system c/w pull cords for 24 VDC wiring.

END OF SECTION