# General

## Related Sections

### Section 01 33 00 - Submittal Procedures.

### Section 01 78 00 - Closeout Submittals.

### Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Section 26 05 00 – Common Work Results - Electrical.

### Section 26 05 21 – Wires and Cables (0-1000 V).

## System Description

### Building entrance control system.

#### Caller pushes button on building entrance panel to sound tone signal in suite.

#### Suite tenant may operate talk-listen switch to converse with caller.

#### Tenant may operate switch to release building entrance door magnetic lock to admit caller.

## Closeout Submittals

### Provide operation and maintenance data for building entrance control system for incorporation into manual specified in Section 01 78 00 - Closeout Submittals.

### Include description of system operation.

### Include parts list, using component identification numbers standard to electronics industry.

## Extra Materials

### Provide maintenance materials in accordance with Section 01 78 00 - Closeout Submittals.

# Products

## Building Entrance Panel

### Control and communication panel at building entrance location as indicated.

#### Enclosed, surface mounting.

#### Pushbuttons, engraved nameplates behind vandal proof transparent cover quantity as indicated.

#### Buzzer.

#### Automatic switching to rear entrance panel.

#### Adjustable volume control.

#### Solid state controls.

#### Power supply: input 120 V, output 24 V.

#### Amplifier.

#### Telephone-type handset.

#### Panel finish: standard

### Tenant directory to be paper.

## Door Opener

### Door unlock indication: buzzer.

### Magnetic door opener front and rear for controlled building entrance doors, reversible for left or right hand doors. Materials: compatible with door load.

## Suite Stations

### Suite stations, as indicated:

#### Enclosed, surface mounting.

#### High impact plastic.

#### Talk-listen switch.

#### Tone buzzer.

#### Speaker/microphone: 90 mm dia min. Sound level: 10 dB.  Adjustable volume control range: 0 – 10 dB.

#### Wall-mounted telephone.

### Tenants personal telephone units.

## Additional Features

### Door open indicating buzzer.

### Emergency paging.

### Security alarm.

### Panel alarm.

### Signalling to office.

### Keyless entry codes.

### Programmable door unlock timer on main entry panel.

### Distinctive ring in suites.

### System/readers.

## Communication Conductors

### Type LVT, in accordance with Section 26 05 21 – Wires and Cables (0-1000 V).

# Execution

## Installation

### Install system in accordance with manufacturer's instructions.

### Connect system to emergency power.

## Field Quality Control

### Perform tests in accordance with Section 26 05 00 – Common Work Results - Electrical and Section 01 91 13.13 – Commissioning (Cx) Requirements.

### Perform intelligibility tests.

END OF SECTION