# GENERAL

## RELATED SECTIONS

### Section 31 11 00 - Clearing and Grubbing.

### Section 31 23 16.26 - Rock Removal.

### Section 31 23 33.01 - Excavation, Trenching and Backfilling.

## REFERENCES

### American Society for Testing and Materials (ASTM)

#### ASTM D698, Test Method for Laboratory Compaction Characteristics of Soil Using Standard Effort (600kN-m/m³),

## EXISTING CONDITIONS

### Examine subsurface investigation report which is available for inspection from Owner.

### Known underground and surface utility lines and buried objects are as indicated on site plan.

### Refer to dewatering in Section 31 23 33.01 - Excavating Trenching and Backfilling.

## PROTECTION

### Protect and/or transplant existing fencing trees, landscaping, natural features, bench marks, buildings, pavement, surface or underground utility lines which are to remain as directed by Owner. If damaged, restore to original or better condition unless directed otherwise.

### Maintain access roads to prevent accumulation of construction related debris on roads.

# PRODUCTS

## MATERIALS

### Fill material: Type 3 in accordance with of Section 31 23 33.01 - Excavating, Trenching and Backfilling.

### Excavated or graded material existing on site may be suitable to use as fill for grading work if approved by Owner.

# EXECUTION

## STRIPPING OF TOPSOIL

### Do not handle topsoil while in wet or frozen condition or in any manner in which soil structure is adversely affected as determined by Owner.

### Commence topsoil stripping of areas as indicated after area has been cleared of brush, weeds and grasses and removed from site.

### Strip topsoil to depths as indicated. Avoid mixing topsoil with subsoil.

### Stockpile in locations as directed by Owner. Stockpile height not to exceed 2.0 m.

### Dispose of unused topsoil as directed by Owner.

## GRADING

### Rough grade to levels, profiles, and contours allowing for surface treatment as indicated.

### Rough grade to following depths below finish grades:

#### 250 mm for concrete slabs and walks precast paving units.

### Slope rough grade away from building 1:50 minimum.

### Grade ditches to depth as indicated.

### Prior to placing fill over existing ground, scarify surface to depth of 150 mm. Maintain fill and existing surface at approximately same moisture content to facilitate bonding.

### Compact filled and disturbed areas to corrected maximum dry density to ASTM D698, as follows:

#### 85% under landscaped areas.

#### 95% under paved and walk areas.

### Do not disturb soil within branch spread of trees or shrubs to remain.

## TESTING

### Inspection and testing of soil compaction will be carried out by testing laboratory designated by Owner. Refer to Sections 01 29 83 - Payment Procedures for Testing Laboratory Services and 01 45 00 – Quality Control.

### Submit testing procedure, frequency of tests, to Owner’ or approval.

## SURPLUS MATERIAL

### Remove surplus material and material unsuitable for fill, grading or landscaping as directed by Owner.

END OF SECTION